## Slide 1: LMR/FTM Replay Counter
Date: 2020-05-27
Authors:

## Slide 2: Abstract
This submission outlines an issue with losing protected Management frames that are pending or retried around a ranging frame sequence
A few options to address the issue are presented

## Slide 3: Protected LMR Transmission Issues
LMR transmissions are hard to coordinate at transmitter as in both TB and Non-TB, there’s a constraint as to when the LMR frame(s) ought to be transmitted
In Non-TB case, ISTA initiates the sequence and RSTA needs to deliver LMR before sequence ends regardless of the status of prior protected management frame transmission
  Pending Protected management frame would need to be retransmitted so if LMR uses the next PN number it essentially results in loosing that frame
    LMR frame uses Protected Management Frame Reply counter to accept a new frame
  In case when I2R LMR is also negotiated, ISTA can have the same issue
  A protected LMR may be queued ahead of time of measurement and other protected management frames may need to be transmitted.
Similarly, in TB case RSTA needs to begin the sequence upon arrival of Availability Window and transmit LMR frame before sequence ends regardless of the status of prior protected management frame transmission
  Similarly ISTA if I2R LMR is negotiated to be sent
TB Passive ranging does NOT need LMR Replay counter for Primus & Secundus frames since they’re sent in clear

## Slide 4: Protected LMR Transmission Issues
Depending on the implementation, buffering can also become another potential issue with LMR/FTM
Case-1
  Delayed LMR/FTM stored in protected management ‘logical queue’ while it also contains two additional frames ahead
  Ranging measurement sequence begins (NTB/TB/DMG)
  LMR/FTM must be transmitted within the ‘ranging sequence’
    LMR/FTM taken out of the queue for transmission
  Outcome results in two protected management frames be dropped since the receiver updates its replay counter with LMR/FTM’s PN number
Case-2
  Delayed LMR/FTM stored in head of the queue with one or more additional protected management frames behind
  Expected ranging sequence does not occur
    TB poll not rcvd, NTB NDPA not rcvd, DMG FTM Trig not rcvd
  Outcome results in ‘head of line (HOL) blocking’ unless LMR/FTM frame deleted & regenerated later trying to guesstimate when its ranging sequence starts
PM1
PM2
LMR/FTM
Case1
PM1
PM2
LMR/FTM
Case2

## Slide 5: Options to Consider
Lose pending protected management frames
  Should avoid this solution as we don’t want to imply 11az is impacting baseline standard
Remove the constraint of transmitting LMR/FTM from the ranging sequence
  Undesired outcome as it impacts device power save & use case performance
Add new Replay counter(s) specifically for LMR/FTM transmissions (Preferred)
  Decouple other protected management frame transmissions from LMR/FTM
    Each kind would have its own replay counter and can be re-ordered independently
    Pending management frame can be retransmitted after sequence ends
  Baseline standard has 16 replay counters (data) decoupling frame transmissions based on ACs/TIDs, additional counters for protected management frame (unicast/QMF, Multicast, Beacons) so LMR replay counter(s) would be additional
  Need unicast LMR/FTM replay counters
Have a different Key & PN number space exclusive for LMR
  Lot of security spec work that is likely to be scrutinized and delay 11az spec adoption
  Implementation Overhead

## Slide 6: Design constraints with LMR/FTM Replay Counter
Need replay checking based on Type + Subtype (i.e., Action/Action+noAck) + Action Category (Protected Dual) + Action field (i.e., LMR/FTM)
  Type/Subtype fields are in clear
  Category field encrypted hence only identified after decryption
  Some implementation perform decryption plus ‘replay protection’ inline in HW hence adding a new replay counter for frames matching the 4-tuple might be an issue
A possible solution is to use Reserved/Extensive Subtypes for protected LMR/FTM frames
For ease of RX parsing use a new Action Category (Table 9-53—Category values)
Code | Meaning | Subclause | Robust | Group addressed privacy
<ANA-PRM> | Protected Ranging Frame (LMR/FTM) | TBD | Yes | No