## Slide 1: Dynamic Link Sets for MLDs
Date: 2020-05-15
Authors:
Name | Affiliations | Address | Phone | Email
Pooya Monajemi | Cisco |  |  | pmonajem@cisco.com
Brian Hart |  |  |  | brianh@cisco.com
Malcolm Smith |  |  |  | mmsmith@cisco.com
Khashayar Mirfakhraei |  |  |  | kmirfakh@cisco.com
Notes: September 2012

## Slide 2: Motivation
11be Introduces the concept of Multi-Link Devices
Enablement/disablement
  A link is defined enabled if there is at least one TIDs mapped to that link
  By default all TIDs are mapped to all links
Static Set of Links
  AP is expected to advertise about all links using MLA IEs in Beacons/Probe Responses/etc
  At association/setup, the AP MLD can grant a set of links to a non-AP STA MLD by sending a list of MLA IEs in the Association Response frame
  Once the setup is complete, no further modifications are currently envisioned to the set of links
Shortcomings
  In this contribution we discuss a few cases where a static set of links will face limitations
  Capability to dynamically add or remove links from an MLD setup is needed

## Slide 3: Case 1 : Dynamic Radio Role Changes
AP Radio Role Switching
  Many multi-radio APs can dynamically switch a radio’s mode of operation
    Radios may be turned on/off in order to manage interference levels/coverage
      Commonly used in 2.4GHz
    Operating band of a radio may be switched
    Radio may be turned into a “monitor-only” role for measurement purposes
      Or turned back into client-serving mode once done
Unrealistic to require a new MLD setup. We need:
  Notification that a new link is available
  Notification that an existing link is about to be shutdown
  Notification that a radio is switching channels/bands
    May be possible to address using extended CSA
TID-to-link-mapping approach is not the answer
  TID to link mapping is a short term solution
  No way to add a new link
  No way to permanently remove a link
  “Negotiated”, i.e. the receiver may reject

## Slide 4: Case 2 : Reachability Disparities
Link qualities between two MLDs may vary
  If the STA and AP can communicate in one link, there is no guarantee that they will also be able to communicate in the other links
  Pathloss differences
    Path loss in 2.4 GHz generally smaller than in 5/6 GHz bands
  Transmit power differences
    Limited by regulation, hardware, or configuration
    Not necessarily reciprocal
  Antenna directionality differences
    Different antenna sets may be assigned to each link
    Impossible to predict/estimate
Directional disparity
  We may have poor connection in either direction (UL/DL), as a result of TX power differences.

## Slide 5: Case 2 : Reachability Disparities - Contd
5GHz Range
2.4GHz Range
Add 5GHz Link
Remove 5GHz Link
MLD AP
MLD Setup phase
  At setup, one or both ends may be missing a measurement in the other links.
  Option 1: link may be added to setup blindly
    By default all TIDs are mapped.
    Need method to initially disable until a measurement is available (e.g. beacon report)
  Option 2: link not granted in initial setup
    Once a measurement is available, then link is added
Post-MLD Setup/Association
  A moving STA can get in or out of range of some of the links
    For example, if moving from a large distance closer towards the AP, then a 5/6 GHz link may become viable at some point.
  Once other links become viable, we need a method to add the new link to the setup.
  Vice versa, if STA moves away from the AP, we may need to remove the 5/6 links and only rely on 2.4.

## Slide 6: Conclusions
We described the need for maintaining a dynamic set of links in MLD setups
  Links may need to be added or removed
  We should not require a new MLD setup in order to change the link set

## Slide 7: SP1
Do you agree that
  11be shall define mechanisms to add links to, and remove links from, an MLD setup.

## Slide 8: SP2
Do you agree that
  An AP MLD may announce the addition of a new link by adding a new MLA element in its Beacons/Probe Responses.
  A non-AP MLD may request the addition of a new link to an existing MLD setup
    Details of the request and response are TBD
  Any MLD entity may notify its counterpart that a link will be removed from the MLD setup.
    Notification details are TBD.
    Ultimatley link’s information element from Beacon/Probe Reponses will be omitted

## Slide 9: References
[1] 11be SFD