## Slide 1: MLO: Link Info in Mgmt. Frames
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Yanjun Sun | Qualcomm Inc. |  |  | 
Date: 2020-04-20

## Slide 2: Problem statement
A non-AP MLD can perform basic BSS operations on a single link [1, 2]
  For example, it may do so to conserve power or it may be a single radio device
In addition, a STA may be unreachable due to range or channel congestion reasons.
The MLO framework needs to provide a mechanism to convey time critical updates for a link when a non-AP STA may be unreachable or in doze state
  Updates related to operational parameter changes, schedule changes or resetting of timers need to be conveyed as quickly as possible
  For example:
    A STA of an MLD may want to change parameter(s) or schedule for an individual TWT
    An AP of an AP MLD may want to reset the MU EDCA parameter for certain AC(s)
    A STA of a non-AP MLD may want to change its operating BW

## Slide 3: Solution: Link Info in Mgmt. frames
An individually addressed Mgmt. frame intended for an MLO receiver carries link identifier to indicate the link(s) for which the information applies to.
Requirements for carrying link identifier info:
  Should not require any changes to existing mgmt. frame format
  Security: Container should be protected so that link ID information is not tampered by an attacker
  Fixed location: simplifies parsing logic
    aids rx-ing STA can quickly determine the link for which the frame’s contents apply to without requiring it to parse the entire frame.
    Rx-ing STA can pass the frame to the relevant module for parsing the contents.

## Slide 4: Thoughts on carrying Link ID
Option 1: Use Address 3 field of MAC header
  Pros: Link ID carried at fixed location and A3 field is protected
  Cons: ?
Option 2: Use HE Control
  Define new A-Control to carry link ID
    Pros: Link ID carried at fixed location
    Cons: HE Control field is not protected
Option 3: Link ID carried as a new element within the frame
    Element carried as the last element in the frame structure
    Pros: Frame content protected
    Cons: Doesn’t provide a fixed location for link info.
      the receiving STA needs to parse the entire frame before it can determine the link for which the contents apply to
Address 3 field (option 1) meets all the requirements

## Slide 5: Address 3 field indicates desired recipient
Currently, the A3 field identifies the intended BSSID
11be MLO will repurpose the field to carry the MAC addr of the recipient STA or MLD for which the information is applicable
When MLD addr is same as one of the STA addr, there will be an ambiguity
    Some thoughts on next slide on how to differentiate MLD vs STA
Notes: For IDF – multi Ies with identifier
Multi-frame
A-MPDU

## Slide 6: Differentiating MLD vs STA
Option A: Based on the frame
  Standard clearly calls out the frames which are intended to the MLD
  For example:
    (Re)Association Request/Response or Authentication frames are always directed to the MLD
Option B: Use a reserved field in the MAC header to signal
  For example, the following combination is reserved for mgmt. frames:
    To DS set to 0 and From DS set to 1 or To DS set to 1 and From DS set to 1
Option C: Spec requires that MLD address is unique
Option A or option A+B should be sufficient to resolve ambiguity
Notes: For IDF – multi Ies with identifier
Multi-frame
A-MPDU

## Slide 7: Example of link signaling in mgmt. frames
TWT Information frame transmitted on one link includes a link identifier to update the schedule or parameter(s) for another link when the non-AP STA on the affected link is assumed to be in doze state (e.g., outside TWT SP)
  Similarly a non-AP STA can indicate an update to the operating BW of another STA of its non-AP MLD while the other STA is in doze state

## Slide 8: Summary
This contribution motivates the need to include link identifier in mgmt. frames directed to an MLO receiver
  Proposes to use Address 3 field to identify the STA or MLD for which the contents of the frame are directed to
    No change to Mgmt. frame format
  The scheme is useful when providing time critical updates such as schedule change, resetting timers or changing basic operational parameters for a STA that is in doze state or unreachable due to channel or range conditions

## Slide 9: SP #1
Do you support that an individually addressed Mgmt. frame intended for an MLO receiver shall identify the intended recipient of the frame’s contents via the Address 3 field of the frame?
  Note: intended recipient refers to the peer MLD or STA of the peer MLD
  Y:
  N:
  A:

## Slide 10: SP #2
Do you support that 11be amendment shall provide a mechanism to differentiate whether a Mgmt. frame is intended for a STA of an MLD or the MLD when the MLD MAC addr is same as the STA’s MAC address?
  Y:
  N:
  A:

## Slide 11: References
[1]: 11-19-1526 Multi-link Power-save (Abhishek Patil, Qualcomm)
[2]: 11-19-1542 Multi-link Broadcast Addressed Frame Reception (Po-Kai Huang, Intel)