## Slide 1: MLO: Link Info in Mgmt. Frames
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Yanjun Sun | Qualcomm Inc. |  |  | 
Date: 2020-04-20

## Slide 2: Motivation
A non-AP MLD can perform basic BSS operations on a single link
  It may do so, for example, to conserve power or it may be a single radio device
  In addition, a STA of a non-AP MLD may be unreachable due to range or channel conditions.
There are several individually addressed mgmt. frames whose content applies to a particular link
  For example updating the TWT schedule for certain link (TWT Info frame) or updating operating mode parameters (OMN frame) for a certain link or resetting certain times (e.g., MU-EDCA Reset) for a certain STA of a non-AP MLD
  In case of MLO, the non-AP MLD may be in doze state on a subset of links
How can an AP MLD deliver link specific mgmt. frame for a dozing STA of a non-AP MLD?
  The MLO framework needs to provide a mechanism to handle such scenarios
NOTE: mgmt. frames directed to the MLD (link agnostic) can be sent on any available link

## Slide 3: Solution
Include link information in an individually addressed mgmt. frame
Receiving MLD applies the content of the mgmt. frame to the link indicated in the link info

## Slide 4: Example of TWT schedule update for a dozing link

## Slide 5: Some thoughts on signaling of Link Info.
Requirements for carrying link info:
  Should not require any changes to existing mgmt. frame format
  Fixed location to simplify parsing at the receiving side
Possible options for signaling link info:
  A-Control field
    Needs security considerations
  Address 3 field of an individually addressed mgmt. frame

## Slide 6: Summary
This contribution motivates the need to identify the link for which the contents of an individually addressed mgmt. frame apply to
  The scheme is useful when providing link-specific information (such as schedule changes, resetting timers or updates to operational parameters) for a STA of an MLD that is in doze state

## Slide 7: SP #1
Do you support that 11be spec shall provide a mechanism to identify the link for which the contents of an individually addressed mgmt. frame apply to?
  NOTE – mechanism to identify the link is TBD
  Y:
  N:
  A:

## Slide 8: References
[1]: 11-19-1526 Multi-link Power-save (Abhishek Patil, Qualcomm)
[2]: 11-19-1542 Multi-link Broadcast Addressed Frame Reception (Po-Kai Huang, Intel)

## Slide 9: Resetting MU EDCA for a dozing link
MU-EDCA Reset sent on link2 identifies link1 as the intended link for which the reset applies