## Slide 1
Tentative (Re)association for Non-AP MLD
Date: 2020-05-19
Authors:
Name | Affiliations | Address | Phone | Email
Guogang Huang | Huawei | Shenzhen, China |  | huangguogang1@huawei.com
Ming Gan |  |  |  | ming.gan@huawei.com
Yunbo Li |  |  |  | liyunbo@huawei.com
Yuchen Guo |  |  |  | guoyuchen@huawei.com
Yifan Zhou |  |  |  | zhouyifan8@huawei.com
Yiqing Li |  |  |  | liyiqing3@huawei.com

## Slide 2
Contribution [1] first proposed the “Make Before Break” concept to reduce the gap in data delivery during a roaming in 2003
  Exploit the power save mechanism to communicate to both old AP and new AP on the different channels
Considering the fact of inter-frequency deployment and the limitation of only one single radio, the data delivery will be still interrupted during the tentative association with the new AP on a different channel
This contribution will address how to implement the “Make Before Break” scheme under the MLD framework
Introduction

## Slide 3
Necessary Actions before data transfer
  802.11 open system authentication
  Exchange Association Request/Response frames
  802.1X authentication if needed
    Derived PMK
  4-way handshake if needed
    Derived PTK and GTK
After successful (re)association, the AP will automatically send DS-STA-NOTIFY.request primitive to the DS to provide STA-AP mapping info
  The DS uses the STA-AP mapping info to decide how to route the MSDU addressed to this associated STA
Recap-Association Operation
(PMK)
Sending DS-STA-NOTIFY. Primitive to DS

## Slide 4
Main Idea
  In order to minimize or eliminate any gap in data delivery while roaming, it is proposed to let a STA make a partial connection with a new AP without dropping the connection with the old AP.
  Then the STA can negotiate with the new AP to set up the correct conditions for data connectivity, while still using the old AP for data connectivity.
  Once the correct conditions are set up, the new AP will trigger DS-STA-NOTIFY.request primitive to update STA-AP mapping info. The STA can then break the connection with the old AP, and start using the new AP for data connectivity.
Recap-Make Before Break [1]

## Slide 5
Split necessary actions before data transfer into two parts
  Part-1 action. All necessary actions except of sending the DS-STA-NOTIFY.request primitive to the DS, e.g.
    Open Authentication,
    Exchange Association Request/Response frames
    802.1 X authentication, 4-way handshake to generate PTK and GTK,
    Exchange ADDTS Request/Response frames to register a time-sensitive traffic flow
    Exchange ADDBA Request/Response frames to set up BA agreement
  Part-2 action. Sending the DS-STA-NOTIFY.request primitive to the DS
Make Before Break under MLD Framework

## Slide 6
Phase 1. Prior roaming
  Non-AP MLD inform AP MLD 1 to disable Link 12 due to low RSSI. Then non-AP MLD will let STA 2 to do the multi-link tentative association with neighboring candidate AP MLD or AP
Make Before Break under MLD Framework
Moving direction

## Slide 7
Phase 2. During roaming
  STA 2 affiliated with non-AP MLD tries to do the tentative multi-link association with AP MLD 2 on CH2@2.4 GHz. In the Multi-link Re-association Request/Response frame, non-AP MLD will inform AP MLD 2 to disable link 21. The the following action within Part-1 action set maybe included, e.g.
    802.11 Authentication Request/Response frames exchange
    (Multi-link) Re-association Request/Response frames exchange
    ADDTS Request/Response exchange to add a time-sensitive TS
    ADDBA Request/Response exchange to set up BA agreement
  Meanwhile, non-AP MLD still can deliver data traffic with AP MLD 1 through Link 11
Make Before Break under MLD Framework
Moving direction

## Slide 8
Phase 3. Post roaming
  Step 1. Non-AP MLD sends a new frame to trigger AP MLD 2 to send the DS-STA-NOTIFY.request primitive to the DS. This will cause that all MSDUs belonged to non-AP MLD will be routed to AP MLD 2.
  Step 2. Then non-AP MLD is allowed to deliver data with AP MLD 2 only through link 22. STA 1 affiliated with non-AP MLD can switch to CH2@5 GHz.
  Step 3. When entering the coverage of AP 21 affiliated with AP MLD 2, non-AP MLD can inform AP MLD 2 to enable link 21. Then non-AP MLD is allowed to deliver data with AP MLD 2 through both Link 21 and Link 22
From the above roaming procedure, we can see that the data delivery with non-AP MLD is not interrupted.
Make Before Break under MLD Framework
Moving direction

## Slide 9
Extension
  For the roaming scenario, assuming that Non-AP MLD having 3 links, it can disable two links and initiate tentative re-association with two neighboring AP MLDs simultaneously. Finally, the Non-AP MLD would have to complete the association with only one AP MLD by sending STA-AP Mapping NOTIFY frame.
    Pros. Increase the success probability of roaming considering the roaming may be rejected by candidate AP MLD due to the specific admission control policy or some reason
  The proposed scheme also can extend to the initial association.
Make Before Break under MLD Framework

## Slide 10
Procedure of BSS Transition using tentative reassociation
STA 1
STA 2
Non-AP MLD
Current AP MLD
Target AP MLD
Tentative Reassociation Request (RSNE[PMKID])
Tentative Reassociation Response (RSNE[PMKID])
Data delivery between current AP MLD and non-AP MLD though STA 1
ADDTS Request
ADDTS Response
ADDBA Request
ADDBA Response
Sending a new frame or existing frame, e.g. Data frame or QoS Null frame to trigger Target AP MLD sending DS-STA-NOTIFY.request primitive to DS
Sending DS-STA-NOTIFY.request primitive to DS
Decide to switch data delivery from current AP to target AP
Key Message 1
Key Message 2
Key Message 3
Key Message 4
Sending DS-STA-NOTIFY.request primitive to DS

## Slide 11
Procedure of Fast BSS transition using tentative reassociation
STA 1
STA 2
Non-AP MLD
Current AP MLD
Target AP MLD
802.11 Authentication-Request (FTAA, RSNE[PMK0Name], MDE, FTE[SNonce, R0KH-ID])
802.11 Authentication-Response (FTAA, RSNE[PMK0Name], MDE,FTE[ANonce, SNonce, R1KH-ID, R0KH-ID])
Tentative Reassociation Request (RSNE[PMKR1Name], MDE,FTE[MIC, ANonce, SNonce, R1KH-ID, R0KH-ID])
Tentative Reassociation Response (RSNE[PMKR1Name], MDE,FTE[MIC, ANonce, SNonce, R1KH-ID, R0KH-ID, GTK[N]], IGTK[M])
Data delivery between current AP MLD and non-AP MLD though STA 1
ADDTS Request
ADDTS Response
ADDBA Request
ADDBA Response
Sending a new frame or existing frame, e.g. Data frame or QoS Null frame to trigger Target AP MLD sending DS-STA-NOTIFY.request primitive to DS
Sending DS-STA-NOTIFY.request primitive to DS
Decide to switch data delivery from current AP to target AP
Sending DS-STA-NOTIFY.request primitive to DS

## Slide 12
Signaling of link status
  Option 1. Non-AP MLD needs to explicitly indicate the status of each non-transmitted link in the Association Request frame
    Disable. For the disable link, maybe further indicate the corresponding Reason Code, e.g. power save, low RSSI and unreachable, tentative association and so on.
    Enable.
  Option 2. use the TID-to-link mapping to implicitly indicate the status of each non-transmitted link in the Association Request frame
Capability indication for tentative association
  Can be carried in Fast BSS Transition element , Mobility Domain element, RSNE or EHT Capabilities element
Related Signaling Indication

## Slide 13
Signaling of tentative association
  In order to allow non-AP MLD simultaneously initiating tentative association with multiple AP MLDs, a frame needs to be defined to trigger AP MLD sending DS-STA-NOTIFY.request
    e.g. new announcement frame or uplink data frame or QoS Null frame
  To differentiate with the conventional association, a signaling indication for tentative association needs to be carried in the Association Request frame
    One method is to define a new element, named Tentative Association element, which includes the following info
      Non-AP MLD Trigger STA-AP Mapping NOTIFY. Set to 1, indicate the non-AP MLD will proactively send a frame to trigger the STA-AP Mapping NOTIFY procedure
      Tentative Association Lifetime. Indicate the tentative association age-out time. Any communication between the non-AP MLD and AP MLD will reset the timer.
Related Signaling Indication (Cont.)
Element ID
Length
Tentative Association Control
Tentative Association Lifetime
Non-AP MLD Trigger STA-AP Mapping NOTIFY
Reserved
B0
B1
B7

## Slide 14
In this contribution, we describe that how to implement the “Make before Break” scheme [1] under the MLD framework.
  The proposed tentative association can really realize that the data delivery is not interrupted during the roaming by exploiting multiple radios of non-AP MLD
    Reduce the delay introduced by ADDTS and ADDBA procedure
    If non-AP MLD expects to transmit/receive data through multiple links with AP MLD, the BA agreement needs to be previously setup.
  It also allows the non-AP MLD to decide the most appropriate time point to immediately switch to an appropriate candidate AP/AP MLD.
    Avoid the ping-pong effect
    Increase the success probability of roaming if some admission control policy is applied to the AP side
Summary

## Slide 15
[1] 11-03-0770-06-frfh-make-before-break
Reference

## Slide 16
Do you support to define tentative (re)association operation in 11be R2?
  NOTE. For the tentative (re)association operation, the non-AP MLD needs to proactively send a specific frame to trigger AP sending DS-STA-NOTIFY.request primitive to the DS, rather than AP automatically sending this primitive after successful (re)association.
  Y
  N
  A
Straw Poll

## Slide 17
Appendix

## Slide 18
Q: In the current Spec., when does the AP send the DS-STA-NOTIFY.request primitive to DS?
  The current Spec. doesn’t clearly define when the AP sending the DS-STA-NOTIFY.request primitive to DS. But from the text, we can interpret that the AP will automatically send DS-STA-NOTIFY.request primitive to the DS after successful association.
Question 1

## Slide 19
From this figure, it clearly demonstrates that
  For both of the no RSNA required case and the RSNA required case, the Class 3 frames are allowed to transmit after successful (re)association.
  Hence, the DS-STA-NOTIFY.request primitive is sent after successful (re)association
Question 1 (Cont.)

## Slide 20
Q: If changing the time of sending DS-STA-NOTIFY.request primitive to DS, whether it will impact to the current 802.1X authentication and 4-way handshake?
  No impact to the current 802.1X authentication and 4-way handshake. Because during IEEE 802.1X authentication, AP served as an intermediary agent between STA and Authentication Server. That means that the DS doesn’t need to know the STA-AP mapping info in this period.
  Note. A single IEEE 802.1X Port maps to one association, and each association maps to an IEEE 802.1X Port. Each association between a pair of STAs creates a unique pair of IEEE 802.1X Ports, and authentication takes place relative to those ports alone. An IEEE 802.1X Port consists of an IEEE 802.1X Controlled Port and an IEEE 802.1X Uncontrolled Port.
  IEEE 802.1X EAPOL PDUs are carried as MSDUs within one or more Data frames and passed via the IEEE 802.1X Uncontrolled Port.
  The IEEE 802.1X Controlled Port is blocked from passing general data traffic between two STAs until an IEEE 802.1X authentication procedure completes successfully over the IEEE 802.1X Uncontrolled Port.
Question 2

## Slide 21
Q: In the current Spec., it defines that “a STA is associated with no more than one AP”. Does the tentative association break this principle?
  No.
  The reason for “a STA is associated with no more than one AP” is that the DS needs to know a unique answer to the question, “Which AP is serving STA X?”. This STA-AP mapping info is provided by AP sending DS-STA-NOTIFY.request primitive to DS. During the tentative association operation, the STA-AP mapping info is always unique.
Question 3

## Slide 22
Q: The resource request (i.e. ADDTS and ADDBA) is already allowed to do during association operation. Why do we need to define the tentative (re)association?
  In 802.11 Spec-2016, BA agreement and TS can be set up according to the following methods when STA is roaming
    Method 1. FT Resource Request protocol
      Nobody implements this protocol
    Method 2. Re-association Request/Response frames carrying corresponding Resource information container (RIC)
      This method is not flexible. For example, when the association succeeds but the resource request failed, there is no opportunity to renegotiate resource request with this AP before sending DS-STA-NOTIFY.request primitive to DS.
      When the resource request failed, it will influence the roaming decision
Question 4

## Slide 23
Question 4 (Cont.)
RDE
RIC Descriptor (BlockAck)
RDE
TSPEC
TCLAS
RDE
RIC Descriptor (BlockAck)
RDE
TSPEC
Schedule
Resource Request
Resource Response
Resource Request #1
Resource Request #2
Resource Response #1
Resource Response #2