## Slide 1: MLO BSS Information Transmission with and without Multiple BSSID
Date: 2020-06-01
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: AP MLD with and without Multiple BSSID in Multiple Links
An AP MLD may support multiple BSSID feature in one link while not supporting multiple BSSID feature in another link.
ML element with Per Link Info elements is used to carry MLO information.
ML element may be carried in Multiple BSSID element.
Elements related to Multiple BSSID are not carried in Association Response frame.
A STA affiliated with a STA MLO and a non-EHT STA may associate with an AP affiliated with an AP MLD.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.

## Slide 3: SSID and Security of AP Affiliated with AP MLD
SSID:
  An AP in a link affiliated with an AP MLD belongs to one SSID:
    A non-EHT STA associated with the AP and a STA MLD that has multi-link association with the AP MLD through the AP see the same SSID.
    In order for the AP device supports different SSIDs in the link, multiple virtual APs are announced in the link.
  All the APs affiliated with an AP MLD belongs to one SSID
Security:
  An AP in a link affiliated with AP MLD supports one security policy:
    A non-EHT STA associated with the AP and a STA MLD that has multi-link association with the AP MLD through the AP see the same security policy.
  In order for the AP device supports different security policies in the link, multiple virtual APs are announced in the link where each virtual AP announces its own security policy.

## Slide 4: Inheritance
Recap: The inheritance similar to 802.11ax is used for MLO:
  Non-Inheritance element defines which information is not inherited by the reported STA from the reporting AP as the frame transmitter or the reporting AP as the non-transmitted BSSID.
  Otherwise the information of the reporting AP is inherited.
  Issue: there is some cases where no inheritance is preferable.
One mode is defined where no-inheritance is applied to the reported AP.

## Slide 5: Incomplete Information after Multi-Link Association
Through the Probe Response in one link (e.g. link 1), a STA MLD may not know the Multiple BSSID arrangement:
  The Per Link Info for an AP in another link (e.g. link2) doesn’t include the Multiple BSSID element.
    Every AP’s Beacon in the link carries the AP in another link that is affiliated with the same AP MLD as the Beacon transmitter.
In the Association Response frame, the Multiple BSSID element and/or Multiple BSSID Configuration element are not carried.
After association, the following features don’t work correctly:
  NAV maintenance.
    Some PPDUs from APs that are in same device with associated AP may be discarded.
  Rx Control Frame To MultiBSS doesn’t work correctly.
    The transmitted BSSID is not known.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are not defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.
AP1x and AP2x are affiliated with one AP MLD.

## Slide 6: Methods to Acquire Full BSS Information
The ML element in (Re)Association Response frame can carry the following information:
  the transmitted BSSID through Multiple BSSID Index,
  the MaxBSSID Indicator.

## Slide 7: Straw Poll 1
Do you support that
  Each AP affiliated with an AP MLD shall have only one SSID that is same as the SSID of the AP MLD.

## Slide 8: Straw Poll 2
Do you support to define a mode where no-inheritance is applied to the reported AP?

## Slide 9: Straw Poll 3
Do you support that the reported AP’s profile in the ML element in Association Response frame shall carry the following information if the reported AP is a non-transmitted BSSID: the non-transmitted BSSID index, the MaxBSSID Indicator?
  Signaling TBD