## Slide 1: Multi-link Individual Addressed Management Frame Delivery
Date: 2020-05-28
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Danny Alexander |  |  |  | 
Daniel F Bravo |  |  |  | 
Ido Ouzieli |  |  |  | 
Robert Stacey |  |  |  | 
Laurent Cariou |  |  |  | 
Notes: September 2012

## Slide 2: Background
Current individual addressed management frame is transmitted in order from the transmitter in only one link
  There is at most one outstanding MMPDU for a specific RA
  Receiver remembers the latest received SN and uses retry bit to detect duplicate
  Under PMF, receiver keeps one replay counter to check for replay
With multi-link, the individual addressed management frame maybe delivered in multiple links
  We discuss how to extend baseline rule to maintain management frame functionalities, achieving duplicate detection, and achieving replay check under PMF
Individual addressed Management
Missed ACK
Retransmitted Individual addressed Management
Filtered out as duplicate

## Slide 3: Requirement of In Order MMPDU Delivery to maintain functionalities
BA management
TS management
Setup management
Needs above transmission in different links to be in order to have correct functionalities like today
Current spec achieves in order delivery by allowing only one outstanding MMPDU and we need to extend to rule to across links
DELBA
ADDBA
Request
DELTS
ADDTS
Request
Multi-link teardown
Multi-link setup request

## Slide 4: Requirement of Duplicate Detection
Need retransmission in different links (if allowed) to be filtered out if it is a duplicate. Shared SN space across links and in order delivery across links are then required to achieve duplicate check
Individual addressed management frame currently shares SN space with group addressed data frame, group addressed management frame, and non-QoS Data frame
Retransmission individual addressed MMPDU in different links is not possible to avoid duplicate unless we enable separate shared SN space across links for individual addressed management frame
  Receiver only maintains most recent record per MLD for individual addressed management frame to check duplicate which is a straightforward extension of current rule
AP 1
AP 2
Non-AP 1
Non-AP 2
Management frame 1
SN x
Management frame 1
SN x

## Slide 5: Requirement of In Order MMPDU Delivery to make PMF replay check work
Under PMF, which uses PTK and one PN space, different management frame needs in order delivery across links for replay check using PN
Receiver only maintains one replay counter per MLD for individual addressed management frame to check replay, which is a straightforward extension of current rule
Breaking in order delivery rule leads to more complicated design for replay check
AP 1
AP 2
Non-AP 1
Non-AP 2
Management frame 1
PN x
Management frame 1
PN x

## Slide 6: Exception
We propose to exclude the following individual addressed frames for further consideration
  Sounding feedback:
    Maybe sent at any time to break in order requirement
    Usually handle in hardware and is hard to use sharing SN space across links
  FTM and LMR:
    Maybe sent at any time to break in order requirement
    Discuss separately in 11az and should be discussed separately in 11be
  Probe response
    Includes TSF and is hard to use sharing SN space across links
For QMF, we propose to focus on the basic rule first, then discuss extension to QMF separately.

## Slide 7: Proposal for Transmitter MLD
Requirement for only one outstanding frame:
  A MLD shall have no more than one outstanding MMPDU (except sounding feedback, probe response, FTM, and LMR) transmitted to another MLD in any links at any time
  Note - The term outstanding refers to an MPDU containing all or part of an MSDU or MMPDU for which transmission has been started, and for which delivery of the MSDU or MMPDU has not yet been completed (i.e., an acknowledgment of the final fragment (#1452)or only corresponding MPDU has not been received and the MSDU or MMPDU has not been discarded due to retries, lifetime, or for some other reason).
Requirement to continue the transmission attempt of the failed MMPDU
  A MLD continues the transmission attempt of the failed MMPDU (except sounding feedback, probe response, FTM, and LMR) until retry limit is met or the MMPDU is successfully delivered whichever occurs first
The above rule is very similar to individual addressed data frame without BA and does not involve further complicated design

## Slide 8: Proposal for SN space
Proposal: Expand Table 10-5—Transmitter sequence number spaces to have a new entry for delivering individual addressed management frame (except sounding feedback and probe response, LMR and FTM) Indexed by <destined MLD Address>
  Aligned with the direction that we already have shared PTK and PN space
  Extension of existing rule about duplicate detection and replay detection to MLD is then natural
  Implementation can be done because of similar requirement for individual addressed data frame
  Retransmission of management frame in different link (if allowed) is feasible
  There is no complication for operation with legacy STAs

## Slide 9: Proposal for Receiver MLD
Extend baseline rule to MLD level
    Expand Table 10-6—Receiver caches to have a new entry for individual addressed management frame (except sounding feedback and probe response, LMR and FTM) indexed by <peer MLD address, sequence number
    Maintain at least the most recent record of <peer MLD address, sequence number> for received individual addressed MMPDU (except sounding feedback and probe response, LMR and FTM)
    Drop the MMPDU (except sounding feedback and probe response, LMR and FTM) with retry bit set and record match
The above rule is very similar to individual addressed data frame without BA
There is a recommendation in baseline to have separate entry for individual addressed management frame anyway

## Slide 10: Conclusion
We discuss how to transmit individual addressed MMPDU in multi-link
  Exclude sounding feedback, probe response, LMR and FTM for further discussion
  QMF is TBD
We propose the following:
  At most one outstanding individual addressed MMPDU
  Continue the transmission attempt of the failed MMPDU until retry limit is met or the MMPDU is successfully delivered whichever occurs first
  Separate Shared SN space for individual addressed management frame
    For transmitter
      Expand Table 10-5—Transmitter sequence number spaces to have a new entry for individual addressed management frame Indexed by <destined MLD Address>
    For receiver
      Expand Table 10-6—Receiver caches to have a new entry for individual addressed management frame indexed by <peer MLD address, sequence number
      Maintain at least the most recent record of <peer MLD address, sequence number> for received individual addressed MMPDU
      Drop the MMPDU with retry bit set and record match

## Slide 11: Straw Poll
Do you support to include the following in 11be SFD in R1?
Deliver individual addressed management frame (except sounding feedback, probe response, LMR and FTM) between two MLDs as follows:
  For transmitter MLD
    Expand Table 10-5—Transmitter sequence number spaces to have a new entry for delivering individual addressed management frame (except sounding feedback and probe response, LMR and FTM) Indexed by <destined MLD Address>
    A MLD shall have no more than one outstanding MMPDU (except sounding feedback and probe response, LMR and FTM) transmitted to another MLD in any links at any time
    A MLD continues the transmission attempt of the failed MMPDU (except sounding feedback, probe response, LMR and FTM) until retry limit is met or the MMPDU is successfully delivered whichever occurs first
  For receiver MLD
    Expand Table 10-6—Receiver caches to have a new entry for individual addressed management frame (except sounding feedback, probe response , LMR and FTM) indexed by <peer MLD address, sequence number>
    Maintain at least the most recent record of <peer MLD address, sequence number> for received individual addressed MMPDU (except sounding feedback, probe response, LMR and FTM)
    Drop the MMPDU (except sounding feedback and probe response, LMR and FTM) with retry bit set and record match
NOTE- QMF is TBD