## Slide 1: LDPC Tone Mapping for NGV
Date: 2020-06-10
Authors:

## Slide 2: Introduction
LDPC has been adopted as the only coding scheme for data portion of 11bd PPDU [1]
Tone mapper for LDPC has not been agreed upon yet
This presentation provides some analysis on the necessity of tone mapper and
Discuss about the correct reference for LDPC encoding process

## Slide 3: Background [3]
In 11n, interleaving was not needed for LDPC, since
  Each 1944-bit LDPC code covers almost all streams and tones within an OFDM symbol
  LDPC has an intrinsic pseudo-randomness property that protects it against burst errors
In higher rates of 11ac, the length of the LDPC codeword can be significantly smaller than the number of bits in an OFDM symbol (NCBPS)
  80MHz/160MHz and/or 256QAM lead to larger NCBPS
  The coded bits from each LDPC codeword are transmitted only through a fraction of the tones, thus not achieving the full frequency diversity
A tone mapping scheme was adopted during 11ac to capture the full frequency diversity without the extra delay of interleaving

## Slide 4: Analysis on Tone Mapper for NGV (Non DCM)
BW 10 MHz
  NCBPS <= 52 * 8(256QAM) * 1(NSS) = 416 < 1CW(1944)
  NCBPS <= 52 * 8(256QAM) * 2(NSS) = 832 < 1CW
BW 20 MHz
  NCBPS <= 108 * 8(256QAM) * 1(NSS) = 864 < 1CW
  NCBPS <= 108 * 8(256QAM) * 2(NSS) = 1728 < 1CW
Tone mapping is not required
  Similar to 11n

## Slide 5: Analysis on Tone Mapper for NGV (BPSK DCM)
BW 10 MHz
  NCBPS <= 26 * 1(BPSK) * 1(NSS) = 26 << 1CW(1944)
  NCBPS <= 26 * 1(BPSK) * 2(NSS) = 52 << 1CW
BW 20 MHz
  NCBPS <= 54 * 1(BPSK) * 1(NSS) = 54 << 1CW
  NCBPS <= 54 * 1(BPSK) * 2(NSS) = 108 << 1CW
Tone mapping is not required at all for 11bd PPDUs

## Slide 6: LDPC Encoding Process
It has been agreed that 11bd devices shall support LDPC codes, with the same code structure and coding methods as defined in 19.3.11.7 (LDPC Codes) [2]
LDPC encoding process of 11bd is similar to that of 11ac
  No PSDU length signaling as in 11n HT-SIG
  APEP_LENGTH is used as in 11ac
Propose to define 11bd LDPC encoding process as specified in 21.3.10.5.4(LDPC coding)
  Note: Set mSTBC = 1

## Slide 7: Summary
Provided a background on the LDPC tone mapping
Analyzed the necessity of LDPC tone mapping for NGV
LDPC tone mapping is not required for 11bd PPDU
Define 11bd LDPC encoding process as that of 11ac

## Slide 8: Reference
[1] Rui Cao and etc., “Discussion on NGV PHY Modes”, 11-20/0045r3
[2] Prashant Sharma and etc., “LDPC Investigation for 11bd”, 11-20/0346r3
[3] Jun Zheng and etc., “LDPC for 11ac”, 11-10/1300r0

## Slide 9: Straw Poll 1
Do you agree that 11bd does not define LDPC Tone Mapper?
Y:
N:
A:

## Slide 10: Straw Poll 2
Do you agree that 11bd PPDU uses the same LDPC encoding process as defined in 21.3.10.5.4(LDPC coding) with parameter mSTBC set to 1?
Note: This over-rides part of Motion #12
Y:
N:
A: