## Slide 1: NS/EP Priority Service Capability Information
Date: 2020-07-10
Authors:

## Slide 2: Overview
Priority access support for National Security and Emergency Preparedness (NS/EP) priority services was approved as a work item in IEEE 802.11be during January 2020 meeting [1]
Priority access indication support for National Security and Emergency Preparedness (NS/EP) Priority Services was accepted in June Teleconference [2]
Objective Summary
  A standardized mechanism to support the NS/EP Priority Services in WLANs without requiring additional infrastructure
  Priority Access in IEEE 802.11be would also be beneficial to other services ( e.g., Public-Safety Mission-Critical Services, Critical medical applications)

## Slide 3: Motivation
If the priority access for NS/EP Priority Services is supported in a BSS, non-AP STA should be able to gather such capability information from an AP STA before Association/Re-association
If the priority access for NS/EP Priority Services is supported in a non-AP STA, it should be able to provide such capability information to an AP STA

## Slide 4: Priority Service Capability Information
We propose to include the NS/EP Priority Service capability information in EHT MAC Capability Information Element

## Slide 5: Indicating Priority Service Capability
When dot11PriorityService is true, priority channel access for NS/EP Priority Service shall be supported
When priority channel access is not supported, dot11PriorityService is false
When the IEEE 802.11 infrastructure is informed of the availability of Priority Service (the mechanism by which is outside the scope of this standard), an AP STA with dot11PriorityService equal true shall advertise the support of the priority channel access by including the Priority Service Information in its Beacon and Probe Response frames
A non-AP STA with dot11PrirotiyService equal true shall include the Priority Service Information in its Probe Request and (Re) Association Request frames
Variable
EHT Capabilities Element ID | Length | … .. EHT MAC Capabilities Information …….
Octets
1
1
…… Priority Service Info ………

## Slide 6: Straw Poll #1
Do you support the addition of following text to TGbe SFD?
  The Priority Service Information shall be defined in EHT MAC Capability Information Element to exchange the Priority Service capability information
Y:
  N:
  A:

## Slide 7: Straw Poll #2
Do you support the addition of following text to TGbe SFD?
  The Priority Service if supported by a BSS, AP STA shall advertise such capability information in Beacon and Probe Response frames
  The Priority Service if supported by a non-AP STA, non-AP STA shall include such capability information in Probe Request and (Re) Association Request frames
Y:
  N:
  A:

## Slide 8: References
[1] 11-19-1901-04-00be-priority-access-support-in-ieee-802-11be-what-and-why.pptx
[2] 11-20-0463-03-00be-priority-access-support-options-for-ns-ep-serveices.pptx
[3] 11-20-0021-01-00be-Priority-Access-support_for_NS_EP_Services.pptx,
[4] IEEE P802.11ax™/D6.0, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications, Amendment 1: Enhancements for High Efficiency WLAN”, November 2019
[5] IEEE Std 802.11™-2016, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications”, 7 December 2016