## Slide 1: NS/EP Priority Service Capability Information and Indication
Date: 2020-07-10
Authors:

## Slide 2: Overview
Priority access support for National Security and Emergency Preparedness (NS/EP) priority services was approved as a work item in IEEE 802.11be during January 2020 meeting [1]
Priority access indication support for National Security and Emergency Preparedness (NS/EP) Priority Services was accepted in June Teleconference in [2]
Objective Summary
  A standardized mechanism to support the NS/EP Priority Services in WLANs without requiring additional infrastructure
  Priority Access in IEEE 802.11be would also be beneficial to other services ( e.g., Public-Safety Mission-Critical Services, Critical medical applications)

## Slide 3: NS/EP Priority Services
Service Objective: Provide priority access to system resources for a limited set of authorized users during network congestion
  Priority Access: Allow preferred access to the wireless medium during network congestion and/or failures to establish a data session
  Limited Set: Number of users is generally a small fraction of the overall user base
  Authorized Users: Only available to some designated individuals who are identified to receive such service
Existing NS/EP Priority Services in the US provide priority voice calls over public networks
  Government Emergency Telecommunications Service (GETS): Landline phone networks
  Wireless Priority Service (WPS): Wireless phone networks
  Next Generation Network Priority Services (NGN-PS): Providers’ IP-based communications networks
Many countries have similar priority telecommunications services, e.g.,
  Belgium: Blue Light Mobile, Canada: WPS, Czech Republic: Mobile Crisis Communications service, Great Britain: MTPAS
  GSM for Railway Communications deployed in multiple countries
NS/EP Priority Services are NOT Emergency Services (e.g., E911 in US; 112, 999, etc. in Europe)

## Slide 4: Assumptions/Requirements
If the priority access for NS/EP Priority Services is supported in a BSS, non-AP STA should be able to gather such capability information from an AP STA before Association/Re-association
If the priority access for NS/EP Priority Services is supported in a non-AP STA, it should be able to provide such capability information to an AP STA
NS/EP Priority Service user’s non-AP STA is associated with BSS prior to invocation of priority capabilities
  Authentication/Association and authorization occur via standard procedures
After association, AP STA has the knowledge of which non-AP STAs are authorized to use NS/EP priority services
NS/EP Priority Service non-AP STA will inform the AP STA regarding the need for Priority Service
Similarly, AP can instruct non-AP STA to enable the priority access
  The priority remains in effect until terminated by either party

## Slide 5: Proposed Approach
Add NS/EP Priority Service capability information in EHT MAC Capability Information Element
Use Action frames (request/response) to indicate the need (enable/disable) for NS/EP Priority Access

## Slide 6: Priority Service Capability
When dot11PriorityService is true, priority channel access for NS/EP Priority Service shall be supported
When priority channel access is not supported, dot11PriorityService is false
When the IEEE 802.11 infrastructure is informed of the availability of Priority Service (the mechanism by which is outside the scope of this standard), an AP STA with dot11PriorityService equal true shall advertise the support of the priority channel access by including the Priority Service Information in its Beacon and Probe Response frames
A non-AP STA with dot11PriorityService equal true shall include the Priority Service Information in its Probe Request and (Re) Association Request frames
Variable
EHT MAC Element ID | Length | …… Priority Service Info …….
Octets
1
1

## Slide 7: Priority Service Indication using Action Frame
Use Request and Response Action frames for enabling/disabling the NS/EP Priority Access
  Request Action frame is used to enable/disable the priority access, and Response Action frame is used to confirm/provide status
Non-AP STA initiated priority
  Non-AP STA sends NS/EP Request Action frame to AP STA to enable NS/EP priority access
    Request is only sent if non-AP STA is associated with an AP
  AP STA sends NS/EP Response Action frame to non-AP STA with status (e.g., SUCCESS)
AP STA initiated priority
  AP STA sends NS/EP Request Action frame to inform non-AP STA that priority access is being enabled
    e.g., start of incoming priority voice call to non-AP STA
  Non-AP STA sends NS/EP Response Action frame to AP STA to confirm receipt
When priority is no longer needed, AP STA or non-AP STA sends NS/EP Request Action frame to disable the Priority Access
  All priority features cease (for both AP and non-AP STA)
  Receipt of request is confirmed with a response

## Slide 8: Expected AP STA and non-AP STA Behavior
When priority access is enabled, priority is applied to all traffic to/from non-AP STA, including:
  AP STA treats all traffic to/from non-AP STA as AC_VO
    AP STA should give preference to traffic to/from non-AP STA over other AC_VO traffic
    Preference applies to ordering of DL MPDU delivery and to UL resource allocation
  Non-AP STA uses AC_VO EDCA parameters for all UL transmissions
When priority access is disabled, all traffic to/from non-AP STA is treated normally
  AP STA treats all DL traffic and assigns UL resources according to assigned ACs
  Non-AP STA uses AC-specific EDCA parameters for all UL transmissions

## Slide 9: Example Priority Service Action Frame Format*
Order | Information
1 | Category (TBD)
2 | Priority Service Action (Request)
3 | Dialog Token
4 | Request Type (Enable/Disable)
* Details TBD
Request Frame
Order | Information
1 | Category (TBD)
2 | Priority Service Action (Response)
3 | Dialog Token
4 | Status Code (Success/Failure)
Response Frame

## Slide 10: Summary
Proposed to use one bit in EHT MAC capability by which NS/EP Priority Service capability can be advertised and or queried
Proposed using dedicated Request/Response Action Frames to enable/disable the Priority Access

## Slide 11: Straw Poll #1
Do you support the addition of following text to TGbe SFD (R1)?
  The Priority Service Information shall be defined in EHT MAC Capability Information Element to exchange the NS/EP Priority Service capability information between AP MLD and non-AP MLD
Y:
  N:
  A:

## Slide 12: Amended Motion Text (#126)
Amend the following paragraph of the TGbe SFD
  The NS/EP Priority Service if supported by a non-AP STA, shall use a TID value (TBD) that is greater than 7 an action frame to indicate the need for priority access to its associated AP STA and to be included in Release 1 specification.
Move:
Second:
Discussion:

## Slide 13: References
[1] 11-19-1901-04-00be-priority-access-support-in-ieee-802-11be-what-and-why.pptx
[2] 11-20-0463-03-00be-priority-access-support-options-for-ns-ep-serveices.pptx
[3] 11-20-0021-01-00be-Priority-Access-support_for_NS_EP_Services.pptx,
[4] IEEE P802.11ax™/D6.0, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications, Amendment 1: Enhancements for High Efficiency WLAN”, November 2019
[5] IEEE Std 802.11™-2016, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications”, 7 December 2016