## Slide 1: Tone Plan Related Corrections
Date: 2020-06-25
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Abstract
It has been discussed in the PHY group that some corrections to old motions and figures in the SFD are needed in light of Motion 112, #SP42 (80MHz OFDMA tone plan)
While working on the proposed changes in the figures also revised them to reflect the SP as shown.
  925r0 On 52+26 M-RU (Ron Porat)
  Proposes one more location for 52+26 MRU.
  SP1 [20/0925r0]:
  Do you support adding the following combination [52,52+26,52,52] to the RU table to be used in 20MHz, 40MHz and 80MHz PPDU?
  Results
  Y/N/A: 36/1/15

## Slide 3: Proposed Figure 2
Added 52 + middle 26 for 20 and 40MHz

## Slide 4: Proposed Figure 3
Corrected 80MHz tone plan
Added 52 + middle 26

## Slide 5: Proposed Figure 4
Corrected 80MHz tone plan

## Slide 6: Motions’ Corrections (1)
802.11be reuses 802.11ax tone plan for 20/40/80/160/80+80 MHz PPDU. For 320 MHz and 160+160 MHz PPDU, 802.11be uses duplicated HE160 for OFDMA tone plan.
[Motion 33, [3] and [6]]
Editor’s note: This motion is expected to be updated because of Motion 112, #SP42.
Change to
802.11be reuses 802.11ax tone plan for 20/40/80/160/80+80 MHz PPDU and, with the exception of pilot locations, for 80/160/80+80 in non-OFDMA PPDU. For 320 MHz and 160+160 MHz PPDU, 802.11be uses duplicated HEEHT160.

## Slide 7: Motions’ Corrections (2)
802.11be 240/160+80 MHz transmission consists of 3x80 MHz segments while the tone plan of each 80 MHz segment is the same as HE80 in 802.11ax.
[Motion 35, [3] and [6]]
Editor’s note: This motion is expected to be updated because of Motion 112, #SP42.
Change to
802.11be 240/160+80 MHz transmission consists of 3x80 MHz segments while the tone plan of each 80 MHz segment is the same as HEEHT80.

## Slide 8: Motions’ Corrections (3)
The 802.11be 320/160+160 MHz non-OFDMA tone plan uses duplicated tone plan of HE160.
NOTE – Puncturing design TBD.
[Motion 34, [3] and [6]]
Editor’s note: This motion is partially superceded expected to be updated because of Motion 112, #SP42.
Change to
The 802.11be 320/160+160 MHz non-OFDMA tone plan uses duplicated tone plan of HEEHT160.