## Slide 1: Thoughts on U-SIG Contents
Date: 2020-06-25
Authors:

## Slide 2: Introduction
Followings are agreed to be included [1]
  In U-SIG
    PHY version identifier: 3 bits
    UL/DL flag: 1 bit
    BSS color: TBD bits
    TXOP duration: TBD bits
    Bandwidth: TBD bits. This field may also convey some puncturing information
    Puncturing Channel Information: TBD bits
    PPDU Type: TBD bits
    EHT-SIG MCS (for multiple users)
    Number of EHT-SIG Symbols (for multiple users)
    GI+EHT-LTF Size
    Number of EHT-LTF symbols
    PE related parameters

## Slide 3: BSS Color and TXOP
If there is no request from MAC, let’s keep same number of bits as 802.11ax
Proposal: BSS Color 6bits
Proposal: TXOP 7bits

## Slide 4: Bandwidth Field
Bandwidth field conveys PPDU BW
20/40/80/160 or 80+80/240 or 160+80/320 or 160+160 MHz: total 6 cases
In case of 240 or 160+80MHz, there is discussion whether it is from 320MHz channelization and puncturing one of 80MHz or from 240MHz channelization
In any case, we believe 3bit PPDU BW should be enough
  At least 2 reserved. 320MHz is already wide enough before it belongs to UWB regulation (≥ 500MHz)
  If 240MHz is from 320MHz channelization with puncturing, then we can delete 240/160+80 from the entry of BW while use 320MHz and puncturing info (like other puncturing case)
Proposal: BW 3bits

## Slide 5: PPDU Type Field (1/4)
What kinds of PPDU type to support in 11be?
  TB, SU, MU, and potentially ER-SU
  Don’t need a separate PPDU Type code for ER-SU in U-SIG
    Can be distinguished by similar mechanism as in 11ax
    Supporting ER-SU is TBD

## Slide 6: PPDU Type Field (2/4)
Separate SU and MU vs. merging SU PPDU in MU compressed
  In aggregated PPDU or multi-segment EHT SIG [2] [3] [4], number of EHT-SIG symbols, GI+EHT-LTF Size, number of EHT-LTF symbols shall be same [5]
  From this point of view, now followings are agreed to be included in U-SIG (even for PPDU transmitted to a single user)
    Number of EHT-SIG Symbols, GI+EHT-LTF Size, Number of EHT-LTF symbols, PE related parameters
In this case, we need number of MU-MIMO Users field in Common field of MU compressed mode
  In this case, it seems difficult to make one EHT-SIG even for single user case
Proposal: 802.11be PPDU transmitted to a single user is using EHT MU PPDU compressed mode (there is no EHT SU PPDU)

## Slide 7: PPDU Type Field (3/4)
In uplink transmission, we can have 1 bit PPDU Type Field to distinguish TB from single user transmission
  UL/DL=1, PPDU Type = 0: Compressed (no RU Allocation, full (punctured) bandwidth)
  UL/DL=1, PPDU Type = 1: TB (no EHT-SIG)
In downlink transmission, we can have 1 bit PPDU Type Field to distinguish compressed EHT-SIG from non-compressed EHT-SIG
  UL/DL=0, PPDU Type = 0: Compressed (no RU Allocation , full (punctured) bandwidth)
  UL/DL=0, PPDU Type = 1: Non-compressed (RU Allocation subfield in common field)
No other PPDU type was identified (for release 2), but we can have one reserved bit which may be used as PPDU type
Proposal: 1 bit PPDU type and one bit reserved right after/before PPDU type

## Slide 8: PPDU Type Field (4/4)
We propose following PPDU types
  EHT MU PPDU with two modes
    Compressed mode:
      Non-OFDMA
      No RU Allocation subfield in the Common field of the EHT-SIG
    Non-compressed mode:
      OFDMA
      RU Allocation subfield(s) in the Common field of the EHT-SIG
  EHT TB PPDU

## Slide 9: Summary
In this contribution, we proposed followings
  BSS Color 6bits
  TXOP 7bits
  BW 3bits
  802.11be PPDU transmitted to a single user is using EHT MU PPDU compressed mode (there is no EHT SU PPDU)
  1 bit PPDU type and one bit reserved right after/before PPDU type
  PPDU types
    EHT MU PPDU with two modes
      Compressed mode:
        Non-OFDMA
        No RU Allocation subfield in the Common field of the EHT-SIG
      Non-compressed mode:
        OFDMA
        RU Allocation subfield(s) in the Common field of the EHT-SIG
    EHT TB PPDU

## Slide 10: Straw Poll #1
Do you support to modify SFD text as follows?
  The U-SIG field includes the following bits in Version-independent bits portion:
    BSS color, number of bits TBD 6 bits.
    TXOP duration, number of bits TBD 7 bits.

## Slide 11: Straw Poll #2
Do you support to modify SFD text as follows?
  The U-SIG shall contain Bandwidth Information, carried as a version independent field.
    This field may also convey some puncturing information.
    Number of bits for this field is TBD 3bits.

## Slide 12: Straw Poll #3
Do you support to modify SFD text as follows?
  The U-SIG shall contain a PPDU type field, carried as a version dependent field.
    Number of bits for this field is TBD 1 bit.
    One bit reserved field right after PPDU type.
    Note: the one bit reserved field may be used as PPDU type if 802.11be supports more than 2 PPDU types

## Slide 13: Straw Poll #4
Do you support to modify SFD text as follows?
  The format of the EHT MU PPDU A PPDU that is sent to multiple user is configured as follow:
    L-STF, L-LTF, L-SIG, RL-SIG, U-SIG, EHT-SIG, EHT-STF, EHT-LTF, DATA, PE
    Additional fields are TBD
    Note: This PPDU format is used for 802.11be PPDU transmitted to a single user or multiple users. There is no EHT SU PPDU.
    There are two modes in the EHT MU PPDU.
      Compressed mode:
        Non-OFDMA
        No RU Allocation subfield in the Common field of the EHT-SIG.
      Non-compressed mode:
        OFDMA
        RU Allocation subfield(s) in the Common field of the EHT-SIG.

## Slide 14: Straw Poll #5
Do you support to modify SFD text as follows?
  The format of the EHT TB PPDU is configured as follow:
    L-STF, L-LTF, L-SIG, RL-SIG, U-SIG, EHT-STF, EHT-LTF, DATA, PE
    Additional fields are TBD
    Note: This format is used for a transmission that is a response to a triggering frame from an AP.

## Slide 15: Reference
[1] 11-20/566r30, “Compendium of straw polls and potential changes to the Specification Framework Document”
[2] 11-20/0693r1, “Aggregated PPDU for Large BW”
[3] 11-20/0674r1, “Forward Compatible OFDMA”
[4] 11-20/0605r0, “Further Discussions on Efficient EHT Preamble”
[5] 11-20/0545r1, “Multi-segment EHT-SIG design discussion”

## Slide 16: Example of U-SIG Contents in MU PPDU
Field | Number of Bits | Note
PHY version identifier | 3 | 
UL/DL flag | 1 | 
BSS color | [6] | 
TXOP duration | [7] | 
Bandwidth | [3] | 
Puncturing Channel Information | [3-4] | 
PPDU Type | [1] | 
Reserved | [1] | 
EHT-SIG MCS [+ DCM] | [3] | Merge EHT-SIG MCS and EHT-SIG DCM (if supported)
Number Of EHE-SIG Symbols | [4] | 
GI+HE-LTF Size | [2] | 
Number of HE-LTF Symbols [And Midamble Periodicity] | [3] | 1/2/4/6/8/12/16 1/2/4 with Midamble two options (if Midamble is supported)
Pre-FEC Padding Factor | [2] | 
PE Disambiguity | [1] | 
LDPC Extra Symbol Segment | [1] | 
[Doppler] | [1] | If supported
[STBC] | [1] | If supported
[Spatial Reuse] | [4] | If supported
CRC | 4 | 
Tail | 6 |