## Slide 1: Consideration on 240MHz
Date: 2020-06-xx
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
11be approved to support 240/160+80 MHz transmission
In [1-3], how to support 240/160+80 MHz transmission was discussed
In [4], 240MHz channelization was proposed
In this contribution, we further discuss 240/160+80 MHz transmission by considering several issues such as channelization, BSS, PPDU, BW indication, and so on
  Whether to define 240/160+80 MHz mask PPDU needs to be decided
  Entries for the BW field need to be defined
We also discuss a unified sequence issue between 240/160+80 MHz and 320/160+160 MHz
  How to design phase rotation / EHT-STF / EHT-LTF sequence for 240/160+80 MHz needs to be determined by finalizing this issue

## Slide 3: Channelization (1/2)
Case 1: 240MHz channelization is defined
  For example, it can be defined as one of the options proposed in [4]
  In this case, 240/160+80 MHz BSS and mask PPDU* can be defined
  One of the entries in the BW field shall be used for 240/160+80 MHz mask PPDU indication
  This may need additional hardware implementations and requirements
  320MHz channels can be used for a wide bandwidth transmission instead of 240MHz ones
    Note that, in 6GHz, there are many 320MHz channels available for STAs operating with both standard and low power as shown in Appendix A
* We assume 240/160+80 MHz mask PPDU requires its own spectral mask different from that of 320/160+160 MHz mask PPDU

## Slide 4: Channelization (2/2)
Case 2: 240MHz channelization is not defined
  There are many 320MHz channels in 6GHz
    Note that all U-NII bands in 6GHz support low power indoor STAs as shown in Appendix A
  In this case, 240/160+80 MHz transmission can be considered as one of the 320/160+160 MHz mask PPDU transmission
    240/160+80 MHz transmission uses IFFT, spectral mask (+ spectral mask for punctured case), etc., defined for 320/160+160 MHz mask PPDU
    One 160MHz channel and one 80MHz channel can be used
    We can classify 320/160+160 MHz mask PPDU transmission into 320/160+160 MHz transmission and 240/160+80 MHz transmission
  Thus, we don’t need to define 240/160+80 MHz BSS and mask PPDU
  BW field doesn’t have to contain 240/160+80 MHz entry
    Even having said that, we can consider indicating 240/160+80 MHz transmission in the BW field for some benefits
    This issue is further discussed in the next several slides

## Slide 5: BW field (1/3)
For case 1, 240/160+80 MHz BSS / mask PPDU can be defined, and in this case, the BW field needs to contain 240/160+80 MHz entry
For case 2, we can consider two options as follows
  Option 1: no 240/160+80 MHz entry
    BW field entries are consistent with the bandwidth of the spectral mask
  Option 2: one 240/160+80 MHz entry
    The bandwidth of the spectral mask for 240/160+80 MHz and 320/160+160 MHz transmission is 320/160+160 MHz
Bit | Entry
000 | 20MHz
001 | 40MHz
010 | 80MHz
011 | 160/80+80MHz
100 | 320/160+160MHz
101 ~ 111 | Reserved
Bit | Entry
000 | 20MHz
001 | 40MHz
010 | 80MHz
011 | 160/80+80MHz
100 | 240/160+80MHz
101 | 320/160+160MHz
110 ~ 111 | Reserved
Option 1
Option 2
Same as spectral mask BW
Same as Spectral mask BW
320/160+160 MHz mask PPDU
100 indicates either 240/160+80 MHz or 320/160+160 MHz transmission

## Slide 6: BW field (2/3)
Since different features are defined in 240/160+80 MHz and 320/160+160 MHz transmission, option 2 may be efficient
  Possible puncturing patterns and MRU combinations have been separately designed
  Different signaling methods which depend on the transmission bandwidth may be desirable
    E.g., puncturing pattern indication for non-OFDMA PPDU
  Hence, it would be better to distinguish these two transmission bandwidths at the beginning of PPDU reception by using option 2
  We can also achieve signaling overhead reduction
    With option 1, since separate signaling may not be possible, there are total 23 puncturing patterns* for 320/160+160 MHz non-OFDMA PPDU as shown in Appendix B
    With option 2, there are 10 & 13 puncturing patterns* for 240/160+80 MHz & 320/160+160 MHz transmission, respectively, in non-OFDMA PPDU as shown in Appendix C
* Note that we basically assume static channel information (i.e., one 160MHz channel and one 80MHz channel information) used for 240/160+80MHz transmission is notified using MAC signaling, e.g., beacon frame

## Slide 7: BW field (3/3)
We need a clear definition of both 240/160+80 MHz and 320/160+160 MHz transmission in case 2
  Both are 320/160+160MHz mask PPDU transmission, i.e., the bandwidth of the spectral mask for both 240/160+80 MHz and 320/160+160 MHz transmission is 320/160+160 MHz
  240/160+80 MHz transmission is one of the 320/160+160 MHz mask PPDU transmission where one of the four 80MHz channels is punctured except for primary 80MHz
    For 240/160+80 MHz transmission, all puncturing patterns and multiple RU combinations defined in 240/160+80 MHz are allowed to be applied to 320/160+160 MHz mask PPDU on top of one 80MHz channel puncturing
  320/160+160 MHz transmission is the other 320/160+160 MHz mask PPDU transmission
    For 320/160+160 MHz transmission, all puncturing patterns and multiple RU combinations defined in 320/160+160 MHz are allowed to be applied to 320/160+160 MHz mask PPDU

## Slide 8: Unified / Separate Sequence in 240/160+80 MHz and 320/160+160 MHz (1/2)
Unified sequence means only one sequence is defined for 240/160+80 MHz and 320/160+160 MHz transmission
  [S1 S2 S3 S4]
    Each ‘S’ is applied to each 80MHz segment in 320/160+160 MHz transmission
  For 240/160+80 MHz transmission, one ‘S’ corresponding to the punctured 80MHz channel is punctured
    E.g., if the second 80MHz channel is punctured, [S1 0 S3 S4] is used
Separate sequence means two different sequences are defined for 240/160+80 MHz and 320/160+160 MHz transmission, respectively
  [S1 S2 S3 S4] for 320/160+160 MHz
  [S5 S6 S7] for 240/160+80 MHz
    Each ‘S’ is applied to each 80MHz segment except for the punctured one

## Slide 9: Unified / Separate Sequence in 240/160+80 MHz and 320/160+160 MHz (2/2)
In case 1, separate sequences (phase rotation/STF/LTF/etc.) may be required
For option 1 in case 2, defining a unified sequence may be valid
  It may be hard for receivers to identify the transmission bandwidth when 320/160+160 MHz PPDU is received
    Especially for 320/160+160 MHz OFDMA PPDU, STAs may need to decode all content channels in EHT-SIG in order to obtain transmission bandwidth information
For option 2 in case 2, defining separate sequences may be better
  It is possible for receiver STAs to identify the transmission bandwidth early
  Separate sequences can further improve PAPR
    Note that, the proposed unified EHT-LTF sequence in [5] causes high PAPR

## Slide 10: Conclusion
First, we have discussed 240MHz channelization
  Case 1: 240MHz channelization is defined
    Need more hardware implementations
  Case 2: 240MHz channelization is not defined
    240/160+80 MHz transmission is one of the 320/160+160 MHz mask PPDU transmission
Then, we have proposed two options for the BW field given Case 2
  Option 1: no 240/160+80 MHz entry
    All entries are consistent with the bandwidth of the spectral mask
    Hard to identify transmission bandwidth early, a bit large overhead
  Option 2: one 240/160+80 MHz entry
    Not consistent with the bandwidth of the spectral mask
    Possible to identify transmission bandwidth early, relatively small overhead
Finally, we have briefly discussed a unified / separate sequence between 240/160+80 MHz and 320/160+160 MHz
  Unified sequence: Implementation-friendly, applicable to both options
  Separate sequence: Better PAPR, more proper for option 2

## Slide 11: Straw Poll #1
Do you agree not to define 240MHz channelization?
  It is not intended for SFD
Y/N/A: //

## Slide 12: Straw Poll #2
Do you agree to add the following text to TGbe SFD?
  240/160+80 MHz transmission is one of the 320/160+160 MHz mask PPDU transmission where one of the four 80MHz channels is punctured except for primary 80MHz
    For 240/160+80 MHz transmission, all puncturing patterns and multiple RU combinations defined in 240/160+80 MHz are allowed to be applied to 320/160+160 MHz mask PPDU on top of one 80MHz channel puncturing
  320/160+160 MHz transmission is the other 320/160+160 MHz mask PPDU transmission
    For 320/160+160 MHz transmission, all puncturing patterns and multiple RU combinations defined in 320/160+160 MHz are allowed to be applied to 320/160+160 MHz mask PPDU
Y/N/A: //

## Slide 13: Straw Poll #2a
Do you agree to add the following text to TGbe SFD?
  240/160+80MHz transmission is subjected to 320/160+160MHz PPDU mask plus additional puncturing mask
  320/160+160MHz transmission is subjected to 320/160+160MHz PPDU mask, additional puncturing mask can be applied according to the puncturing patterns and MRUs
  The masks TBD
Y/N/A: 37/3/14

## Slide 14: Straw Poll #3
Which option do you agree with for the BW field?
  Option 1: no 240/160+80MHz entry
  Option 2: one 240/160+80MHz entry
  Note: It is not intended for SFD
Op1/Op2/A: ///

## Slide 15: Straw Poll #4
Do you agree to add the following text to TGbe SFD?
  BW field: 3 bits
    Note: all entries are consistent with the bandwidth of the spectral mask and 320/160+160 MHz includes 240/160+80 MHz and 320/160+160 MHz transmission
Y/N/A: //
Bit | Entry
000 | 20MHz
001 | 40MHz
010 | 80MHz
011 | 160/80+80MHz
100 | 320/160+160MHz
101 ~ 111 | Reserved

## Slide 16: Straw Poll #5
Do you agree to add the following text to TGbe SFD?
  BW field: 3 bits
    Note: the bandwidth of the spectral mask for 240/160+80 MHz is 320/160+160 MHz and the other entries are consistent with the bandwidth of the spectral mask
Y/N/A: //
Bit | Entry
000 | 20MHz
001 | 40MHz
010 | 80MHz
011 | 160/80+80MHz
100 | 240/160+80MHz
101 | 320/160+160MHz
110 ~ 111 | Reserved

## Slide 17: Straw Poll #6
Do you agree that a separate phase rotation / EHT-STF / EHT-LTF sequence is defined in each 240/160+80 MHz and 320/160+160 MHz transmission?
  It is not intended for SFD
Y/N/A: //

## Slide 18: Straw Poll #7
Do you agree to add the following text to TGbe SFD?
  240/160+80MHz transmission is obtained from the 320/160+160MHz PPDU rather than from 240/160+80MHz PPDU where one of the four 80MHz channels is punctured except for primary 80MHz
Y/N/A: //

## Slide 19: References
[1] 802-11-19/1521r2 Further Thoughts on 11be Tone Plan
[2] 802-11-19/1889r2 Discussion on 240MHz Bandwidth
[3] 802.11-20/0022r1 Consideration on 240MHz and Preamble Puncturing
[4] 802.11-20/0479r0 240MHz Channelization
[5] 802.11-20/0825r1 EHT-LTF Sequences in New Tone Plan

## Slide 20: Appendix A
6GHz regulation

## Slide 21: Appendix B
Puncturing patterns in 320/160+160 MHz PPDU for option 1
  1 case for 4x996 in 320/160+160 MHz transmission
    [oooo oooo oooo oooo]
  4 cases for 3x996 in 320/160+160 MHz transmission
    [xxxx oooo oooo oooo], [oooo xxxx oooo oooo], [oooo oooo xxxx oooo], [oooo oooo oooo xxxx]
  8 cases for 3x996+484 in 320/160+160 MHz transmission
    [xxoo oooo oooo oooo], [ooxx oooo oooo oooo], [oooo xxoo oooo oooo], [oooo ooxx oooo oooo],
    [oooo oooo xxoo oooo], [oooo oooo ooxx oooo], [oooo oooo oooo xxoo], [oooo oooo oooo ooxx]
  1 case for 3x996 in 240/160+80 MHz transmission
    [oooo oooo oooo]
  3 cases for 2x996 in 240/160+80 MHz transmission
    [xxxx oooo oooo], [oooo xxxx oooo], [oooo oooo xxxx]
  6 cases for 2x996+484 in 240/160+80 MHz transmission
    [xxoo oooo oooo], [ooxx oooo oooo], [oooo xxoo oooo], [oooo ooxx oooo],
    [oooo oooo xxoo], [oooo oooo ooxx]
o: non-punctured 20MHz channel
x: punctured 20MHz channel

## Slide 22: Appendix C
Puncturing patterns for option 2
  240/160+80 MHz transmission
    [oooo oooo oooo], [xxxx oooo oooo], [oooo xxxx oooo], [oooo oooo xxxx],
    [xxoo oooo oooo], [ooxx oooo oooo], [oooo xxoo oooo], [oooo ooxx oooo],
    [oooo oooo xxoo], [oooo oooo ooxx]
  320/160+160 MHz transmission
    [oooo oooo oooo oooo], [xxxx oooo oooo oooo], [oooo xxxx oooo oooo],
    [oooo oooo xxxx oooo], [oooo oooo oooo xxxx], [xxoo oooo oooo oooo],
    [ooxx oooo oooo oooo], [oooo xxoo oooo oooo], [oooo ooxx oooo oooo],
    [oooo oooo xxoo oooo], [oooo oooo ooxx oooo], [oooo oooo oooo xxoo],
    [oooo oooo oooo ooxx]