## Slide 1: Bandwidth Indication for EHT PPDU
Date: 2020-06-28
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Mengshi Hu | Huawei |  |  | 
Ming Gan | Huawei |  |  | 

## Slide 2: Introduction and Recap
We have the following passed SPs/Motions regarding Bandwidth:
  The U-SIG shall contain Bandwidth Information, carried as a version independent field.
    This field may also convey some puncturing information.
    Number of bits for this field is TBD.
    [Motion 88, [14] and [36]]
  802.11be supports that U-SIG in each 80 MHz shall carry puncturing channel info for at least the specific 80 MHz where it is transmitted.
    Note: Within each 80 MHz segment, U-SIG is duplicated in every non-punctured 20 MHz.
    Whether BW/Puncturing info can be different for different 80 MHz is TBD.
    Whether BW and puncturing info in U-SIG are carried as a combined or a separate field is TBD.
    [Motion 111, #SP0611-10, [7] and [37]]
  802.11be supports BW field which does not include puncturing information.
    [Motion 112, #SP29, [7] and [38]]

## Slide 3: BW Indication in U-SIG
We consider the following two options regarding the BW indication in U-SIG. :
  Opt1: BW field in U-SIG shall be the same across different segments. The BW field indicates the PPDU BW.
    Pro: similar concept as 11n/ac/ax. BW field reflects the PPDU BW.
    Con: Different segments contain the same number of RU allocation subfields, may have larger overhead.
  Opt 2: BW field in U-SIG can be different across different segments. The BW field indicates the channel bandwidth which covers the assigned RUs of the STAs parking in the corresponding segments of U-SIG.
    Pro: each segment can have the minimum required number of RU allocation subfields, smaller overhead.
    Con: different concept as 11n/ac/ax. BW field sometimes doesn’t reflect the PPDU BW.

## Slide 4: BW Indication in U-SIG
Two options regarding BW indication are discussed:
  Opt 1: BW field in U-SIG shall be the same across different segments. The BW field indicates the PPDU BW.
  Opt 2: BW field in U-SIG can be different across different segments. The BW field indicates the channel bandwidth which covers the assigned RUs of the STAs parking in the corresponding segments of U-SIG.
Opt2 is slightly preferred for OFDMA transmission.
  More flexible regarding number of RU allocation subfields, compression mode/non-compression mode
Opt 1 is preferred for non-OFDMA transmission.
  Same RU/aggregated RUs for all the STAs, which make Opt 2 and Opt1 the same.
  The only gap is that if no target parking STAs on some of the segment, suggest to still indicate the PPDU BW.

## Slide 5: Summary
Two options of BW indication are proposed.
  Opt 1: BW field in U-SIG shall be the same across different segments. The BW field indicates the PPDU BW.
  Opt 2: BW field in U-SIG can be different across different segments. The BW field indicates the channel bandwidth which covers the assigned RUs of the STAs parking in the corresponding segments of U-SIG.
    Opt 2 is a superset of Opt 1
Opt2 is slightly preferred for OFDMA transmission.
Opt 1 is preferred for non-OFDMA transmission.

## Slide 6: Straw Poll #1
Which option do you prefer for bandwidth indication for OFDMA transmission in an EHT non-TB PPDU?
  Opt 1: BW field in U-SIG shall be the same across different segments. The BW field indicates the PPDU BW.
  Opt 2: BW field in U-SIG can be different across different segments. The BW field indicates the channel bandwidth which covers the assigned RUs of the STAs parking in the corresponding segments of U-SIG.
  Neither
  Abstain
  Note: not for SFD

## Slide 7: Straw Poll #2
Which option do you prefer for bandwidth indication for non-OFDMA transmission in an EHT non-TB PPDU?
  Opt 1: BW field in U-SIG shall be the same across different segments. The BW field indicates the PPDU BW.
  Opt 2: BW field in U-SIG can be different across different segments. The BW field indicates the channel bandwidth which covers the assigned RUs of the STAs parking in the corresponding segments of U-SIG.
  Neither
  Abstain
  Note: not for SFD

## Slide 8: Straw Poll #3
Do you agree to add the following text in the TGbe SFD:
  In EHT non-TB PPDU, for OFDMA transmission, BW field in U-SIG might be different across different segments. The BW field indicates the channel bandwidth which covers the assigned RUs of the STAs parking in the corresponding segments of U-SIG.

## Slide 9: Straw Poll #4
Do you agree to add the following text in the TGbe SFD:
  In EHT non-TB PPDU, for non-OFDMA transmission, BW field in U-SIG shall be the same across different segments. The BW field indicates the PPDU BW.

## Slide 10: Straw Poll #5
Do you agree that N RU allocation subfields are present in an EHT-SIG content channel in an EHT PPDU sent to multiple users?
  Where, N is the number of RU Allocation subfield in Common field of EHT-SIG content channel.
  N = 4 if the BW field in U-SIG indicates 160MHz/80+80MHz channel bandwidth.
  N = 6 if the BW field in U-SIG indicates 240MHz/160+80MHz channel bandwidth.
  N = 8 if the BW field in U-SIG indicates 320MHz/160+160MHz channel bandwidth.
  Compressed modes are TBD.

## Slide 11
https://mentor.ieee.org/802.11/dcn/20/11-20-0566-34-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document.docx, Edward Au, Huawei
References