## Slide 1: 1x EHT-LTF Sequences Design
Date: 2020-06-30
Authors:
Name | Affiliations | Address | Phone | email
Dandan Liang | Huawei Technologies Co., Ltd | Huawei Base, Bantian, Shenzhen |  | Dandan.liang@huawei.com
Chenchen Liu |  |  |  | 
Ming Gan |  |  |  | 
Yan Xin |  |  |  | 
Wei Lin |  |  |  | 

## Slide 2: Abstract
This contribution proposes the 1x EHT-LTF sequences for 320/160+160MHz.

## Slide 3: Introduction
In [1], the 320MHz/160MHz+160MHz EHT-LTF sequences has been proposed without considering the punctured 240MHz/160MHz+80MHz transmission.
In this contribution, the 320MHz/160MHz+160MHz 1x EHT-LTF sequences are proposed for both with and without considering the punctured 240MHz/160MHz+80MHz transmission.

## Slide 4: Introduction
BW | 1x EHT-LTF Full bandwidth & MRU & Preamble Puncturing Patterns |  |  |  |  | Note
P1: (without punctured 240MHz transmission) [1] | Case1 : 320MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1] Case2：280MHz [0 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1] Case3：280MHz [1 1 0 0 1 1 1 1 1 1 1 1 1 1 1 1] Case4：280MHz [1 1 1 1 0 0 1 1 1 1 1 1 1 1 1 1] Case5：280MHz [1 1 1 1 1 1 0 0 1 1 1 1 1 1 1 1] Case6：280MHz [1 1 1 1 1 1 1 1 0 0 1 1 1 1 1 1] Case7：280MHz [1 1 1 1 1 1 1 1 1 1 0 0 1 1 1 1] Case8：280MHz [1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 1] Case9：280MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0] Case10: 240MHz [1 1 1 1 0 0 0 0 1 1 1 1 1 1 1 1] Case11: 240MHz [1 1 1 1 1 1 1 1 0 0 0 0 1 1 1 1] Case12: 240MHz [1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0] Case13: 240MHz [0 0 0 0 1 1 1 1 1 1 1 1 1 1 1 1]. |  |  |  |  | “1” stands for non-punctured 20MHz; “0” stands for punctured 20MHz.
P2: (with punctured 240MHz transmission) | Case1 : 320MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1], Case2：280MHz [0 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1], Case3：280MHz [1 1 0 0 1 1 1 1 1 1 1 1 1 1 1 1], Case4：280MHz [1 1 1 1 0 0 1 1 1 1 1 1 1 1 1 1], Case5：280MHz [1 1 1 1 1 1 0 0 1 1 1 1 1 1 1 1], Case6：280MHz [1 1 1 1 1 1 1 1 0 0 1 1 1 1 1 1], Case7：280MHz [1 1 1 1 1 1 1 1 1 1 0 0 1 1 1 1], Case8：280MHz [1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 1], Case9：280MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0], Case10: 240MHz [1 1 1 1 0 0 0 0 1 1 1 1 1 1 1 1], Case11: 240MHz [1 1 1 1 1 1 1 1 0 0 0 0 1 1 1 1], Case12: 240MHz [1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0], Case13: 240MHz [0 0 0 0 1 1 1 1 1 1 1 1 1 1 1 1]. | [based on punctured Case10]: Case14: [0 0 1 1 0 0 0 0 1 1 1 1 1 1 1 1], Case15: [1 1 0 0 0 0 0 0 1 1 1 1 1 1 1 1], Case16: [1 1 1 1 0 0 0 0 0 0 1 1 1 1 1 1], Case17: [1 1 1 1 0 0 0 0 1 1 0 0 1 1 1 1], Case18: [1 1 1 1 0 0 0 0 1 1 1 1 0 0 1 1], Case 19: [1 1 1 1 0 0 0 0 1 1 1 1 1 1 0 0], Case 20: [0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1], Case 21: [1 1 1 1 0 0 0 0 0 0 0 0 1 1 1 1], Case 22: [1 1 1 1 0 0 0 0 1 1 1 1 0 0 0 0], | [based on punctured Case11]: Case23: [0 0 1 1 1 1 1 1 0 0 0 0 1 1 1 1], Case24: [1 1 0 0 1 1 1 1 0 0 0 0 1 1 1 1], Case25: [1 1 1 1 0 0 1 1 0 0 0 0 1 1 1 1], Case26: [1 1 1 1 1 1 0 0 0 0 0 0 1 1 1 1], Case27: [1 1 1 1 1 1 1 1 0 0 0 0 0 0 1 1], Case28: [1 1 1 1 1 1 1 1 0 0 0 0 1 1 0 0], Case29: [0 0 0 0 1 1 1 1 0 0 0 0 1 1 1 1], Case30: [1 1 1 1 0 0 0 0 0 0 0 0 1 1 1 1], Case31: [1 1 1 1 1 1 1 1 0 0 0 0 0 0 0 0], | [based on punctured Case12]: Case32: [0 0 1 1 1 1 1 1 1 1 1 1 0 0 0 0], Case33: [1 1 0 0 1 1 1 1 1 1 1 1 0 0 0 0], Case34: [1 1 1 1 0 0 1 1 1 1 1 1 0 0 0 0], Case35: [1 1 1 1 1 1 0 0 1 1 1 1 0 0 0 0], Case36: [1 1 1 1 1 1 1 1 0 0 1 1 0 0 0 0], Case37: [1 1 1 1 1 1 1 1 1 1 0 0 0 0 0 0], Case38: [0 0 0 0 1 1 1 1 1 1 1 1 0 0 0 0], Case39: [1 1 1 1 0 0 0 0 1 1 1 1 0 0 0 0], Case40: [1 1 1 1 1 1 1 1 0 0 0 0 0 0 0 0], | [based on punctured Case13]: Case41: [0 0 0 0 0 0 1 1 1 1 1 1 1 1 1 1], Case42: [0 0 0 0 1 1 0 0 1 1 1 1 1 1 1 1], Case43: [0 0 0 0 1 1 1 1 0 0 1 1 1 1 1 1], Case44: [0 0 0 0 1 1 1 1 1 1 0 0 1 1 1 1], Case45: [0 0 0 0 1 1 1 1 1 1 1 1 0 0 1 1], Case46: [0 0 0 0 1 1 1 1 1 1 1 1 1 1 0 0], Case47: [0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1], Case48: [0 0 0 0 1 1 1 1 0 0 0 0 1 1 1 1], Case49: [0 0 0 0 1 1 1 1 1 1 1 1 0 0 0 0]. | 

## Slide 5: Design Methods[3-4]
Option 1: Based on 80MHz EHT-LTF:
Repeating 11ax 80MHz LTF sequences and apply the coefficient value on each 80MHz [1].
Option 2: Based on partial of 80MHz EHT-LTF.
For 1x, repeating 11ax 80MHz LTF sequences and apply the coefficient value on the left - right part of 80MHz LTF [1,4].

## Slide 6: Sequences Design Considerations
Optimized the PAPR of all RU or aggregated RU size: page 4 & 5.
Single stream pilot impact [5]:
  Pilot position: passed SPs [2]
  P matrices:

## Slide 7: Sequences Design Considerations
RU type | RU index and subcarrier range for3 20MHz |  |  |  |  |  |  | 
484-tone RU | RU1 [-2036:-1795, -1789:-1548] | RU2 [-1524:-1283, -1277:-1036] | RU3 [-1012:-771, -765:-524] | RU4 [-500:-259, -253:-12] | RU5 [12:253, 259:500] | RU6 [524:765, 771:1012] | RU7 [1036:1277, 1283: 1524] | RU8 [1548:1789, 1795: 2036]
996-tone RU | RU1 [-2036:-1539, -1533:-1036] | RU2 [-1012:-514, -508:-12] | RU3 [12:508, 514:1012] | RU4 [1036:1533, 1539:2036] |  |  |  | 
RU type | Pilot indices for 320MHz
484-tone RU | {-2030 -2004 -1962 -1936 -1896 -1870 -1828 -1802 -1782 -1756 -1714 -1688 -1648 -1622 -1580 -1554}, {-1518 -1492 -1450 -1424 -1384 -1358 -1316 -1290 -1270 -1244 -1202 -1176 -1136 -1110 -1068 -1042}, {-1006 -980 -938 -912 -872 -846 -804 -778 -758 -732 -690 -664 -624 -598 -556 -530}, {-494 -468 -426 -400 -360 -334 -292 -266 -246 -220 -178 -152 -112 -86 -44 -18}, {18 44 86 112 152 178 220 246 266 292 334 360 400 426 468 494}, {530 556 598 624 664 690 732 758 778 804 846 872 912 938 980 1006}, {1042 1068 1110 1136 1176 1202 1244 1270 1290 1316 1358 1384 1424 1450 1492 1518}, {1554 1580 1622 1648 1688 1714 1756 1782 1802 1828 1870 1896 1936 1962 2004 2030}
996-tone RU | {-2004 -1936 -1870 -1802 -1756 -1688 -1622 -1554 -1518 -1450 -1384 -1316 -1270 -1202 -1136 -1068}， {-980 -912 -846 -778 -732 -664 -598 -530 -494 -426 -360 -292 -246 -178 -112 -44}， {44 112 178 246 292 360 426 494 530 598 664 732 778 846 912 980}， {1068 1136 1202 1270 1316 1384 1450 1518 1554 1622 1688 1756 1802 1870 1936 2004}
  For each 80MHz segment in 320MHz transmission: the 80MHz OFDMA tone plan is used for the punctured and OFDMA scenarios, while the 996 RU tone plan is used for the non-OFDMA and non-punctured scenarios [6].
    For 3x996+484 RU combinations, the 996 RU uses 996 RU tone plan and the 484 RU uses 484 RU tone plan, respectively.

## Slide 8: 320MHz 1x EHT-LTF
Option 1:
P1:320MHz 1x EHT-LTF-2036,2036 = [HE-LTF80MHz_1x 023 HE-LTF80MHz_1x 023 (-1)* HE-LTF80MHz_1x 023 (-1)*HE-LTF80MHz_1x];
Coefficient values = [1 1 -1 -1]
Option 2:
P1: 320MHz 1x EHT-LTF-2036,2036 = [HE-LTF80MHz_left_1x 0 (-1)* HE-LTF80MHz_right_1x 023 HE-LTF80MHz_left_1x 0 HE-LTF80MHz_right_1x 023 HE-LTF80MHz_left_1x 0 HE-LTF80MHz_right_1x 023 (-1)*HE-LTF80MHz_left_1x 0 (-1)* HE-LTF80MHz_right_1x];
Coefficient values = [1 -1 1 1 1 1 -1 -1]
P2:320MHz 1x EHT-LTF-2036,2036 = [HE-LTF80MHz_1x 023 HE-LTF80MHz_1x 023 (-1)* HE-LTF80MHz_1x 023 (-1)*HE-LTF80MHz_1x];
Coefficient values = [1 1 -1 -1]
P2: 320MHz 1x EHT-LTF-2036,2036 = [HE-LTF80MHz_left_1x 0 HE-LTF80MHz_right_1x 023 HE-LTF80MHz_left_1x 0 HE-LTF80MHz_right_1x 023 (-1)* HE-LTF80MHz_left_1x 0 (-1)* HE-LTF80MHz_right_1x 023 (-1)*HE-LTF80MHz_left_1x 0 (-1)* HE-LTF80MHz_right_1x];
Coefficient values = [1 1 1 1 -1 -1 -1 -1]

## Slide 9: P1: 320MHz 1x EHT-LTF [1]
Patterns | Option 1: | Option 2:
Case1：320MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1] | 8.9944 8.5362 | 7.2138 6.6917
Case2：280MHz [0 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1] | 8.0424 7.5917 | 8.3602 7.6754
Case3：280MHz [1 1 0 0 1 1 1 1 1 1 1 1 1 1 1 1] | 8.2230 7.8690 | 7.1859 6.8401
Case4：280MHz [1 1 1 1 0 0 1 1 1 1 1 1 1 1 1 1] | 8.8837 8.5916 | 8.0696 6.4414
Case5：280MHz [1 1 1 1 1 1 0 0 1 1 1 1 1 1 1 1] | 8.9778 8.3838 | 6.7074 5.857
Case6：280MHz [1 1 1 1 1 1 1 1 0 0 1 1 1 1 1 1] | 9.0837 8.2841 | 8.1376 7.4562
Case7：280MHz [1 1 1 1 1 1 1 1 1 1 0 0 1 1 1 1] | 8.9009 8.5967 | 6.7785 6.0188
Case8：280MHz [1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 1] | 8.2149 7.6949 | 7.8276 5.9677
Case9：280MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0] | 8.2885 7.8110 | 7.3592 6.5960
Case10: 240MHz [1 1 1 1 0 0 0 0 1 1 1 1 1 1 1 1] | 8.9613 8.5031 | 8.1866 6.7521
Case11: 240MHz [1 1 1 1 1 1 1 1 0 0 0 0 1 1 1 1] | 8.9613 8.5031 | 7.4535 7.0361
Case12: 240MHz [1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0] | 7.5154 7.0794 | 8.1341 6.8461
Case13: 240MHz [0 0 0 0 1 1 1 1 1 1 1 1 1 1 1 1] | 7.5154 7.0794 | 7.5154 7.0794
Worst PAPR [dB]: | 9.0837 [Case 6] | 8.3602 [Case 2]
Note: In this contribution, the first line value of each sub-block is the PAPR values for the EHT-LTF tones expect pilot tones multiplied by elements of P matrix(up to 16x16), while the second line value of each block is the single stream PAPR values. The Worst PAPR is the max PAPR for the EHT-LTF tones except pilot tones multiplied by elements of P matrix.

## Slide 10: P2: 320MHz 1x EHT-LTF
Patterns | Option 1: PAPR [dB] | Option 2: PAPR [dB]
Case1：320MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1] | 8.9944 | 8.9944
Case2：280MHz [0 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1] | 8.0424 | 8.0424
Case3：280MHz [1 1 0 0 1 1 1 1 1 1 1 1 1 1 1 1] | 8.2230 | 8.2230
Case4：280MHz [1 1 1 1 0 0 1 1 1 1 1 1 1 1 1 1] | 8.8837 | 8.8837
Case5：280MHz [1 1 1 1 1 1 0 0 1 1 1 1 1 1 1 1] | 8.9778 | 8.9778
Case6：280MHz [1 1 1 1 1 1 1 1 0 0 1 1 1 1 1 1] | 9.0837 | 9.0837
Case7：280MHz [1 1 1 1 1 1 1 1 1 1 0 0 1 1 1 1] | 8.9009 | 8.9009
Case8：280MHz [1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 1] | 8.2149 | 8.2149
Case9：280MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0] | 8.2885 | 8.2885
Case10: 240MHz [1 1 1 1 0 0 0 0 1 1 1 1 1 1 1 1] | 8.9613 | 8.9613
Case11: 240MHz [1 1 1 1 1 1 1 1 0 0 0 0 1 1 1 1] | 8.9613 | 8.9613
Case12: 240MHz [1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0] | 7.5154 | 7.5154
Case13: 240MHz [0 0 0 0 1 1 1 1 1 1 1 1 1 1 1 1] | 7.5154 | 7.5154
Worst PAPR [dB]: | 9.0837 [Case 6] | 9.0837 [Case 6]
Note: The PAPR value is for the EHT-LTF tones expect pilot tones multiplied by elements of P matrix(up to 16x16). The Worst PAPR is the max PAPR for the EHT-LTF tones except pilot tones multiplied by elements of P matrix.

## Slide 11: P2: 320MHz 1x EHT-LTF
Patterns | Option 1: PAPR [dB] | Option 2: PAPR [dB]
Case14: [0 0 1 1 0 0 0 0 1 1 1 1 1 1 1 1] | 8.2709 | 8.2709
Case15: [1 1 0 0 0 0 0 0 1 1 1 1 1 1 1 1] | 8.3622 | 8.3622
Case16: [1 1 1 1 0 0 0 0 0 0 1 1 1 1 1 1] | 8.7755 | 8.7755
Case17: [1 1 1 1 0 0 0 0 1 1 0 0 1 1 1 1] | 8.5458 | 8.5458
Case18: [1 1 1 1 0 0 0 0 1 1 1 1 0 0 1 1] | 8.6197 | 8.6197
Case 19: [1 1 1 1 0 0 0 0 1 1 1 1 1 1 0 0] | 8.5826 | 8.5826
Case 20: [0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1] | 8.0064 | 8.0064
Case 21: [1 1 1 1 0 0 0 0 0 0 0 0 1 1 1 1] | 8.1480 | 8.1480
Case 22: [1 1 1 1 0 0 0 0 1 1 1 1 0 0 0 0] | 8.3072 | 8.3072
Patterns | Option 1: PAPR [dB] | Option 2: PAPR [dB]
Case23: [0 0 1 1 1 1 1 1 0 0 0 0 1 1 1 1] | 8.5199 | 8.5199
Case24: [1 1 0 0 1 1 1 1 0 0 0 0 1 1 1 1] | 8.4525 | 8.4525
Case25: [1 1 1 1 0 0 1 1 0 0 0 0 1 1 1 1] | 8.7406 | 8.7406
Case26: [1 1 1 1 1 1 0 0 0 0 0 0 1 1 1 1] | 8.6802 | 8.6802
Case27: [1 1 1 1 1 1 1 1 0 0 0 0 0 0 1 1] | 8.1251 | 8.1251
Case28: [1 1 1 1 1 1 1 1 0 0 0 0 1 1 0 0] | 8.2758 | 8.2758
Case29: [0 0 0 0 1 1 1 1 0 0 0 0 1 1 1 1] | 8.3072 | 8.3072
Case30: [1 1 1 1 0 0 0 0 0 0 0 0 1 1 1 1] | 8.1480 | 8.1480
Case31: [1 1 1 1 1 1 1 1 0 0 0 0 0 0 0 0] | 8.0064 | 8.0064
Patterns | Option 1: PAPR [dB] | Option 2: PAPR [dB]
Case32: [0 0 1 1 1 1 1 1 1 1 1 1 0 0 0 0] | 7.1151 | 7.1151
Case33: [1 1 0 0 1 1 1 1 1 1 1 1 0 0 0 0] | 7.2152 | 7.2152
Case34: [1 1 1 1 0 0 1 1 1 1 1 1 0 0 0 0] | 8.2661 | 8.2661
Case35: [1 1 1 1 1 1 0 0 1 1 1 1 0 0 0 0] | 7.9758 | 7.9758
Case36: [1 1 1 1 1 1 1 1 0 0 1 1 0 0 0 0] | 7.2433 | 7.2433
Case37: [1 1 1 1 1 1 1 1 1 1 0 0 0 0 0 0] | 7.0408 | 7.0408
Case38: [0 0 0 0 1 1 1 1 1 1 1 1 0 0 0 0] | 8.1480 | 8.1480
Case39: [1 1 1 1 0 0 0 0 1 1 1 1 0 0 0 0] | 8.3072 | 8.3072
Case40: [1 1 1 1 1 1 1 1 0 0 0 0 0 0 0 0] | 8.0064 | 8.0064
Patterns | Option 1: PAPR [dB] | Option 2: PAPR [dB]
Case41: [0 0 0 0 0 0 1 1 1 1 1 1 1 1 1 1] | 7.2055 | 7.2055
Case42: [0 0 0 0 1 1 0 0 1 1 1 1 1 1 1 1] | 6.9584 | 6.9584
Case43: [0 0 0 0 1 1 1 1 0 0 1 1 1 1 1 1] | 8.1436 | 8.1436
Case44: [0 0 0 0 1 1 1 1 1 1 0 0 1 1 1 1] | 8.0593 | 8.0593
Case45: [0 0 0 0 1 1 1 1 1 1 1 1 0 0 1 1] | 7.5331 | 7.5331
Case46: [0 0 0 0 1 1 1 1 1 1 1 1 1 1 0 0] | 6.9584 | 6.9584
Case47: [0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1] | 8.0064 | 8.0064
Case48: [0 0 0 0 1 1 1 1 0 0 0 0 1 1 1 1] | 8.3072 | 8.3072
Case49: [0 0 0 0 1 1 1 1 1 1 1 1 0 0 0 0] | 8.1480 | 8.1480
Worst PAPR [dB]: | 9.0837 [Case 6] | 9.0837 [Case 6]

## Slide 12: Conclusion
In this contribution, 1x EHT-LTF sequences in
320MHz/160MHz+160MHz transmission are proposed.

## Slide 13: Reference
[1]Dandan Liang, et al, <EHT-LTFs Sequences Design>, IEEE 802.11-20/0926r0
[2]Edward Au, <IEEE P802.11 Wireless LANs>, IEEE 802.11-20/0566r29
[3] <802.11ax Draft>, D6.0.
[4] Jinyoung Chun, et al, <EHT-LTF sequences in new tone plan>, IEEE 802.11-20/825r1
[5] Le Liu, et al, <HE-LTF Sequence Design>, IEEE 802.11-15/1334
[6] Ron Porat, et al, <80MHz OFDMA Tone Plan>, IEEE 802.11-20/0666r2

## Slide 14: Straw Poll 1
Do you support to add to SFD: 320MHz/160MHz+160MHz 1x EHT-LTF sequence:
Option 1: 320MHz 1x EHT-LTF-2036,2036 = [HE-LTF80MHz_1x 023 HE-LTF80MHz_1x 023 (-1)* HE-LTF80MHz_1x 023 (-1)*HE-LTF80MHz_1x];
Coefficient values = [1 1 -1 -1]
Option 2: 320MHz 1x EHT-LTF-2036,2036 = [HE-LTF80MHz_left_1x 0 (-1)* HE-LTF80MHz_right_1x 023 HE-LTF80MHz_left_1x 0 HE-LTF80MHz_right_1x 023 HE-LTF80MHz_left_1x 0 HE-LTF80MHz_right_1x 023 (-1)*HE-LTF80MHz_left_1x 0 (-1)* HE-LTF80MHz_right_1x];
Coefficient values = [1 -1 1 1 1 1 -1 -1]
Option 3: 320MHz 1x EHT-LTF-2036,2036 = [HE-LTF80MHz_left_1x 0 HE-LTF80MHz_right_1x 023 HE-LTF80MHz_left_1x 0 HE-LTF80MHz_right_1x 023 (-1)* HE-LTF80MHz_left_1x 0 (-1)* HE-LTF80MHz_right_1x 023 (-1)*HE-LTF80MHz_left_1x 0 (-1)* HE-LTF80MHz_right_1x];
Coefficient values = [1 1 1 1 -1 -1 -1 -1]

## Slide 15: Appendix
 | 320MHz |  |  |  |  | 
Patterns | P1 & Option 1: PAPR [dB] |  |  | P1 & Option 2: PAPR [dB] |  | 
 | 1ss | P matrices with +1, -1 | P matrices with +1,-1, w | 1ss | P matrices with +1, -1 | P matrices with +1,-1, w
Case1：320MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1] | 8.5362 | 8.9944 | 8.9944 | 6.6917 | 7.0772 | 7.2138
Case2：280MHz [0 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1] | 7.5917 | 7.8585 | 8.0424 | 7.6754 | 8.085 | 8.3602
Case3：280MHz [1 1 0 0 1 1 1 1 1 1 1 1 1 1 1 1] | 7.869 | 8.0466 | 8.2230 | 6.8401 | 7.095 | 7.1859
Case4：280MHz [1 1 1 1 0 0 1 1 1 1 1 1 1 1 1 1] | 8.5916 | 8.769 | 8.8837 | 6.4414 | 8.0696 | 8.0696
Case5：280MHz [1 1 1 1 1 1 0 0 1 1 1 1 1 1 1 1] | 8.3838 | 8.7763 | 8.9778 | 5.857 | 6.5621 | 6.7074
Case6：280MHz [1 1 1 1 1 1 1 1 0 0 1 1 1 1 1 1] | 8.2841 | 8.382 | 9.0837 | 7.4562 | 8.1376 | 8.1376
Case7：280MHz [1 1 1 1 1 1 1 1 1 1 0 0 1 1 1 1] | 8.5967 | 8.9009 | 8.9009 | 6.0188 | 6.7785 | 6.7785
Case8：280MHz [1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 1] | 7.6949 | 8.1591 | 8.2149 | 5.9677 | 7.8276 | 7.8276
Case9：280MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0] | 7.811 | 8.0114 | 8.2885 | 6.596 | 7.3592 | 7.3592
Case10: 240MHz [1 1 1 1 0 0 0 0 1 1 1 1 1 1 1 1] | 8.5031 | 8.9613 | 8.9613 | 6.7521 | 7.7001 | 8.1866
Case11: 240MHz [1 1 1 1 1 1 1 1 0 0 0 0 1 1 1 1] | 8.5031 | 8.9613 | 8.9613 | 7.0361 | 7.3258 | 7.4535
Case12: 240MHz [1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0] | 7.0794 | 7.4069 | 7.5154 | 6.8461 | 7.8044 | 8.1341
Case13: 240MHz [0 0 0 0 1 1 1 1 1 1 1 1 1 1 1 1] | 7.0794 | 7.4069 | 7.5154 | 7.0794 | 7.4069 | 7.5154
Worst PAPR [dB] | 8.5967 [Case 7] | 8.9944 [case 1] | 9.0837 [Case 6] | 7.6754 [Case 2] | 8.1376 [case6] | 8.3602 [Case 2]

## Slide 16: Appendix: QAM Data PAPR

## Slide 17: Appendix
1x LTF 240MHz/160+80
BW | Full bandwidth & Preamble Puncturing Patterns | Note
240MHz | Case1: 240MHz [1 1 1 1 1 1 1 1 1 1 1 1] Case2：200MHz [0 0 1 1 1 1 1 1 1 1 1 1] Case3：200MHz [1 1 0 0 1 1 1 1 1 1 1 1] Case4：200MHz [1 1 1 1 0 0 1 1 1 1 1 1] Case5：200MHz [1 1 1 1 1 1 0 0 1 1 1 1] Case6：200MHz [1 1 1 1 1 1 1 1 0 0 1 1] Case7：200MHz [1 1 1 1 1 1 1 1 1 1 0 0] Case8：160MHz [0 0 0 0 1 1 1 1 1 1 1 1] Case9：160MHz [1 1 1 1 0 0 0 0 1 1 1 1] Case10: 160MHz [1 1 1 1 1 1 1 1 0 0 0 0]. | “1” stands for non-punctured 20MHz; “0” stands for punctured 20MHz.