## Slide 1: Yet Another Fast Link Adaptation Attempt
Date: 2020-03-15
Authors:

## Slide 2: Abstract
In this submission, new methods to enable Fast Link Adaptation are discussed and recommendation is provided to break the curse of “Nobody Implements It”

## Slide 3: The Art of Link Adaptation
Open Loop Control System via Sampling-based algorithm
  Sampling specific MCS index, NSS, GI, Bandwidth etc. over certain probing interval
  Heuristically derive the next rate based on packet loss, throughput and so on
Algorithm Design
Parameter Tuning
+
Huge System Bring up effort!

## Slide 4: Fast Link Adaptation
Close-loop Control System via Measurement-based algorithm
  MCS feedback mechanism via HT/VHT/HE Variant HT Control field [1-3]
TX
RX
1, MCS Feedback Request
2, monitor the received packets or channel characteristics
3, compute optimal
MCS
4, MCS Feedback Response

## Slide 5: The Curse of “Nobody Implements It”
Hardware Limitations
Different Assumption at TX and RX
In case of immediate feedback, not all the hardware can finish the computational task in time
Even it can finish, the result may not be trustworthy
RX computes the optimal MCS under the assumption to maximize the throughput
TX’s algorithm may choose to use lower MCS to reduce retransmission
Delayed feedback may not be useful

## Slide 6: Antidote 1: Prefer Measurement over Computation
Feedback PHY handy measurement results rather than MCS
  RSSI
  CSI: SNR per stream, SNR per RU
  Codeword Error Rate

## Slide 7: Antidote 2: Negotiated Support
Establish trust between TX and RX on feedback results
  At least devices from the same ecosystem can faithfully utilize the feedback
  Define measurement accuracy capabilities
Feedback support negotiation with different levels
  Level 0: feedback based on certain criteria [4]
    Ex: limited connectivity, RTS/CTS request
  Level 1: measurement feedback
    Ex: RSSI, CSI, etc.
  Level 2: computation feedback
    Ex: genie MCS

## Slide 8: Antidote 3: Immediate Feedback
Existing Methods
  Control Wrapper for ACK, Compressed BA frame
    Only available for HT/VHT, rarely implemented
  Compressed BA + QoS Null with A-Control: HE
    QoS Null frame processing is not mandated, big overhead for 26-bit A-Control
New method: Enhanced Multi-STA BA frame
  Define “Per AID TID Info” with AID11>2007 to new meanings, i.e., link adaptation feedbacks
  Negotiated Usage
    Enhanced Multi-STA BA frame support is signaled in Extended Capabilities for 11ax devices and newer generation devices
    Using reserved bits in ADDBA Extension element, ADDBA exchanges set new an additional BA Parameter if using Multi-STA BA for the whole session

## Slide 9: Enhanced Multi-STA BA Frame
Use any AID11>2007 to signal non-block-ack session related information using TLV format

## Slide 10: Summary
We recommend to adopt the negotiation-based immediate feedback of PHY measurements for fast link adaptation.

## Slide 11: Straw Poll
Do you agree to enhance the usage of Multi-STA BA frame to include information beyond MPDU acknowledgments by assigning new meanings to “Per TID AID Info” with AID>2007?
  Y
  N
  A

## Slide 12: References
[1] Next Generation Wireless LANs: 802.11n and 802.11ac, Eldad Perahia and Robert Stacey, Cambridge University Press
[2] IEEE STD 802.11-2016
[3] IEEE STD 802.11ax D5.0
[4] Temporary-Limited-Connection, Matthew Fischer, 2019, available at https://mentor.ieee.org/802.11/dcn/19/11-19-0306-05-000m-temporary-limited-connection.docx