## Slide 1: Indication of Large-size RU Combinations
Date: 2020-07-12
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Yanyi Ding |  |  |  | 
Urabe Yoshio |  |  |  | 
Rojan Chitrakar |  |  |  | 
Rajat Pushkarna |  |  |  | 

## Slide 2: Background
Regarding RU allocation signaling in the EHT-SIG of an EHT PPDU transmitted to multiple users, SPs have been passed on how to indicate small-size RU combinations in RU allocation table [1].
This contribution addresses how to indicate large-size RU combinations in RU allocation table for non-compressed OFDMA mode [2] which features：
  RU Allocation (RUA) subfields in the Common field indicates the RU assignment information with granularity of 20MHz.
  N RU Allocation subfields per EHT-SIG content channel (CC), where N = 1 for 20/40MHz, 2 for 80MHz, 4 for 160/80+80MHz, 6 for 240/160+80MHz, 8 for 320/160+160MHz.

## Slide 3: Proposal
A value of each RUA subfield is only able to indicate sizes of a large-size RU combination, but cannot indicate any information on frequency-domain positions of the large-size RU combination.
  Pros: the number of entries required for large-size RU combinations in RU allocation table is minimized.
Frequency-domain positions of each large-size RU combination can be calculated according to RUA subfield index and/or EHT-SIG CC index
  Pros: It may be unnecessary to store mappings between frequency-domain positions of each large-size RU combination and EHT-SIG CC indices and/or RUA subfield indices.
B7….B1B0 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | # of Entries
TBD | 242-tone RU+484-tone RU |  |  |  |  |  |  |  |  | 8
TBD | 484-tone RU+996-tone RU |  |  |  |  |  |  |  |  | 8
TBD | 2*996-tone RU+484-tone RU |  |  |  |  |  |  |  |  | 8
TBD | 3*996-tone RU |  |  |  |  |  |  |  |  | 8
TBD | 3*996-tone RU+484-tone RU |  |  |  |  |  |  |  |  | 8
RU allocation table
Lei Huang (Panasonic)

## Slide 4: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 80MHz
 | Mapping of Frequency-Domain Positions of RU Combinations |  |  | 
RU Combination | CC1, RUA1 | CC2, RUA1 | CC1, RUA2 | CC2, RUA2
484-tone RU+ 242-tone RU | 484-tone RU1, 242-tone RU3 | 484-tone RU1, 242-tone RU4 | 484-tone RU2, 242-tone RU1 | 484-tone RU2, 242-tone RU2
When a RUA subfield indicates 484-tone RU+242-tone RU
  484-tone RU index (j) can be calculated based on RUA subfield index (m)
    j = m, where m=1,2
  242-tone RU index (i) can be calculated based on EHT-SIG CC index (n) and RUA subfield index (m)
    i = 2*(2-m)+n, where m=1,2; n=1,2
Lei Huang (Panasonic)

## Slide 5: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 160/80+80MHz
When a RUA subfield indicates 484-tone RU+242-tone RU
  484-tone RU index (j) can be calculated based on RUA subfield index (m)
    j = m, where m = 1 to 4
  242-tone RU index (i) can be calculated based on EHT-SIG CC index (n) and RUA subfield index (m)
    i = 8*ceil(m/2)-2m+n-4, where m=1 to 4; n=1,2
When a RUA subfield indicates 996-tone RU+484-tone RU
  996-tone RU index (k) and 484-tone RU index (j) can be calculated based on RUA subfield index (m)
    k = ceil(m/2), where m = 1 to 4
    j = m-4*ceil(m/2)+6
 | Mapping of Frequency-Domain Positions of RU Combinations |  |  |  |  |  |  | 
RU Combination | CC1, RUA1 | CC2, RUA1 | CC1, RUA2 | CC2, RUA2 | CC1, RUA3 | CC2, RUA3 | CC1, RUA4 | CC2, RUA4
484-tone RU+242-tone RU | 484-tone RU1, 242-tone RU3 | 484-tone RU1, 242-tone RU4 | 484-tone RU2, 242-tone RU1 | 484-tone RU2, 242-tone RU2 | 484-tone RU3, 242-tone RU7 | 484-tone RU3, 242-tone RU8 | 484-tone RU4, 242-tone RU5 | 484-tone RU4, 242-tone RU6
996-tone RU+484-tone RU | 996-tone RU1, 484-tone RU3 |  | 996-tone RU1, 484-tone RU4 |  | 996-tone RU2, 484-tone RU1 |  | 996-tone RU2, 484-tone RU2 | 
Lei Huang (Panasonic)

## Slide 6: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 240/160+80MHz
 | Mapping of Frequency-Domain Positions of RU Combinations |  |  |  |  |  |  |  |  |  |  | 
RU Combination | CC1, RUA1 | CC2, RUA1 | CC1, RUA2 | CC2, RUA2 | CC1, RUA3 | CC2, RUA3 | CC1, RUA4 | CC2, RUA4 | CC1, RUA5 | CC2, RUA5 | CC1, RUA6 | CC2, RUA6
484-tone RU+ 242-tone RU | 484-tone RU1, 242-tone RU3 | 484-tone RU1, 242-tone RU4 | 484-tone RU2, 242-tone RU1 | 484-tone RU2, 242-tone RU2 | 484-tone RU3, 242-tone RU7 | 484-tone RU3, 242-tone RU8 | 484-tone RU4, 242-tone RU5 | 484-tone RU4, 242-tone RU6 | 484-tone RU5, 242-tone RU11 | 484-tone RU5, 242-tone RU12 | 484-tone RU6, 242-tone RU9 | 484-tone RU6, 242-tone RU10
996-tone RU+ 484-tone RU | 996-tone RU1, 484-tone RU3 |  | 996-tone RU1, 484-tone RU4 |  | 996-tone RU2, 484-tone RU1 | 996-tone RU2, 484-tone RU2 | 996-tone RU2, 484-tone RU5 | 996-tone RU2, 484-tone RU6 | 996-tone RU3, 484-tone RU3 |  | 996-tone RU3, 484-tone RU4 | 
2*996-tone RU+ 484-tone RU | 996-tone RU1, 996-tone RU2, 484-tone RU5 |  | 996-tone RU1, 996-tone RU2, 484-tone RU6 |  | 996-tone RU2, 996-tone RU3, 484-tone RU1 |  | 996-tone RU2, 996-tone RU3, 484-tone RU2 |  | 996-tone RU3, 996-tone RU1, 484-tone RU3 |  | 996-tone RU3, 996-tone RU1, 484-tone RU4 | 
Lei Huang (Panasonic)

## Slide 7: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 240/160+80MHz
When a RUA subfield indicates 484-tone RU+242-tone RU
  RUA subfield index (m) determines 484-tone RU index (j)
    j = m, where m = 1 to 6
  EHT-SIG CC index (n) and RUA subfield index (m) determine 242-tone RU index (i)
    i = 8*ceil(m/2)-2m+n-4, where m=1 to 6; n=1,2
When a RUA subfield indicates 996-tone RU+484-tone RU
  RUA subfield index (m) determines 996-tone RU index (k)
    k = ceil(m/2), where m = 1 to 6
  EHT-SIG CC index (n) and RUA subfield index (m) determines 484-tone RU index (j)
    j = m-4*ceil(m/3)+6 where m = 1, 2, 5, 6
    j = (m-3)*4+n where m = 3, 4; n = 1,2
When a RUA subfield indicates 2*996-tone RU+484-tone RU
  RUA subfield index (m) determines 1st 996-tone RU index (k1), 2nd 996-tone RU index (k2) and 484-tone RU index (j)
    k1 = ceil(m/2), where m = 1 to 6
    k2 = mod(k1,3)+1
    j = mod(m+3,6)+1, where m = 1 to 6
Lei Huang (Panasonic)

## Slide 8: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 320/160+160MHz
 | Mapping of Frequency-Domain Positions of RU Combinations |  |  |  |  |  |  | 
RU Combination | CC1, RUA1 | CC2, RUA1 | CC1, RUA2 | CC2, RUA2 | CC1, RUA3 | CC2, RUA3 | CC1, RUA4 | CC2, RUA4
484-tone RU+242-tone RU | 484-tone RU1, 242-tone RU3 | 484-tone RU1, 242-tone RU4 | 484-tone RU2, 242-tone RU1 | 484-tone RU2, 242-tone RU2 | 484-tone RU3, 242-tone RU7 | 484-tone RU3, 242-tone RU8 | 484-tone RU4, 242-tone RU5 | 484-tone RU4, 242-tone RU6
996-tone RU+484-tone RU | 996-tone RU1, 484-tone RU3 |  | 996-tone RU1, 484-tone RU4 |  | 996-tone RU2, 484-tone RU1 |  | 996-tone RU2, 484-tone RU2 | 
3*996-tone RU | 996-tone RU1, 996-tone RU2, 996-tone RU3 |  |  |  | 996-tone RU1, 996-tone RU2, 996-tone RU4 |  |  | 
3*996-tone RU +484-tone RU | 996-tone RU1, 996-tone RU2, 996-tone RU3, 484-tone RU7 |  | 996-tone RU1, 996-tone RU2, 996-tone RU3, 484-tone RU8 |  | 996-tone RU1, 996-tone RU2, 996-tone RU4, 484-tone RU5 |  | 996-tone RU1, 996-tone RU2, 996-tone RU4, 484-tone RU6 | 
 | Mapping of Frequency-Domain Positions of RU Combinations |  |  |  |  |  |  | 
RU Combination | CC1, RUA5 | CC2, RUA5 | CC1, RUA6 | CC2, RUA6 | CC1, RUA7 | CC2, RUA7 | CC1, RUA8 | CC2, RUA8
484-tone RU+242-tone RU | 484-tone RU5, 242-tone RU11 | 484-tone RU5, 242-tone RU12 | 484-tone RU6, 242-tone RU9 | 484-tone RU6, 242-tone RU10 | 484-tone RU7, 242-tone RU15 | 484-tone RU7, 242-tone RU16 | 484-tone RU8, 242-tone RU13 | 484-tone RU8, 242-tone RU14
996-tone RU+484-tone RU | 996-tone RU3, 484-tone RU7 |  | 996-tone RU3, 484-tone RU8 |  | 996-tone RU4, 484-tone RU5 |  | 996-tone RU4, 484-tone RU6 | 
3*996-tone RU | 996-tone RU1, 996-tone RU3, 996-tone RU4 |  |  |  | 996-tone RU2, 996-tone RU3, 996-tone RU4 |  |  | 
3*996-tone RU +484-tone RU | 996-tone RU1, 996-tone RU3, 996-tone RU4, 484-tone RU3 |  | 996-tone RU1, 996-tone RU3, 996-tone RU4, 484-tone RU4 |  | 996-tone RU2, 996-tone RU3, 996-tone RU4, 484-tone RU1 |  | 996-tone RU2, 996-tone RU3, 996-tone RU4, 484-tone RU2 | 
Lei Huang (Panasonic)

## Slide 9: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 320/160+160MHz
When a RUA subfield indicates 484-tone RU+242-tone RU
  484-tone RU index (j) can be calculated based on RUA subfield index (m)
    j = m, where m = 1 to 8
  242-tone RU index (i) can be calculated based on EHT-SIG CC index (n) and RUA subfield index (m)
    i = 8*ceil(m/2)-2m+n-4, where m=1 to 8; n=1,2
When a RUA subfield indicates 996-tone RU+484-tone RU
  996-tone RU index (k) and 484-tone RU index (j) can be calculated based on RUA subfield index (m)
    k = ceil(m/2), where m = 1 to 8
    j = m-4*ceil(m/2)+8*floor(m/5)+6
When a RUA subfield indicates 3*996-tone RU
  1st 996-tone RU index (k1), 2nd 996-tone RU index (k2) and 3rd 996-tone RU index (k3) can be calculated based on RUA subfield index (m)
    k1 = ceil(m/4)+floor(m/5), where m = 1 to 8
    k2 = k1+1
    k3 = k1+ceil(m/2)-5*floor(m/5)
When a RUA subfield indicates 3*996-tone RU+484-tone RU
  1st 996-tone RU index (k1), 2nd 996-tone RU index (k2), 3rd 996-tone RU and 484-tone RU index (j) can be calculated based on RUA subfield index (m)
    k1 = ceil(m/4)+floor(m/5), where m = 1 to 8
    k2 = k1+1
    k3 = k1+ceil(m/2)-5*floor(m/5)
    j = m-2*ceil(m/2)-2*floor(m/5)+8
Lei Huang (Panasonic)

## Slide 10: Summary
We proposed a value of each RU Allocation subfield only indicates sizes of a large-size RU combination; and frequency-domain positions of each large-size RU combination can be calculated according to RU Allocation subfield index and/or EHT-SIG CC index

## Slide 11: Reference
IEEE 802.11-20/0566r35, Compendium of straw polls and potential changes to the Specification Framework Document.
IEEE 802.11-20/0922r2, RU allocation subfield in EHT-SIG Follow up II.

## Slide 12: SP #1
Do you agree that for RU242+RU484 and RU484+RU996, in the RU allocation table, 8 entries per RU size will be used to indicate contributing 1~8 User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield?
  Make the following change in the baseline RU allocation table in 11be SFD
  Compressed modes are TBD.
  Yes/No/Abstain
B7….B1B0 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | # of Entries
TBD | 242-tone RU+484-tone RU |  |  |  |  |  |  |  |  | 8
TBD | 484-tone RU+996-tone RU |  |  |  |  |  |  |  |  | 8

## Slide 13: SP #2
Do you agree the following mapping of frequency-domain positions of RU242+RU484 to RU Allocation (RUA) subfield index and EHT-SIG content channel (CC) index for PPDU BW = 80 MHz?
  Yes/No/Abstain
 | Mapping of Frequency-Domain Positions of RU Combinations |  |  | 
RU combination | CC1, RUA1 | CC2, RUA1 | CC1, RUA2 | CC2, RUA2
484-tone RU+ 242-tone RU | 484-tone RU1, 242-tone RU3 | 484-tone RU1, 242-tone RU4 | 484-tone RU2, 242-tone RU1 | 484-tone RU2, 242-tone RU2

## Slide 14: SP #3
Do you agree the following mapping of frequency-domain positions of RU242+RU484 and RU484+RU996 to RU Allocation (RUA) subfield index and EHT-SIG content channel (CC) index for PPDU BW = 160/80+80 MHz?
  Yes/No/Abstain
 | Mapping of Frequency-Domain Positions of RU Combinations |  |  |  |  |  |  | 
RU combination | CC1, RUA1 | CC2, RUA1 | CC1, RUA2 | CC2, RUA2 | CC1, RUA3 | CC2, RUA3 | CC1, RUA4 | CC2, RUA4
484-tone RU+242-tone RU | 484-tone RU1, 242-tone RU3 | 484-tone RU1, 242-tone RU4 | 484-tone RU2, 242-tone RU1 | 484-tone RU2, 242-tone RU2 | 484-tone RU3, 242-tone RU7 | 484-tone RU3, 242-tone RU8 | 484-tone RU4, 242-tone RU5 | 484-tone RU4, 242-tone RU6
996-tone RU+484-tone RU | 996-tone RU1, 484-tone RU3 |  | 996-tone RU1, 484-tone RU4 |  | 996-tone RU2, 484-tone RU1 |  | 996-tone RU2, 484-tone RU2 |