## Slide 1: Indication of Large-Size RU Combinations
Date: 2020-07-19
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Yanyi Ding |  |  |  | 
Yoshio Urabe |  |  |  | 
Rojan Chitrakar |  |  |  | 
Rajat Pushkarna |  |  |  | 

## Slide 2: Background
Regarding RU allocation signaling in the EHT-SIG of an EHT PPDU transmitted to multiple users, SPs have been passed on how to indicate small-size RU combinations in RU allocation table [1].
This contribution addresses how to indicate large-size RU combinations in RU allocation table for non-compressed OFDMA mode [2] which features：
  RU Allocation (RUA) subfields in the Common field indicates the RU assignment information with granularity of 20MHz.
  N RU Allocation subfields per EHT-SIG content channel (CC), where N = 1 for 20/40MHz, 2 for 80MHz, 4 for 160/80+80MHz, 6 for 240/160+80MHz, 8 for 320/160+160MHz.

## Slide 3: Design Principle
In our proposal, the large-size RU combination indication is designed in order to
  minimize the number of entries required for large-size RU combinations in RU allocation table;
  enable dynamic split of user fields for any large-size RU combinations; and
  simplify receiver processing for parsing RU Allocation subfields.
Lei Huang (Panasonic)

## Slide 4: Proposal
B7….B1B0 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | # of Entries
TBD | 242(1)+484 |  |  |  |  |  |  |  |  | 8
TBD | 242(2)+484 |  |  |  |  |  |  |  |  | 8
TBD | 484(1)+996 |  |  |  |  |  |  |  |  | 8
TBD | 484(2)+996 |  |  |  |  |  |  |  |  | 8
Lei Huang (Panasonic)
For RU242+RU484 and RU484+RU996, we propose to make the following changes in the baseline RU allocation table in 11be SFD.
  242(1)+484 or 242(2)+484 indicates a RU242+RU484 where the RU242 is the 1st or 2nd RU242 of a 40MHz segment within a same 80MHz segment as the RU484.
  484(1)+996 or 484(2)+996 indicates a RU484+RU996 where the RU484 is the 1st or 2nd RU484 of a 80MHz segment adjacent to the RU996.
  Actual frequency-domain positions of RU242+RU484 and RU484+RU996 can be calculated according to RUA subfield index.

## Slide 5: Proposal (cont.)
B7….B1B0 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | # of Entries
TBD | 484+2*996 |  |  |  |  |  |  |  |  | 8
TBD | 3*996 |  |  |  |  |  |  |  |  | 8
TBD | 484+3*996 |  |  |  |  |  |  |  |  | 8
Lei Huang (Panasonic)
For RU484+2*RU996, 3*RU996 and RU484+3*RU996, we propose to make the following changes in the baseline RU allocation table in 11be SFD.
  Frequency-domain positions of RU484+2*RU996, 3*RU996 and RU484+3*RU996 can be calculated according to RUA subfield index.

## Slide 6: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 80MHz
 | Mapping of Frequency-Domain Positions of RU Combinations | 
RU Combination | CC1 & CC2, RUA1 | CC1 &CC2, RUA2
242+484 | 484-tone RU1, 242-tone RU3 or RU4 | 484-tone RU2, 242-tone RU1 or RU2
When a RUA subfield indicates 242(1)+484 or 242(2)+484
  242-tone RU index (i) and 484-tone RU index (j) can be calculated based on RUA subfield index (m), where m=1,2
    i = 5-2*m when the RUA subfield indicates 242(1)+484
    i = 6-2*m when the RUA subfield indicates 242(2)+484
    j = m
Lei Huang (Panasonic)

## Slide 7: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 160/80+80MHz
When a RUA subfield indicates 242(1)+484 or 242(2)+484
  242-tone RU index (i) and 484-tone RU index (j) can be calculated based on RUA subfield index (m), where m = 1 to 4
    i = 8*ceil(m/2)-2*m-3 when the RUA subfield indicates 242(1)+484
    i = 8*ceil(m/2)-2*m-2 when the RUA subfield indicates 242(2)+484
    j = m
When a RUA subfield indicates 484(1)+996 or 484(2)+996
  996-tone RU index (k) and 484-tone RU index (j) can be calculated based on RUA subfield index (m) where m = 1 to 4
    j = m-4*ceil(m/2)+6
    k = ceil(m/2)
 | Mapping of Frequency-Domain Positions of RU Combinations |  |  | 
RU Combination | CC1 & CC2, RUA1 | CC1 & CC2, RUA2 | CC1 & CC2, RUA3 | CC1 & CC2, RUA4
242+484 | 484-tone RU1, 242-tone RU3 or RU4 | 484-tone RU2, 242-tone RU1 or RU2 | 484-tone RU3, 242-tone RU7 or RU8 | 484-tone RU4, 242-tone RU5 or RU6
484+996 | 996-tone RU1, 484-tone RU3 | 996-tone RU1, 484-tone RU4 | 996-tone RU2, 484-tone RU1 | 996-tone RU2, 484-tone RU2
Lei Huang (Panasonic)

## Slide 8: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 240/160+80MHz
 | Mapping of Frequency-Domain Positions of RU Combinations |  |  |  |  | 
RU Combination | CC1 & CC2, RUA1 | CC1 & CC2, RUA2 | CC1 & CC2, RUA3 | CC1 & CC2, RUA4 | CC1 & CC2, RUA5 | CC1 & CC2, RUA6
242+484 | 484-tone RU1, 242-tone RU3 or RU4 | 484-tone RU2, 242-tone RU1 or RU2 | 484-tone RU3, 242-tone RU7 or RU8 | 484-tone RU4, 242-tone RU5 or RU6 | 484-tone RU5, 242-tone RU11 or RU12 | 484-tone RU6, 242-tone RU9 or RU10
484+996 | 996-tone RU1, 484-tone RU3 | 996-tone RU1, 484-tone RU4 | 996-tone RU2, 484-tone RU1 or RU2 | 996-tone RU2, 484-tone RU5 or RU6 | 996-tone RU3, 484-tone RU3 | 996-tone RU3, 484-tone RU4
484+2*996 | 996-tone RU1, 996-tone RU2, 484-tone RU5 | 996-tone RU1, 996-tone RU2, 484-tone RU6 | 996-tone RU2, 996-tone RU3, 484-tone RU1 | 996-tone RU2, 996-tone RU3, 484-tone RU2 | 996-tone RU3, 996-tone RU1, 484-tone RU3 | 996-tone RU3, 996-tone RU1, 484-tone RU4
Lei Huang (Panasonic)
When a RUA subfield indicates 242(1)+484 or 242(2)+484
  242-tone RU index (i) and 484-tone RU index (j) can be calculated based on RUA subfield index (m), where m=1 to 6
    i = 8*ceil(m/2)-2m-3 when the RUA subfield indicates 242(1)+484
    i = 8*ceil(m/2)-2m-2 when the RUA subfield indicates 242(2)+484
    j = m

## Slide 9: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 240/160+80MHz
When a RUA subfield indicates 484(1)+996 or 484(2)+996
  484-tone RU index (j) and 996-tone RU index (k) can be calculated based on RUA subfield index (m) where m = 1 to 6
    j = m-4*ceil(m/3)+6 when m = 1, 2, 5, 6
    j = 4m-11 when m = 3, 4 and the RUA subfield indicates 484(1)+996
    j = 4m-10 when m = 3, 4 and the RUA subfield indicates 484(2)+996
    k = ceil(m/2)
When a RUA subfield indicates 484+2*996
  484-tone RU index (j) , 1st 996-tone RU index (k1) and 2nd 996-tone RU index (k2) can be calculated according to the RUA subfield index (m) where m = 1 to 6
    j = mod(m+3,6)+1
    k1 = ceil(m/2)
    k2 = mod(k1,3)+1
Lei Huang (Panasonic)

## Slide 10: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 320/160+160MHz
 | Mapping of Frequency-Domain Positions of RU Combinations |  |  | 
RU Combination | CC1 & CC2, RUA1 | CC1 & CC2, RUA2 | CC1 & CC2, RUA3 | CC1 & CC2, RUA4
242+484 | 484-tone RU1, 242-tone RU3 or RU4 | 484-tone RU2, 242-tone RU1 or RU2 | 484-tone RU3, 242-tone RU7 or RU8 | 484-tone RU4, 242-tone RU5 or RU6
484+996 | 996-tone RU1, 484-tone RU3 | 996-tone RU1, 484-tone RU4 | 996-tone RU2, 484-tone RU1 | 996-tone RU2, 484-tone RU2
3*996 | 996-tone RU1, 996-tone RU2, 996-tone RU3 |  | 996-tone RU1, 996-tone RU2, 996-tone RU4 | 
484+3*996 | 996-tone RU1, 996-tone RU2, 996-tone RU3, 484-tone RU7 | 996-tone RU1, 996-tone RU2, 996-tone RU3, 484-tone RU8 | 996-tone RU1, 996-tone RU2, 996-tone RU4, 484-tone RU5 | 996-tone RU1, 996-tone RU2, 996-tone RU4, 484-tone RU6
 | Mapping of Frequency-Domain Positions of RU Combinations |  |  | 
RU Combination | CC1 & CC2, RUA5 | CC1 & CC2, RUA6 | CC1 & CC2, RUA7 | CC1 & CC2, RUA8
242+484 | 484-tone RU5, 242-tone RU11 or RU12 | 484-tone RU6, 242-tone RU9 or RU10 | 484-tone RU7, 242-tone RU15 or RU16 | 484-tone RU8, 242-tone RU13 or RU14
484+996 | 996-tone RU3, 484-tone RU7 | 996-tone RU3, 484-tone RU8 | 996-tone RU4, 484-tone RU5 | 996-tone RU4, 484-tone RU6
3*996 | 996-tone RU1, 996-tone RU3, 996-tone RU4 |  | 996-tone RU2, 996-tone RU3, 996-tone RU4 | 
484+3*996 | 996-tone RU1, 996-tone RU3, 996-tone RU4, 484-tone RU3 | 996-tone RU1, 996-tone RU3, 996-tone RU4, 484-tone RU4 | 996-tone RU2, 996-tone RU3, 996-tone RU4, 484-tone RU1 | 996-tone RU2, 996-tone RU3, 996-tone RU4, 484-tone RU2
Lei Huang (Panasonic)

## Slide 11: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 320/160+160MHz
When a RUA subfield indicates 242(1)+484 or 242(2)+484
  242-tone RU index (i) and 484-tone RU index (j) can be calculated based on RUA subfield index (m), where m=1 to 8
    i = 8*ceil(m/2)-2m-3 when the RUA subfield indicates 242(1)+484
    i = 8*ceil(m/2)-2m-2 when the RUA subfield indicates 242(2)+484
    j = m
When a RUA subfield indicates 484(1)+996 or 484(2)+996
  484-tone RU index (j) and 996-tone RU index (k) can be calculated based on RUA subfield index (m), where m = 1 to 8
    j = m-4*ceil(m/2)+8*floor(m/5)+6
    k = ceil(m/2)
Lei Huang (Panasonic)

## Slide 12: Mapping of Frequency-Domain Positions of Large-Size RU Combination for PPDU BW = 320/160+160MHz
When a RUA subfield indicates 3*996
  1st 996-tone RU index (k1), 2nd 996-tone RU index (k2) and 3rd 996-tone RU index (k3) can be calculated based on RUA subfield index (m), where m = 1 to 8
    k1 = ceil(m/4)+floor(m/5),
    k2 = k1+1
    k3 = k1+ceil(m/2)-5*floor(m/5)
When a RUA subfield indicates 484+3*996
  1st 996-tone RU index (k1), 2nd 996-tone RU index (k2), 3rd 996-tone RU and 484-tone RU index (j) can be calculated based on RUA subfield index (m), where m = 1 to 8
    j = m-2*ceil(m/2)-2*floor(m/5)+8
    k1 = ceil(m/4)+floor(m/5)
    k2 = k1+1
    k3 = k1+ceil(m/2)-5*floor(m/5)
Lei Huang (Panasonic)

## Slide 13: Summary
We proposed to make the following changes in the baseline RU allocation table in 11be SFD for large-size RU combinations.
B7….B1B0 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | # of Entries
TBD | 242(1)+484 |  |  |  |  |  |  |  |  | 8
TBD | 242(2)+484 |  |  |  |  |  |  |  |  | 8
TBD | 484(1)+996 |  |  |  |  |  |  |  |  | 8
TBD | 484(2)+996 |  |  |  |  |  |  |  |  | 8
TBD | 484+2*996 |  |  |  |  |  |  |  |  | 8
TBD | 3*996 |  |  |  |  |  |  |  |  | 8
TBD | 484+3*996 |  |  |  |  |  |  |  |  | 8
Frequency-domain positions of a large-size RU combination can be calculated according to RUA subfield index.

## Slide 14: Reference
IEEE 802.11-20/0566r42, Compendium of straw polls and potential changes to the Specification Framework Document.
IEEE 802.11-20/0922r2, RU allocation subfield in EHT-SIG Follow up II.

## Slide 15: SP #1
Do you agree to make the following change in the baseline RU allocation table in 11be SFD for RU242+RU484?
  242(1)+484 or 242(2)+484 indicates a RU242+RU484 where the RU242 is the 1st or 2nd RU242 of a 40MHz segment within a same 80MHz segment as the RU484.
  Yes/No/Abstain
B7….B1B0 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | # of Entries
TBD | 242(1)+484 |  |  |  |  |  |  |  |  | 8
TBD | 242(2)+484 |  |  |  |  |  |  |  |  | 8

## Slide 16: SP #2
Do you agree to make the following change in the baseline RU allocation table in 11be SFD for RU484+RU996?
  484(1)+996 or 484(2)+996 indicates a RU484+RU996 where the RU484 is the 1st or 2nd RU484 of a 80MHz segment adjacent to the RU996.
  Yes/No/Abstain
B7….B1B0 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | # of Entries
TBD | 484(1)+996 |  |  |  |  |  |  |  |  | 8
TBD | 484(2)+996 |  |  |  |  |  |  |  |  | 8

## Slide 17: SP #3
Do you agree to make the following change in the baseline RU allocation table in 11be SFD for RU484+2*RU996, 3*RU996 and RU484+3*RU996?
  Yes/No/Abstain
B7….B1B0 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | # of Entries
TBD | 484+2*996 |  |  |  |  |  |  |  |  | 8
TBD | 3*996 |  |  |  |  |  |  |  |  | 8
TBD | 484+3*996 |  |  |  |  |  |  |  |  | 8