## Slide 1: Experimental results for TGbb centre frequency discussion
Date: 2020-07-10
Authors:
July 2020

## Slide 2: Abstract
This presentation aims to discuss our experimental validation on the centre frequency for the common mode mandatory PHY

## Slide 3: Review (1)
In https://mentor.ieee.org/802.11/dcn/20/11-20-0572-00-00bb-proposed-center-frequency-mandatory-phy.pptx, we calculated the optimal center frequency for each BW.
BW [MHz] | fc* [MHz] | Δ* [MHz]
20 | 12.5 (-21.68 dBr) | 2.5
40 | 24 (-21.43 dBr) | 4
80 | 47 (-21.32 dBr) | 7
160 | 96 (-21.56 dBr) | 16
Note: Δ*=fc* - BW/2

## Slide 4: Review (2)
However, we need one global center frequency for all BW configurations
In https://mentor.ieee.org/802.11/dcn/20/11-20-0572-02-00bb-proposed-center-frequency-mandatory-phy.pptx, we proposed the following global center frequency
BW [MHz] | fc* [MHz] | Δ* [MHz]
20 | 26 | 16
40 | 36 | 16
80 | 56 | 16
160 | 96 | 16

## Slide 5: Experimental Setup
802.11ac
Laptop
eth0
SBC + RF down-conversion
Down-
conversion
5 GHz band
fc
OWC Front-end
70 cm
PD
Oscilloscope
CPU/host
802.11ac
Up-
conversion
fc
SBC + RF up-conversion
eth0
OWC Front-end
Laptop
CPU/host
5 GHz band

## Slide 6: Experimental Setup video
https://photos.google.com/share/AF1QipNTcH1Fe5Yqsj92M-nTI-5Ks7mOoES7_cAVPSmrp2qGaZV5O4sW2eqUEnda-EbKwQ/photo/AF1QipNv5hXvyyJYri_C17R3GPwhMryHYtJgPiYyFurH?key=SXFPdkwwZldoNFFoQWlCNHRQWDNrRHNsTzFqckJn

## Slide 7: Initial Measurement
Using an 802.11ac chipset and a down-conversion, we obtain the following optical spectrum, for example, with fc =12.5 MHz and fc = 111.25 MHz, respectively

## Slide 8: Experimental video for 21 MHz centre freq.
https://photos.google.com/share/AF1QipNTcH1Fe5Yqsj92M-nTI-5Ks7mOoES7_cAVPSmrp2qGaZV5O4sW2eqUEnda-EbKwQ/photo/AF1QipPX0cHX0Fjegiyonlfp2iP1PIEUOE8Pl01ld_g8?key=SXFPdkwwZldoNFFoQWlCNHRQWDNrRHNsTzFqckJn

## Slide 9: Measurements with BW = 20 MHz
Note: Our simulation shows the optimum center frequency of 12.5 MHz based on the knee-point criterion.
fc [MHz] | Data rate [Mbps] (1 min measurement)
10 | 20-25
11 | 30
12 | 55
12.5* | 60-65
17 | 70
21 | 78.5
5.06 GHz (default) | 79.5

## Slide 10: Measurements with BW = 40 MHz
Note: Our simulation shows the optimum center frequency of 24 MHz based on the knee-point criterion.
fc [MHz] | Data rate [Mbps] (1 min measurement)
20 | 40
22 | 60
24* | 130-140
25 | 140-145
27 | 145-150
34 | 150-155
5.06 GHz (default) | 165

## Slide 11: Conclusions
The experiments and simulations match for BW = 20 MHz and 40 MHz.

## Slide 12: Appendix: Discussions
Spectrum masks for 802.11ac

## Slide 13: Appendix
Another measurement
5.6 dB per div
10 MHz per div
≈-20 dBr