## Slide 1: EDCA queue for RTA
Date: 2020-08-27
Authors:
Name | Company | Address | Phone | Email
Liangxiao Xin | Sony Corporation |  |  | Liangxiao.Xin@sony.com
Mohamed Abouelseoud |  |  |  | Mohamed.Abouelseoud@sony.com
Yusuke Tanaka |  |  |  | Yusuke.YT.Tanaka@sony.com
Thomas Handte |  |  |  | Thomas.Handte@sony.com

## Slide 2: Introduction
A lot of contributions have suggested, or proposed solutions include updating the queue system to satisfy the latency requirement for RTA traffic [1-10].
In this presentation, we discuss several solutions to enhance EDCA queues for RTA traffic.

## Slide 3: Motivation
EDCA queue maps user priority as defined in 802.1D to the transmit queues. The VI and VO traffic types are already characterized as low latency traffic in 802.1D
  VI: < 100ms latency and jitter, VO: <10ms latency and jitter
However, EDCA queue does not prioritize the delivery of RTA MSDUs within the bounded latency and jitter
  Non-RTA MSDUs do not have bounded latency requirement
  RTA MSDUs have different bounded latency requirements
We discuss options to manage the RTA MSDUs for VI or VO traffic in the EDCA queues
  Differentiate RTA traffic from VI or VO traffic
  Prioritize the transmission of RTA traffic to meet its bounded latency requirement

## Slide 4: Proposed solution 1
EDCA queue management: differentiate the RTA traffic and non-RTA traffic and prioritize the RTA traffic in an existing queue
  Reorder the MSDUs in the transmit queue based on the expiration time of bounded latency. Then, the MSDU with shorter expiration time could be transmitted earlier in the transmit queue with higher probability. The bounded latency of non-RTA traffic could be EDCA lifetime or infinity.
Limitation:
  RTA MSDUs and non-RTA MSDUs share the same transmit queue.
    It requires heavy processing to manage dynamic changes in the queue
    It is possible that the queue buffer is fully occupied by non-RTA MSDUs and RTA MSDUs cannot be enqueued.
Examples of other ideas for EDCA queue management
  DCN0468r0 [1]: use a new UP for a high priority service
  DCN0418r4 [9]: use TIDs 8~15 to classify traffic streams with different QoS requirement
  DCN1045r3 [10]: use L-Marker to classify traffic streams per (source/destination, TID)

## Slide 5: Proposed solution 2
Add new transmit queues to the existing EDCA queue system
  R_VI transmit queue
    Enqueue RTA VI traffic (RTA traffic with UP 5)
    Has higher priority than A_VI & VI transmit queues
  R_VO transmit queue
    Enqueue RTA VO traffic (RTA traffic with UP 6)
    Has higher priority than VO transmit queue
    Has lower priority than A_VO transmit queue
Proposed solution 1 can be applied to the new transmit queue.
Need to consider the fairness between RTA queue and non-RTA queue
  DCN1175r0 [2]: limit the size and frequency of frames enqueued to RTA queue
Limitation: new transmit queue shares the same EDCA parameters with old ones.

## Slide 6: Proposed solution 3
Add new EDCAF (i.e., AC) to the existing EDCA queue system
  LL EDCAF with R_VO transmit queue
    Enqueue RTA traffic (with UP 6) to R_VO transmit queue
Possible techniques can be added onto the new AC
  DCN1851r0 [3] & DCN1524r0 [4] : Operation of EDCAF parameters
  DCN1287r1 [5] : Time-Aware Shaping (802.1Qbv) over Wireless
  DCN1960r1 [11] : Early channel contention
Limitation:
  Should update internal collision mechanism

## Slide 7: Summary
In this presentation, we propose to differentiate RTA traffic from non-RTA traffic and prioritize the transmission of RTA traffic.
Multiple solutions to provide low latency service in the existing EDCA queue systems are proposed:
  Proposal 1: Add new features to the existing EDCA queue system only
  Proposal 2: Add new transmit queues for RTA traffic
  Proposal 3: Add new EDCAF/AC for RTA traffic

## Slide 8: SP1
Do you support to include the following in SFD?
  11be shall define an EDCA mechanism that differentiates RTA traffic from non-RTA traffic and that prioritizes the transmission of RTA traffic.

## Slide 9: SP2
Which option do you support to enhance EDCA queue for RTA?
  Option 1: EDCA queue management
  Option 2: new transmit queues for current EDCAF
  Option 3: a new RTA EDCAF
  Something else
  Abstain
  Note: you can choose more than one option.

## Slide 10: References
[1] 11-20/0468r0: Channel Access Category
[2] 11-19/1175r0: Considerations of New Queue Mechanism for Real-Time Application
[3] 11-19/1851r0: Latency enhancement in multi-link
[4] 11-19/1524r0: Latency enhancement for EHT
[5] 11-19/1287r1: TSN support in 802.11 and potential extensions for Tgbe
[6] 11-19/1933r1: Capabilities to support Time-Aware Scheduling in 802.11be
[7] 11-19/1780r0: AR/VR on EHT: Design Considerations
[8] 11-20/0005r1: Proposals on Latency Reduction
[9] 11-20/0418r4: Low latency service in 802.11be
[10] 11-20/1045r3: Prioritized EDCA channel access
[11] 11-19/1960r1: Reducing Channel Access Delay for RTA Traffic