## Slide 1: MLO: TID-to-link negotiation
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho |  |  |  | 
George Cherian |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Yanjun Sun |  |  |  | 
Date: 2020-02-26

## Slide 2: Background
TID-to-link feature maps a TID to one or more links
  The frames belonging to the TID are sent on the mapped link(s)
Such traffic separation can aid latency sensitive traffic flow
  Assign a high-volume, latency tolerant traffic flow to a subset of link while mapping latency sensitive flows to all links
  Increases channel access opportunities for a latency sensitive flow
  At a system level, reduces contention between latency sensitive and latency tolerant flows
Other use cases include load balancing, co-ex conditions, separating UL/DL flows etc
STAa 1
…
Link 1
Link 2
STAa 2
TIDvo
…
STAb 1
STAb 2
Link 3
STAa 3
STAb 3
…
TIDbe
MLDa
MLDb
…

## Slide 3: Motivation
In this contribution, we propose a simple mechanism to negotiate a TID-to-Link mapping between an AP MLD and a non-AP MLD.

## Slide 4: TID-to-link mapping negotiation
By default, all TIDs map to all setup links
  Also applies when no explicit TID-to-link mapping is negotiated
  It is optional for an MLD to support TID-to-link mapping negotiation
When TID-to-link mapping is supported by both MLDs, the AP MLD can initiate a TID-to-link mapping negotiation
  AP MLD considers non-AP MLD’s capabilities such as MLSR
    E.g., in case of MLSR, all TIDs are mapped to all setup links
  AP MLD has the global view and considers BSS-wide conditions such as traffic profiles (e.g., latency sensitive flows) and load on each link to make mapping decisions for each STA
    All clients are expected to benefit from such mapping
A non-AP MLD is recommended to accept AP’s proposal
  A non-AP MLD provides its capabilities and constraints during ML Setup phase
  A non-AP MLD can suggest its desired mapping for the AP MLD to consider
  A non-AP MLD can teardown the negotiated mapping if local conditions change

## Slide 5: Summary
In summary we propose a simplified TID-to-link mapping negotiation scheme where:
  A non-AP MLD can suggest its preferred TID-to-link mapping
  An AP MLD considers TID-to-link mapping suggested by the non-AP MLDs, traffic profiles and constraints of non-AP MLDs
  An AP MLD initiates a TID-to-link mapping for the links that are setup between the MLDs
The mechanism fits well with existing and upcoming features
  Blends well with existing power-save schemes, link setup/teardown procedures etc
    Including proposals on BU indication for each TID

## Slide 6: SP #1
Do you agree in R1:
  An MLD may initiate a TID-to-link mapping negotiation with an associated MLD that supports TID-to-link mapping by sending an individually addressed request frame
    The proposed TID-to-link mapping is established if the responding MLD responds with a response frame indicating ACCEPT
    A multi-link multi-radio (MLMR) non-AP MLD should accept AP MLD’s proposed TID-to-link mapping by responding with an individually addressed response frame indicating ACCEPT
    An MLD may suggest a TID-to-link mapping by transmitting an individually addressed frame indicating SUGGEST
    An MLD may teardown a negotiated TID-to-link mapping by sending an individually addressed teardown frame