## Slide 1: Protected TWT Enhancement for Latency Sensitive Traffic
Date: 2020-07-29
Name | Affiliations | Address | Phone | email
Chunyu Hu | Facebook Inc. | 1 Hacker way Menlo Park, CA |  | chunyuhu@fb.com
Payam Torab |  |  |  | torab@ieee.org
George Cherian | Qualcomm Inc. | 5665 Morehouse Dr, San Diego CA 92131 |  | gcherian@qti.qualcomm.com
Duncan Ho |  |  |  | dho@qti.qualcomm.com

## Slide 2: Abstract
Discuss a solution in R1 timeline based on protected TWT to provide latency sensitive traffic more predictable latency performance

## Slide 3: Background
11-20/1045 proposed a general channel access that provides a more predictable latency performance to latency sensitive traffic
  Can work with TWT/U-APSD for power saving gain
This contribution discusses an approach in R1 timeline based on protected TWT
  Intending to leveraging existing support in meeting timeline
  Trade off with some flexibility
Time Slot structure
pEDCA
TWT
+
U-APSD e.g.
+
11-20/1045
Proposing in R1:
Protected TWT
Channel access protection
Signaling (advertising, req/resp etc.)

## Slide 4: TWT Revisit
TWT is a mechanism where a set of Service Periods (SPs) are defined and shared between AP and non-AP STAs to reduce medium contention and improve the power efficiency of STAs.
TWT provides a periodic operation (implicit TWT) suiting periodic traffic
Broadcast TWT: AP can schedule TWT SP(s) with supporting STAs and shares schedule info in Beacon frames
  Reduced negotiation overhead compared to individual TWT, but further reduction of signaling overhead can be considered
  Information is shared on per TWT flow basis
Individual TWT: A protection mode using a NAV protection mechanism to protect medium access of TWT SP
  The session info is not shared in the beacon
TWT is associated with a STA but not associated with a traffic class (TID or AC)
TWT is defined for AP/STA pairs or TDLS peers
Notes: Individual TWT can be set up between STAs / TDLS case
Bcast TWT has to be between AP/STAs per 11ax
26.8.2 Individual TWT agreements
— May set the TWT Protection field to 1 to indicate that TXOPs within the TWT SPs shall be initiated
with a NAV protection mechanism, such as (MU) RTS/CTS, or CTS-to-self frame; otherwise it shall
set it to 0.
— An HE STA shall not use the RAW mechanism for protection of TWT SPs.

## Slide 5: Re-Cap: Latency Sensitive Traffic Characteristics
A latency sensitive traffic stream can be characterized by the following parameterized model:
  Bursty, periodic
  Traffic amount varies driven by application (e.g. compression) in addition to wireless medium dynamics
An application may contain multiple such streams of different parameters
Tethered link is a common design to balance computation power, network bandwidth and latency
  Require support of peer-to-peer communication
XR System Paradigms
Example:

## Slide 6: Proposal Summary
Enhance channel access protection for TWT SP
Extend the concept of protected individual TWT to Broadcast TWT
Extend the usage of Broadcast TWT signaling for protected SPs
Extend the usage of TWT for low latency peer-to-peer communication
Define support allowing associating TIDs with a TWT flow

## Slide 7: Protected TWT
Existing Protected TWT: TXOPs within TWT SPs shall be initiated with a NAV protection mechanism, such as (MU) RTS/CTS, or CTS-to-self frame. Under this rule:
  SP start time may vary if previous transmission didn’t finish
     resulting in unpredictability of delay jitter
Proposed additional rule: TXOP shall stop before a protected TWT SP starts
  Provide a more predictable latency performance: reduce jitter
  Reduce wake-up time: additional power saving
Example:
Notes: cts-2-self
Trigger
Let other STA(s) to tx on themselves. We can avoid that.
P2p: softAP / GO they send trigger.

## Slide 8: NAV Rules for Allowing Member STAs to Tx
Current limitation: Per the current NAV rules, only the TXOP owner is allowed to transmit
  But we want to allow the member STAs to be able to transmit in the TXOP
Proposed modification:
  Introduce a special MAC address to allow UL transmissions from more than one STAs in a TXOP reserved by the AP
    With the special MAC address that is assigned to a group of STAs (group, by the virtue that the set of STAs that joined a particular protected TWT), any of the STAs that are part of the group will be able to transmit
  For example, a CTS sent with the RA set to this special MAC address
    Format of this special MAC address can be further discussed

## Slide 9: Extension to Support Latency Sensitive P2P Traffic
Proposed extensions of TWT:
  AP shall be able to protect an SP for P2P LS traffic who are the members of the protected TWT session (e.g., between two TDLS peers)
  Using CTS-2-self as follows is a recommended mechanism
Example:
Notes: cts-2-self
Trigger
Let other STA(s) to tx on themselves. We can avoid that.
P2p: softAP / GO they send trigger.

## Slide 10: TWT Protection Field
802.11ax D6.1 has defined:
  Individual TWT:
  Broadcast TWT
Propose: change bit-15 of the Request Type field to be <TWT Protection>, same as for Individual TWT

## Slide 11: What else is Needed?
A STA needs to learn the protected broadcast TWT sessions
  => The AP shall include sufficient info of these TWT sessions in the Beacon/Probe Response
A STA shall include its own traffic and QoS requirement when requesting for a TWT session
  => This allows the AP to perform admission control (accept/reject the request) and update its scheduling
To avoid abuse by the STAs, the AP shall announce a policy
  That limits the type of traffic that it can accept for the protected TWT sessions, and/or
  Limits the amount of time allocated to each and total protected TWT sessions.
Notes: cts-2-self
Trigger
Let other STA(s) to tx on themselves. We can avoid that.
P2p: softAP / GO they send trigger.

## Slide 12: SP #1
Do you agree to add to the TGbe SFD (in R1), a mode where an AP shall be able to announce protected TWT session(s) such that:
  A STA carrying latency sensitive traffic may choose to join the protected TWT session
  Any STA that accesses the medium shall end its TXOP before the start of the protected SP
Notes: (verbal discussion: rest following existing protection rules.)

## Slide 13: SP #2
Do you agree to add to the TGbe SFD (in R1):
  Within a protected TWT SP, a STA that is a member of the TWT session shall be able to access the medium within this SP through one of the following means:
    As a triggered PPDU sent in response to a trigger frame
    An SU PPDU using EDCA
Notes: Discussion:
This is more a clarification. It extends to the second bullet.

## Slide 14: SP #3
Do you agree that the TGbe SFD shall include (in R1) the support of protected TWT in Broadcast TWT as described below:
  Change the Reserved bit in Figure 9-688a as in 802.11ax D6.1 to TWT Protection

## Slide 15: SP #4
Do you agree to add to the TGbe SFD (in R1):
  The definition and usage of a special MAC address to indicate a group of STAs that are part of a TWT session, identified by <MAC address, TWT indicator>
    Format TBD
  Note: the TWT session could be broadcast or individual

## Slide 16: SP #5
Do you agree that the TGbe SFD shall add (in R1):
  A TBD signaling procedure to associate a protected TWT session with indicated TID(s)
  Another TBD signaling procedure to associate the TCLAS with the TID

## Slide 17: SP #6
Do you agree that the TGbe SFD shall add support that (in R1):
  An AP shall include sufficient information (detailed Signaling TBD) of the protected TWT sessions in the Beacon and Probe Response for a STA to:
    Understand the SP start boundary
    Decide whether to join such a TWT session

## Slide 18: SP #7
Do you agree to add to the TGbe SFD (in R1):
  An AP shall be able to announce protected TWT session(s) that are for P2P STAs such that:
    Only P2P STAs that are member of the TWT session can access the medium

## Slide 19: SP #8
Do you agree to add to the TGbe SFD (in R1):
  An AP shall be able to announce a policy for admitting a STA into a protected TWT session
  Note: may need to define a new term for the protected TWT session with additional access rules as described in this document

## Slide 20: SP #9
Do you agree to add to the TGbe SFD (in R1) the following:
  A STA shall include its traffic and QoS requirements (e.g., latency delay tolerance, throughput needs, periodicity, offset, etc.) when requesting for a protected TWT session