## Slide 1: EHT BSS Follow Up: EHT (BSS) Operating Parameter Update
Date: 2020-04-01
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: VHT/HE Operating Parameter Update
Operating Mode Notification element is used for VHT operating parameter change.
  Operating Mode Notification element also changes the HE operating parameters.
OM Control field is used for HE operating parameter change.
  OM Control field also changes the VHT operating parameters.
VHT BSS BW is not more than 160/80+80MHz.
HE BSS BW in 5/6GHz band is not more than 160/80+80MHz. HE BSS in 2.4GHz band is no more than 40MHz.
VHT MCS can’t use more than 256QAM.
HE MCS can’t use more than 1024 QAM.
Operating Mode Notification element
Operating Mode field
OM Control field

## Slide 3: Recap: EHT BSS Assumption
EHT BSS BW is no more than 320/160+160MHz.
EHT MCS can’t use more than 2048 QAM.
An EHT AP can announce whole BSS operating BW change and/or Rx Nss change.
An EHT STA can announce its Rx/Tx Nss and/or BW change.

## Slide 4: EHT Operating Parameter Change through HE Control
Option 1: A new HE Control field (e.g. EHT OM Control) is used to announce the EHT Operating Parameter Change that includes (Note: HE OM Control can’t be used since the BW, MCS in HE OM Control are not enough):
  3-bit Rx BW (20, 40, 80, 160/80+80, 320/160+160 MHz),
  4-bit Rx Nss (1 to 16 SS): (option 1…. Nss at 80MHz, option 2…. Nss at the announced BW.)
  3-bit Tx BW (20, 40, 80, 160/80+80, 320/160+160 MHz),
  4-bit Tx Nsts (1 to 16 STS),
  1-bit UL MU Disable,
  1-bit UL MU Data Disable.
Option 2: An new HE Control field (e.g. Addition EHT OM Control) is used to announce the additional EHT Operating Parameter Change (>160MHz, >8Nss etc.)

## Slide 5: EHT Operating Parameter Change through IE
The reason for IE besides HE Control field
  This can be easily transmitted through broadcast frame, e.g. in Beacon, without having PPDU restriction.
    In 5/2.4GHz band, HE Control field is not allowed in legacy PPDU.
  By using Operating Mod Notification, multiple Action frames can be transmitted in short time to let the STAs receive the new parameters.
Method 1:
  Define a new element EHT Operating Mode Notification element (EHT Operating Mode Notification element):
    3-bit Rx BW that indicates 20. 40, 80, 160/80+80, 320/160+160 MHz,
    4-bit Rx Nss field that indicates Nss 1 to Nss 16.
    1-bit No LDPC,
    1-bit Rx Nss Type.
Method 2: Adding additional fields, i.e. EHT BW, EHT Rx Nss, to Operating Mode Notification element (Enhanced Operating Mode Notification element)
  This is preferable since Operating Mode Notification element is extensible element.

## Slide 6: SP 1
Do you support to announce the EHT operating mode through adding the additional fields (EHT BW, EHT Rx Nss) to Operating Mode Notification element?