## Slide 1: Consideration on compression mode in 11be
Date: 2020-08-xx
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Aug. 2020

## Slide 2: Introduction
Several contributions [1 ~ 3] have suggested the new compression mode in 11be by taking into account for either transmission(ex. SU or MU-MIMO) or preamble puncturing.
  The detailed definition of compressed mode is different for each contribution, but the three cases for compression mode are considered in common.
    Non-compressed mode (i.e., OFDMA transmission )
    Compressed mode for full bandwidth
    Compressed mode for punctured case
In this contribution, we investigate how to apply the compression mode regarding preamble punctured cases defined in the 11be SFD and discuss the related issues.

## Slide 3: Compression in 11ax
In 11ax, the signaling for compression is used for indication of Full bandwidth MU-MIMO transmission when MU-PPDU is sent.
  For indication of compression in 11ax, the HE-SIG-B compression subfield in HE-SIG-A is used. And, if this field is set to 1, it means that the common field in HE-SIG-B is not present because full bandwidth is used.
  Also, preamble puncturing is not supported when the HE-SIG-B Compression field is 1.
In addition, the HE-SIG-B Compression field in the HE-SIG-A can be used to indicate the SU transmission using HE MU-PPDU.
  For indicating one user transmission, the compression field is set to 1 and the Number Of HE-SIG-B Symbols Or MU-MIMO Users field in the HE-SIG-A is set to 0.
  Then the User Specific field consists of a single User Block field containing one User field.

## Slide 4: Consideration for compression in 11be (1/2)
In common, we agree that non-compressed mode is used for OFDMA transmission.
  And, the common field which includes the RU allocation subfield(s) are present in EHT-SIG.
while, regarding compressed mode, the additional compressed modes were discussed in the previous PHY conference call for supporting the various preamble puncturing per BW in 11be MU transmission.
However, we have already agreed that the information for various preamble puncturing per BW can be conveyed on U-SIG and/or EHT-SIG field to identify the preamble puncturing.
Therefore, as using this information, we can support the punctured BW MU-MIMO transmission enough without the definition of additional compressed mode.

## Slide 5: Consideration for compression in 11be (2/2)
For the 11be PPDU sent to multiple user, the compressed mode can be defined as following.
  Non-Compressed mode
    OFDMA transmission.
    The RU allocation subfield(s) in the common field for the EHT-SIG field is present.
  Compressed mode
    Full Bandwidth MU-MIMO transmission
    Punctured Bandwidth MU-MIMO transmission
    The RU allocation subfield in the common field for the EHT-SIG field is not present.
The subfield for the indication of compressed mode consists of 1bit and it can be included in U-SIG.

## Slide 6: SU/MU Indication (1/2)
Regarding SU transmission, followings are defined in 11be SFD.
  “The EHT PPDU sent to a single user has the EHT-SIG field.
  “There is STA-ID related information in the EHT PPDU preamble sent to a single user and multiple users.”
Due to the limitation of a room of U-SIG, U-SIG can not contain the all necessary information to interpret PPDU. So, some of that information should be included in EHT-SIG.
Thus, as explained above, the PPDU sent to a single user can be composed similar to the PPDU sent to multiple users.
In addition, by applying a similar indication way of 11ax, the 11be PPDU for multiple user transmission can be used for SU transmission without definition for a SU-PPDU.
Therefore, in 11be transmission, one PPDU type can be used for both SU and MU transmission.
Including the STA-ID related information

## Slide 7: SU/MU Indication (2/2)
A signaling such as 11ax can be considered to indicate the SU transmission when one PPDU type is used for SU and MU transmission.
  The indication of SU transmission.
    The compressed mode subfield* is set to 1.
    Unlike 11ax, a separated field for the indication of the number of MU-MIMO users is defined in the EHT-SIG field.
      The Number Of MU-MIMO Users field* in the EHT-SIG field of an EHT PPDU sent to multiple user is 0
        This indicates the 1 user similar to 11ax
  In addition, the RU allocation subfield is not present in EHT-SIG field.
It is desirable that a subfield indicating compressed mode is included in the U-SIG field because this field can also be used to identify the SU or MU transmission on one PPDU type.
* : The name of the field can be changed.

## Slide 8: PPDU Type field in U-SIG
For the indication of 11be PPDU, PPDU type subfield is included in U-SIG and, we defined the following two types of PPDU for 11be transmission in 11be SFD.
  One is the 11be PPDU sent to multiple users, i.e., MU-PPDU
  Another is TB-PPDU
As explained in previous slides, since by using the one PPDU type, we can support the both SU transmission and MU transmission, we don’t need to define the additional PPDU type for SU transmission.
In addition, since 11be must follow the rules for the low power indoor(i.e., LPI) operation to use the wide bandwidth in 6GHz, the DL/UL range can be reduced in 11be transmission due to the limitation of power.
So, in order to improve the DL/UL range in 11be, we can consider the additional transmission mode for range extension as described in [5].

## Slide 9: Summary
In the 11be transmission, the compressed mode is defined as two modes
  Non-compressed mode
    OFDMA transmission.
    The RU allocation subfield(s) in the common field for the EHT-SIG field is present.
  Compressed mode
    Full Bandwidth MU-MIMO transmission
    Punctured Bandwidth MU-MIMO transmission
    The RU allocation subfield in the common field for the EHT-SIG field is not present.
  For indicating of compressed mode, a specific field(ex. Compressed mode) is included in U-SIG and it consists of 1bit.
By using the one PPDU type(i.e., MU-PPDU), we can support both SU and MU transmission.
In addition, to support the range extension in 6GHz, an additional transmission mode can be considered in 11be.

## Slide 10: Straw Poll# 1
Do you agree that a subfield for indication of compressed mode is included in U-SIG as version dependent field?
  A subfield for the indication of compressed mode consists of 1bit.
  Y/N/A

## Slide 11: Straw Poll# 2
Do you agree that a subfield for the indication for the number of MU-MIMO users is included in EHT-SIG of EHT MU PPDU?
  Note : for the non-compressed mode, this field can be replaced with other information.
  Y/N/A

## Slide 12: Straw poll #3
Do you agree that for the identification of SU transmission, the indications for compressed mode and the number of MU-MIMO users are set to as follows?
  A subfield for compressed mode is set to 1.
  The number of MU-MIMO users is indicated as zero.
  Y/N/A

## Slide 13: Straw poll #4
Do you agree that a transmission mode for range extension is defined in 11be?
  Y/N/A

## Slide 14: Reference
[1] 11-20/049r1, PPDU Types and U-SIG Content
[2] 11-20/783r1, EHT-SIG Compression Format
[3] 11-20/829r0, EHT SIG Structure for Multi-user Support
[4] 11-20/566r35, compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document
[5] 11-20/0965r0, 6ghz-lpi-range-extension