## Slide 1: 4x EHT-LTFs Sequences Design
Date: 2020-07-12
Authors:
Name | Affiliations | Address | Phone | email
Chenchen Liu | Huawei Technologies Co., Ltd | Huawei Base, Bantian, Shenzhen |  | liuchenchen1@huawei.com
Dandan Liang |  |  |  | 
Bo Gong |  |  |  | 
Ming Gan |  |  |  | 
Yan Xin |  |  |  | 
Wei Lin |  |  |  | 

## Slide 2: Abstract
This contribution proposes 4x EHT-LTFs sequences for
320/160+160MHz.

## Slide 3: Introduction
In [1], the 320MHz/160+160MHz 4x EHT-LTF sequences has been proposed without considering the punctured 240MHz/160MHz+80MHz transmission.
In this contribution, the 320MHz/160+160MHz 4x EHT-LTF sequences are proposed considering the punctured 240MHz/160MHz+80MHz transmission.

## Slide 4: Introduction
 | 4x EHT-LTF Full bandwidth & PP & MRU Patterns |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RU size | RU26 | RU52 | RU26+RU52 | RU106 | RU26+RU106 | RU242 | RU484 | RU242+RU484 | RU996 | RU484+RU996 | RU2*996 | RU484+RU2*996 | RU 3*996 | RU3*996+RU484 | RU 4*996
Number of type considered | 36*4 | 16*4 | 4*4 | 8*4 | 4*4 | 4*4 | 2*4 | 4*4 | 1*4 | 4*2 | 2 | 2*6 | 4 | 8 | 1

## Slide 5: Design Methods
Option 1: Based on partial of 80MHz EHT-LTF [3-4]
For 4x, repeating 11ax 80MHz LTF sequences and apply the coefficient value on the first - fifth part of 80MHz LTF.
Option 2: New Sequences
Not using 11ax 80MHz 4x LTF sequences to construct the 320MHz/160+160MHz 4x LTF sequences.

## Slide 6: Sequences Design Considerations
Optimized the PAPR of all RU or aggregated RU size: page 4 & 5.
Single stream pilot impact [5]:
  Pilot position: passed SPs [2]
  P matrices:

## Slide 7: 320MHz 4x EHT-LTF
Option 1:
320MHz 4x EHT-LTF = [HE-LTF80MHz_part1_4x , HE-LTF80MHz_part2_4x , (-1)* HE-LTF80MHz_part3_4x , HE-LTF80MHz_part4_4x , (-1)* HE-LTF80MHz_part5_4x , 023 , (-1)* HE-LTF80MHz_part1_4x , HE-LTF80MHz_part2_4x , (-1)*HE-LTF80MHz_part3_4x , (-1)* HE-LTF80MHz_part4_4x , (-1)* HE-LTF80MHz_part5_4x , 023 , (-1)* HE-LTF80MHz_part1_4x , (-1)* HE-LTF80MHz_part2_4x , (-1)* HE-LTF80MHz_part3_4x , HE-LTF80MHz_part4_4x , (-1)* HE-LTF80MHz_part5_4x , 023 , (-1)* HE-LTF80MHz_part1_4x , HE-LTF80MHz_part2_4x , HE-LTF80MHz_part3_4x , HE-LTF80MHz_part4_4x , HE-LTF80MHz_part5_4x];
Where, Coefficient values = [1 1 -1 1 -1 -1 1 -1 -1 -1 -1 -1 -1 1 -1 -1 1 1 1 1],
HE-LTF80MHz_part1_4x =HE-LTF80M_4x (-500:-259),
HE-LTF80MHz_part2_4x =HE-LTF80M_4x (-258:-17),
HE-LTF80MHz_part3_4x =HE-LTF80M_4x (-16:16),
HE-LTF80MHz_part4_4x =HE-LTF80M_4x 17:258),
HE-LTF80MHz_part5_4x =HE-LTF80M_4x (259:500),

## Slide 8: 320MHz 4x EHT-LTF
Option 2A:
LTF320M_4x =
[ C(1)*LTF80M_4x_left, zeros(1,5), C(2)*LTF80M_4x_right, zeros(1,23), ...
C(3)*LTF80M_4x_left, zeros(1,5), C(4)*LTF80M_4x_right, zeros(1,23), ...
C(5)*LTF80M_4x_left, zeros(1,5), C(6)*LTF80M_4x_right, zeros(1,23), ...
C(7)*LTF80M_4x_left, zeros(1,5), C(8)*LTF80M_4x_right ];
where, C =[ 1 1 1 -1 -1 -1 -1 1], =[LTF80M_4x_left, zeros(1,5), LTF80M_4x_right]
LTF80M_4x_left =[+1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 +1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 +1 -1 +1 -1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 -1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 +1 -1 +1 +1 +1 +1 +1 +1 -1 +1 -1 -1 +1 -1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 +1 +1 +1 -1 +1 +1 -1 +1 +1 -1 -1 +1 +1 -1 -1 -1 -1 +1 +1 +1 +1 +1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 +1 -1 -1 -1 -1 -1 +1 -1 -1 -1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 +1 -1 -1 +1 +1 -1 -1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 +1 -1 +1 +1 -1 -1 -1 +1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 +1 +1 +1 +1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 -1 +1 +1 -1 -1 +1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 +1 +1 +1 -1 -1 -1 -1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 -1 +1 -1 -1]
LTF80M_4x_right =[ -1 -1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 +1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 +1 -1 -1 -1 +1 +1 -1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 +1 -1 +1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 -1 +1 +1 +1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 -1 -1 +1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 -1 +1 -1 +1 +1 -1 +1 +1 +1 +1 +1 -1 +1 +1 +1 -1 -1 +1 -1 +1 -1 +1 +1 +1 +1 +1 -1 -1 -1 +1 +1 -1 -1 -1 -1 -1 -1 -1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 +1 +1 +1 +1 +1 +1 +1 +1 -1 -1 -1 -1 +1 +1 -1 +1 -1 +1 -1 +1 -1 +1 -1 -1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 +1 -1 +1 +1 +1 -1 +1 -1 +1 +1 +1 -1 -1 -1 -1 -1 -1 +1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 +1 -1 +1 +1 -1 -1 +1 +1 -1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 +1 +1 -1 +1 +1 +1 -1 -1 +1 +1 +1 -1 +1 +1 -1 +1 +1 +1 +1 -1 ]

## Slide 9: 320MHz 4x EHT-LTF
Option 2B:
LTF320M_4x =
[ C(1)*LTF80M_4x_left, zeros(1,5), C(2)*LTF80M_4x_right, zeros(1,23), ...
C(3)*LTF80M_4x_left, zeros(1,5), C(4)*LTF80M_4x_right, zeros(1,23), ...
C(5)*LTF80M_4x_left, zeros(1,5), C(6)*LTF80M_4x_right, zeros(1,23), ...
C(7)*LTF80M_4x_left, zeros(1,5), C(8)*LTF80M_4x_right ];
where, C =[ 1 1 1 -1 1 1 -1 1], =[LTF80M_4x_left, zeros(1,5), LTF80M_4x_right]
LTF80M_4x_left =[-1 -1 -1 +1 +1 -1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 +1 -1 +1 +1 +1 -1 -1 -1 +1 -1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 -1 +1 +1 -1 -1 -1 +1 +1 -1 -1 -1 -1 -1 +1 +1 +1 -1 +1 -1 +1 -1 +1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 -1 +1 +1 -1 +1 +1 -1 +1 -1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 -1 +1 +1 +1 +1 -1 -1 +1 -1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 +1 -1 -1 +1 -1 +1 -1 -1 +1 -1 -1 -1 -1 -1 -1 -1 +1 +1 +1 -1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 +1 +1 +1 +1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 -1 -1 +1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 +1 +1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 -1 -1 -1 -1 -1 -1 -1 +1 -1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 +1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 -1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 -1 +1 -1 -1 -1 -1 -1 -1 -1 +1 +1 -1 -1 +1 +1 -1 +1 +1 +1 +1 +1 -1 -1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 -1 -1 +1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 +1 +1 +1 +1 -1 -1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 -1 -1 +1 -1 +1 +1 +1 -1 -1 -1 +1 -1 +1 -1 +1 +1 +1 +1 +1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 -1 +1 +1 +1 +1 ]
LTF80M_4x_right =[ +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 +1 +1 +1 -1 +1 -1 -1 +1 -1 +1 +1 -1 -1 -1 +1 -1 +1 +1 +1 +1 +1 +1 +1 -1 -1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 +1 -1 -1 +1 -1 +1 +1 +1 +1 +1 -1 -1 +1 -1 +1 -1 +1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 +1 +1 -1 -1 -1 -1 -1 -1 -1 +1 -1 +1 -1 +1 -1 +1 +1 +1 -1 -1 +1 -1 +1 +1 -1 +1 +1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 -1 +1 +1 +1 +1 -1 -1 +1 -1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 +1 -1 -1 +1 -1 +1 -1 -1 +1 -1 -1 -1 -1 -1 -1 -1 +1 +1 +1 -1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 +1 +1 +1 +1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 -1 -1 -1 -1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 +1 -1 -1 -1 +1 +1 +1 +1 +1 +1 +1 -1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 -1 -1 +1 +1 -1 +1 -1 +1 -1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 -1 +1 +1 +1 +1 -1 +1 +1 -1 +1 +1 +1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 +1 +1 -1 -1 +1 -1 -1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 +1 -1 +1 -1 -1 +1 -1 -1 +1 +1 -1 +1 +1 +1 +1 +1 -1 -1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 -1 -1 +1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 +1 +1 +1 +1 -1 -1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 -1 -1 +1 -1 +1 +1 +1 -1 -1 -1 +1 -1 +1 -1 +1 +1 +1 +1 +1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 ]

## Slide 10: New Sequences Simulation Results:
Multi-RU PAPR for Nss = 1 to 8
RU size | BPSK | LTF Opt1 | LTF Opt2A | LTF Opt2B
996 | 8.84 | 8.33 | 5.87 | 5.61
 |  | 8.01 | 5.89 | 5.8
 |  | 8.52 | 5.87 | 5.61
 |  | 8.52 | 5.89 | 5.8
996 + 484 | 9.17 | 8.21 | 7.57 | 8.0
 |  | 8.59 | 7.9 | 7.76
 |  | 8.23 | 7.7 | 7.84
 |  | 7.74 | 7.66 | 7.43
 |  | 8.54 | 7.57 | 7.92
 |  | 7.71 | 7.9 | 7.88
 |  | 8.13 | 7.7 | 7.69
 |  | 8.57 | 7.66 | 7.67
2*996 | 9.27 | 8.03 | 6.17 | 6.03
 |  | 8.61 | 6.17 | 5.82
3*996 (puncture 80MHz) | 9.54 | 8.17 | 7.83 | 8.02
 |  | 8.08 | 8.15 | 7.78
 |  | 7.67 | 7.83 | 7.75
 |  | 7.52 | 8.15 | 7.91
3*996 + 484 (puncture 40MHz) | 9.55 | 8.93 | 8.3 | 7.54
 |  | 8.65 | 8.34 | 7.59
 |  | 8.55 | 8.24 | 8.12
 |  | 8.59 | 8.18 | 7.94
 |  | 9.10 | 8.24 | 7.21
 |  | 8.86 | 8.17 | 7.14
 |  | 8.71 | 8.28 | 8.17
 |  | 8.52 | 8.33 | 8.05
4*996 | 9.60 | 8.15 | 8.44 | 6.07
RU size | BPSK | LTF Opt1 | LTF Opt2A | LTF Opt2B
2*996 + 484 | 9.50 | 9.34 | 7.05 | 8.18
 |  | 8.94 | 7.21 | 8.07
 |  | 8.24 | 8.3 | 9.25
 |  | 8.48 | 8.17 | 9.24
 |  | 8.98 | 7.01 | 8.18
 |  | 9.33 | 7.23 | 8.07
 |  | 9.06 | 6.87 | 7.39
 |  | 8.77 | 7.12 | 7.27
 |  | 8.66 | 8.47 | 8.36
 |  | 8.60 | 8.4 | 8.52
 |  | 8.70 | 6.89 | 7.32
 |  | 9.29 | 6.98 | 7.21

## Slide 11: New Sequences Simulation Results:
Worst case PAPR for Nss = 1 to 8
Sequence | BPSK Median | LGE HE based | LGE New Seq | BRCM | Opt1 Huawei | Opt2A Huawei | Opt2B Huawei
RU26 | 5.89 | 6.13 | 3.78 | 4.01 | 7.29 | 4.2 | 4.17
RU52 | 6.71 | 7.6 | 4.63 | 5.20 | 8.48 | 4.64 | 4.62
RU52 + RU26 | 7.10 | 6.29 | 6.29 | 6.82 | 6.90 | 5.99 | 5.37
RU106 | 7.29 | 6.15 | 5.54 | 4.90 | 7.21 | 4.90 | 4.98
RU106 + RU26 | 7.44 | 6.42 | 6.41 | 6.08 | 7.47 | 5.76 | 5.72
RU242 | 7.94 | 7.83 | 5.6 | 5.49 | 7.08 | 5.42 | 5.45
RU484 | 8.44 | 7.46 | 8.03 | 6.38 | 7.57 | 5.71 | 5.79
RU484 + RU242 | 8.83 | 8.97 | 8.35 | 8.44 | 8.79 | 7.85 | 7.95
RU996 | 8.84 | 8.47 | 7.74 | 6.78 | 8.52 | 5.89 | 5.8
RU996 + RU484 | 9.17 | 8.78 | 8.64 | 8.70 | 8.59 | 7.9 | 8.0
RU2*996 | 9.27 | 8.52 | 7.63 | 7.07 | 8.61 | 6.17 | 6.03
RU2*996 + RU484 | 9.50 | 9.09 | 8.97 | 8.72 | 9.34 | 8.47 | 9.25
RU3*996 | 9.54 | 8.48 | 8.39 | 7.97 | 8.17 | 8.15 | 8.02
RU3*996 + RU484 | 9.55 | 9.09 | 8.68 | 8.61 | 9.10 | 8.34 | 8.17
RU4*996 | 9.60 | 8.79 | 8.40 | 7.75 | 8.15 | 8.44 | 6.07

## Slide 12: Conclusion
In this contribution, 4x EHT-LTF sequences in
320MHz/160+160 transmission are proposed.

## Slide 13: Reference
[1]Dandan Liang, et al, <EHT-LTFs Sequences Design>, IEEE 802.11-20/0926r0
[2]Edward Au, <IEEE P802.11 Wireless LANs>, IEEE 802.11-20/0566r29
[3] <802.11ax Draft>, D6.0.
[4] Jinyoung Chun, et al, <EHT-LTF sequences in new tone plan>, IEEE 802.11-20/825r1
[5] Le Liu, et al, <HE-LTF Sequence Design>, IEEE 802.11-15/1334

## Slide 14: Straw Poll 1
Do you support to add to SFD：320MHz/160+160MHz 4x EHT-LTF sequences(Opt 2A in slides 8):
LTF320M_4x =
[ C(1)*LTF80M_4x_left, zeros(1,5), C(2)*LTF80M_4x_right, zeros(1,23), ...
C(3)*LTF80M_4x_left, zeros(1,5), C(4)*LTF80M_4x_right, zeros(1,23), ...
C(5)*LTF80M_4x_left, zeros(1,5), C(6)*LTF80M_4x_right, zeros(1,23), ...
C(7)*LTF80M_4x_left, zeros(1,5), C(8)*LTF80M_4x_right ];
where, C =[ 1 1 1 -1 -1 -1 -1 1]
LTF80M_4x_left =[+1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 +1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 +1 -1 +1 -1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 -1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 -1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 +1 -1 +1 +1 +1 +1 +1 +1 -1 +1 -1 -1 +1 -1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 +1 +1 +1 -1 +1 +1 -1 +1 +1 -1 -1 +1 +1 -1 -1 -1 -1 +1 +1 +1 +1 +1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 +1 -1 -1 -1 -1 -1 +1 -1 -1 -1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 +1 -1 -1 +1 +1 -1 -1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 +1 -1 +1 +1 -1 -1 -1 +1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 +1 +1 +1 +1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 -1 +1 +1 -1 -1 +1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 +1 +1 +1 -1 -1 -1 -1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 -1 +1 -1 -1]
LTF80M_4x_right =[ -1 -1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 -1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 +1 -1 +1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 +1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 +1 -1 -1 -1 +1 +1 -1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 +1 -1 +1 +1 +1 -1 -1 -1 +1 -1 -1 +1 +1 -1 +1 +1 +1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 -1 +1 +1 -1 -1 -1 +1 -1 -1 +1 -1 -1 +1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 -1 +1 -1 +1 +1 -1 +1 +1 +1 +1 +1 -1 +1 +1 +1 -1 -1 +1 -1 +1 -1 +1 +1 +1 +1 +1 -1 -1 -1 +1 +1 -1 -1 -1 -1 -1 -1 -1 -1 +1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 -1 +1 +1 -1 -1 +1 -1 -1 +1 -1 -1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 -1 -1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 +1 +1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 +1 +1 +1 +1 +1 +1 +1 +1 -1 -1 -1 -1 +1 +1 -1 +1 -1 +1 -1 +1 -1 +1 -1 -1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 +1 -1 +1 +1 +1 -1 +1 -1 +1 +1 +1 -1 -1 -1 -1 -1 -1 +1 -1 +1 -1 -1 -1 +1 -1 +1 -1 -1 +1 -1 +1 +1 -1 -1 +1 +1 -1 -1 -1 +1 +1 +1 -1 +1 +1 -1 -1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 -1 -1 -1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 +1 +1 -1 +1 +1 +1 -1 -1 +1 +1 +1 -1 +1 +1 -1 +1 +1 +1 +1 -1 ]