## Slide 1: STR capability signalling
Date: 2020-07-22
Authors:

## Slide 2: Abstract
Discusses how the STR capability can be signalled.

## Slide 3: Background (ML channel access)
The current 11be spec contains the following text about STR/NSTR multi-link channel access:
  “An MLD can indicate capability to support exchanging frames simultaneously by affiliated STAs on a set of links to another MLD in TBD capability field/element. The capability field/element indicates the MLD is a multi-radio MLD or other types of MLD. A multi-radio MLD operating on multiple links can announce whether it supports transmission on one link concurrent with reception on the other link for each pair of links, in which case the pair of link is STR or NSTR. The two links of each link pair are on different channels. “
  In this presentation we provide more details on the signaling related to above text.
Notes: 1. Check MTk contrib.. :

## Slide 4: Background (ML capability signaling)
Current agreement on MLD-level information sharing:
  New “ML element”: A new element will be defined as a container to advertise and exchange capability information for multi-link setup.
  Common and per STA info in ML element: Do you support that an STA of an MLD can provide MLD-level information that is common to all STAs affiliated with the MLD and per-link information that is specific to the STA on each link in management frames during multi-link setup?
    The specific information is TBD [#SP65]
  Do you agree to define mechanism(s) to include MLO information that a STA of an MLD provides in its mgmt. frames, during discovery and ML setup, as described below?
    MLD (common) Information
      Information common to all the STAs of the MLD
    Per-link information
      Capabilities and Operational parameter of other STAs of the MLD other than the advertising STA [#SP91]

## Slide 5: Assumption:
ML element contains signaling (explicit or implicit) about the number of STA profiles (N).
    For example, a single non-AP radio STA that tries to set up ML with a tri-band AP, N =3.
Some pair of links are always assumed to be STR in spec (e.g., one link in 2.4 GHz band and one in 5 GHz) and hence don’t need to be signaled.

## Slide 6: Proposal
The common part of ML element shall contain a field signaling the number of links in which that MLD can exchange frames simultaneously (M).
  For example, for Single Radio MLDs, M = 1, for dual radio, M = 2
We propose that the default mechanism in 11be R1 for signaling STR/NSTR capability for a pair of links in a multi-radio MLD is through a bit-map signaling.

## Slide 7: Signaling of STR/NSTR capability
Option 1: signal as an MLD-level capability information within common part of the ML element that is only present if a MR MLD.
  Signal # of supportable links (M) can be used simultaneously (in STR/NSTR mode).
  Bit-map for each pair of links ( 1=> STR pair; 0 otherwise) when M > 1.
Element ID | Length | Element ID extension | MLD common Info | Information about STA-1 | … | Information about STA N
Other params | # of Supportable links (N) | # of simultaneous links (M) | STR capability bitmap
STR/Non-STR (links 1 &2)
STR capability bitmap when N =2 and M > 1
Bits: 1
STR/NSTR (links 1&2) | STR/NSTR (links 1&3) | STR/NSTR(links 2&3)
STR capability bitmap when N =3 and M > 1
Bits: 1 1 1
Notes: We can also consider a STR Capability Info element which could be scalable to more than 3 links but has a bit higher overhead.

## Slide 8: Signaling of STR capability (contd.)
Option 2: signal as an MLD-level capability information the # of supportable links but STA level information for individual pairs.
Element ID | Length | Element ID extension | MLD common Info | Information about STA-1 | … | Information about STA N
Other params | # of Supportable links (N) | # of simultaneous links (M)
Other params | STR/NSTR (links 1&2) | STR/NSTR (links 1&3)
Information about STA-1 when N =3 & M > 1 (similarly for STA-2,3).
Bits: x 1 1
MLD common Info
Other params | STR/NSTR (links 1&2)
Information about STA-1 when N =2 & M > 1 (similarly for STA-2).
Bits: x 1
Notes: Add an example clarifying linked/ other way to identify STA profile

## Slide 9: Signaling of STR capability (contd.)
Option 3: mixed mode between Option 1 & 2 where the bitmap signaling is inside STA-profile without duplication.
Element ID | Length | Element ID extension | MLD common Info | Information about STA-1 | … | Information about STA N
Other params | SR/MR | # of Supportable links (N) | # of simultaneous links (M)
Other params | STR/NSTR (links 1&2) | STR/NSTR (links 1&3)
N =3 & M > 1 case
Bits: x 1 1
MLD common Info
Bits: x 1 2 2
Information about STA-1.
Other params | STR/NSTR (links 2&3)
x 1 x
Information about STA-2.
Other params
Information about
STA-3.
Notes: Add an example clarifying linked/ other way to identify STA profile

## Slide 10: Comparison and Usage
Option 2 is preferable because even though it has slightly higher overhead, the parsing is easier.
At non-AP STA side,
  Probe Request does not contain STR Capability Info.
  Association Request contains STR Cap Info.

## Slide 11: EMLSR/EMLMR support
The draft 0.1 spec mentions that EMLSR and EMLMR capability are at MLD-level:
  “An MLD with dot11EHTEMLSROptionImplemented equal to true shall set the EMLSR mode subfield of the TBD Capabilities element, which is an MLD level capabilities element, to 1…”
  “An MLD with dot11EHTEMLMROptionImplemented equal to true shall set the EMLMR Support subfield of the TBD Capabilities element, which indicates MLD level capabilities, to 1..”;
We propose that since those two fields represent MLD-level information, the common part of the basic ML element shall contain them.

## Slide 12: Summary
Proposed bitmap to signal pairwise STR/NSTR capability of an MLD.
Signaling to be carried in the ML element during MLO Setup.

## Slide 13: SP 1
Do you agree to add the following to SFD:
the common info part of the basic ML element transmitted by a non-AP MLD in a (Re)Association Request frame shall include a field that indicates the maximum number of affiliated STAs in the non-AP MLD that support simultaneous exchange of data frames (n)
  a field value that corresponds to n=1 indicates that the non-AP MLD is a single radio MLD
  a field value that corresponds to n=2 or more indicates that the non-AP MLD is a multi-radio MLD ?

## Slide 14: SP 2
Do you agree to add the following to SFD:
The common part of the basic ML element transmitted by an MLD contains an EMLSR Mode subfield and an EMLMR Support subfield ?

## Slide 15: SP 3
Do you agree to add the following to SFD:
an MLMR non-AP MLD that has at least one NSTR pair of links shall include in the STA profiles of a basic ML element, a bitmap where each bit represents STR/NSTR capability for a pair of links containing this STA, otherwise it shall not include the bitmap?
  Note: some pair of links (e.g., one link in 2.4 GHz band and another in 5 GHz band) may be specified to be always STR in spec and not included in bitmap ?

## Slide 16: Definition of constrained MLO
The existing SFD text identifies simultaneous transmit/receive issue over a pair of links but not a clear definition of the constraints.
In this presentation (similar to that proposed in 081r3) we assume that a pair of links at an MLD is considered non-STR if transmission by the MLD in one link impairs its Receiver minimum input level sensitivity or CCA sensitivity on the other link; otherwise that pair is considered STR .
  The transmission may be assumed at max transmit power capability.
Note that this definition still allows potential STR operation by a non-STR pair of links depending on RSSI, MCS level etc.
  For example, Rx at MCS-4 may be possible but not Rx at MCS-13 during Tx on the other link.
Note: the signaling in this presentation is largely independent of this definition.
Notes: Instead of Receiver minimum input level should it be CCA sensitivity for primary 20 MHz channel ? The latter seems to be less conservative.

## Slide 17: Proposal (Contd.)
STR capability related submissions:
  Submission 0921r0 proposes an option to signal STR capability + cross-link interference estimate.
  Submission 0809r0 also proposes that a STA signals its leakage estimates to AP.
  Submission 1550r1 lists bit-wise signaling of pairwise STR capability as an option.
We believe that the default mechanism for R1 signaling STR/NSTR capability to be the bit-map signaling.

## Slide 18: 20/0226r5 (MLO Constraint Indication and Operating Mode, Sharan Naribole, Samsung)
Do you support the addition of the following text to TGbe SFD?
A non-AP MLD may update its ability to perform simultaneous transmission and reception on a pair of setup links after multi-link setup.
  This update for any pair of setup links can be announced by non-AP MLD on any enabled link.
NOTE – Specific signaling for update indication is TBD
NOTE - Limitations on dynamic updating is TBD
Y/N/A/No answer: 43/7/29/19