## Slide 1: Discussions on EHT Non-contiguous PPDU
Date: 2020-07-16
Authors:

## Slide 2: Introduction
11ac/ax defines PHY non-contiguous transmission of 80+80MHz based on dual-LO.
  PHY uses the same coding and modulation as 160MHz.
  Use the same BW bit to signal 160MHz/80+80MHz.
In 11be SFD, non-contiguous PHY modes are added by default for each large signal bandwidth
  Including 80+80MHz, 160+80MHz, 160+160MHz.
  The tone plan and MRU discussions only based on contiguous BW.
In this contribution, we discuss about 11be PPDU BW.
  Propose 11be PHY only defines PPDU modes with contiguous BW.

## Slide 3: Non-contiguous PHY transmission
5GHz band has limited contiguous 160MHz channels
  80+80MHz allow more flexibility in terms of 160MHz BSS setup.
The reality is: few 80+80 operating STA on the market.
  This mode is practically not used.
Dual-LO does not bring throughput gain:
  Split antennas to different 80MHz segments with half of Nsts support.
  The same peak PHY throughput as 80MHz with same number of antennas.
  Does not achieve multi-radio diversity gain:
    if P80 is busy, S80 cannot be used

## Slide 4: Example: 80+80MHz vs 160MHz
Use two antenna STA as the example.
  STA1: 80MHz (1ss) + 80MHz (1ss)
  STA2: 80MHz (2ss)
Peak throughput: STA1 = STA2
  STA2 has easier design with lower cost.
  To achieves the best throughput: 160MHz STA with 2ss support.
Same observations for 160+160MHz vs 320MHz.

## Slide 5: Example: 160+80MHz
Discussions on potential use of 160+80MHz in 5GHz band.
  For example, 2-antenna STA.
    STA 1: 160MHz 1ss + 80MHz 1ss.
    STA 2: 160MHz with 2ss
  STA 2 has higher peak throughput than STA1
    STA1 is not preferred in product design: extra cost with no benefits.
For 6GHz band,
  160+80MHz within 320MHz is part of 320MHz transmission.
  Other dis-joint 160+80MHz, same argument as 5GHz.

## Slide 6: 11be MLO
In addition, EHT defines multi-link operation (MLO).
  Separate MAC, independent EDCA.
  Support different modes: parallel Tx/Rx, simultaneous Tx/Tx, etc.
  Provides improved throughput and latency.
  Preferable design for multi-radio systems.
If both MLO and non-contiguous PHY modes defined, an 11be multi-radio STA may have many choices:
  Support MLO and contiguous PHY modes only
  Support non-contiguous PHY transmission only, but no MLO.
  Support both MLO and non-contiguous PHY transmission
  Unnecessary complexity.

## Slide 7: Proposal
Propose that EHT does NOT define PPDU with non-contiguous BW.
  Remove 80+80MHz, 160+80MHz, 160+160MHz PPDU.
Leave all non-contiguous cases to MLO.
Each link only transmits PPDU with contiguous BW.
Simplify spec development and product design.

## Slide 8: SP
Do you agree that 11be does NOT define PPDU with non-contiguous signal bandwidth?
  Non-contiguous signal bandwidth includes 80+80MHz, 160+80MHz or 160+160MHz.
Y
N
A