## Slide 1: Zero User RUs for Per-80MHz Resource Unit Allocation Signaling
Date: 2020-07-10
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek Inc. |  |  | jianhan.liu@mediatek.com
Shengquan Hu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2
To reduce the length of EHT SIG, per-80MHz preamble signaling is preferred.
  U-SIG only duplicates within each 80MHz
  EHT-SIG can keep 2 content channels or 4 content channels
This implies that each STA must know in which 80MHz its content channels are located before receive this EHT PPDU.
  Each STA only need to process the preamble (including STFs and LTFs) in one 80MHz.

## Slide 3: Goal
Enable per-80MHz RU signaling for OFDMA and MU-MIMO cases
  MU-MIMO including compression modes and non-compressed modes.
Enable per-80MHz RU signaling can enhance signaling efficiency.
  For example, it is desirable that each 80MHz only contains only 4 user fields only for the following case:
    Totally 16 users on 320MHz;
    4 users parked in each 80MHz;

## Slide 4: Per-80MHz EHT Signaling for OFDMA
Using zero user RU in the RU allocation subfield instead of using spoofing user field for users not parked in the corresponding 80MHz.
  Zero user RU: 9bits v.s. Spoofing user field:23 bits

## Slide 5: Discussion on zero user RU
Using zero user RU as a place holder of RU allocation field and enabling efficient per-80MHz signaling.
  Although only using zero user RU242 can work for the aforementioned purpose, we prefer to also add zero user RU484 and zero user RU996 for two reasons:
    1. Consistent with to 11ax. In 11ax, the RU allocation subfield table already has zero-user RU242/484/996.
    2. Zero user RU242/484/996 all have their physical meaning and in some scenarios convey more precise information on RU allocations.
      Note that punctured RU which can be RU242,484, 996.
Given that zero user RU242 has been already adopted in 11be SFD, we propose to add zero user RU484 and zero user RU996 to the RU allocation table.

## Slide 6: Per-80MHz RU Signaling for MU-MIMO
Using the 6-bit expanded Spatial Configuration subfield encoding.
  For MU-MIMO (both full-bandwidth MU-MIMO in the compression modes or hybrid MU-MIMO and OFDMA modes), fill the user fields for users not parked in the given 80MHz for MU-MIMO.

## Slide 7: Straw Poll #1
  Do you agree to add zero user RU484 and zero user RU996 to 11be RU allocation subfield?
    Note use zero user RU can be used in the RU allocation field for the users operates on other 80MHz sub-channels in OFDMA.