## Slide 1: MLO-Probe Mechanism
Date: 2020-11-01
Authors:

## Slide 2: Background
We agree to define a mechanism for a STA of a non-AP MLD to send a probe request frame to an AP belonging to an AP MLD, which enables to request a probe response from the AP that includes the complete set of capabilities, parameters and operation elements of other APs affiliated to the same MLD as the AP
  The complete information is defined as all elements that would be provided if the reported AP was transmitting that same frame (exceptions TBD)
  ML element with “ML Probe request” [1] could be used for this mechanism
  A few contributions [2] [3] and [4] have touched the design for ML Probe mechanism
In this contribution, we discuss the Probe mechanism related to AP MLD from legacy support

## Slide 3: ML Probe
In [4], it proposed to use new element to solicit the info of a few APs or all the APs in an AP MLD as follows
However in [2], it proposes to reuse ML element to solicit the above info
All of them need a new element, changing the frame format of the Probe Response frame
 | Element ID | Length | Number Of Link ID Fields | Link ID
Octets: | 1 | 1 | 1 | Variable
Frame Control
Duration
A1
A2
A3
Sequence Control
HT Control
……
Multi-Link Element
……
FCS
Probe Request Frame

## Slide 4: Regular Probe
  Like Multiple BSSID feature, we propose that the AP could respond the Probe Response frame on behalf of the solicited AP that is in the same AP MLD
  In Multiple BSSID set, transmitted BSSID responds with a Probe Response frame instead of the solicited non-tx BSSID
  This mechanism could reuse the regular Probe Request frame to solicit the info of any single AP in an AP MLD.

## Slide 5: Regular Probe
We propose a STA that receives a Probe Request frame shall not respond if any of the following apply:
b)The Address 1 field of the Probe Request frame contains an individual address and one of the following criteria is met:
  1) The STA is not a member of a multiple BSSID set, and the individual address is not the MAC address of the STA.
  2) The STA is a member of a multiple BSSID set, and the individual address does not match the BSSID of any of the BSSs in the multiple BSSID set.
  3) The STA is affiliated with a MLD, and the individual address does not match the MAC address of any of the APs in the MLD
  …
Otherwise, the STA that receives a Probe Request frame shall respond with a Probe Response frame

## Slide 6: Regular Probe
We propose a STA that receives a Probe Request frame shall not respond if any of the following apply:
h) The STA is not a mesh STA and the Address 3 field of the Probe Request frame does not contain a wildcard BSSID and one of the following criteria is met:
  1) The STA is not a member of a multiple BSSID set and the Address 3 field of the Probe Request frame does not match the BSSID of the STA’s BSS(#2599).
  2) The STA is a member of a multiple BSSID set and the Address 3 field of the Probe Request frame does not match the BSSID of any of the BSSs in the multiple BSSID set.
  3) The STA is affiliated with a MLD, and the Address 3 field of the Probe Request frame does not match the BSSID of any of the BSSs in the MLD
  ….
  Otherwise, the STA that receives a Probe Request frame shall respond with a Probe Response frame

## Slide 7: Example
An individual addressed Probe Request frame is sent on 2.4 GHz to solicit the info of another AP (AP 2)
  This individual addressed Probe Request frame is sent by a legacy STA or an EHT STA in a non-AP MLD
  An AP in an AP MLD shall provide the info of another AP in the same AP MLD when it receives the Probe Request that solicits the info of that AP （AP 2）
AP1/ 2.4G
AP2/ 5G
AP3/ 6G
Legacy STA or EHT STA in non-AP MLD
The regular Probe Request frame that solicits the info of AP2, the RA is set to AP’s address
The Probe Response frame frame that providing the info of AP2

## Slide 8: Discussion
EHT STA can could reuse the regular Probe Request to solicit the info of single AP in the AP MLD for the following cases
  Switch one link to another link
  A change to the value of CSN of single AP in the AP MLD
  Request partial info of single AP in the AP MLD, no any change to the Regular Probe Request since it already carries Request Element…
Moreover, the typical case is dual band MLD especial for non-AP MLD, so probing the info of single AP is also typical since the info of transmitting AP could be obtained by the Beacon or unsolicited Probe Response
Besides soliciting the info of single AP in an AP MLD by EHT STA, this Regular Probe Request could also be used for legacy support
  RNR becomes a very important tool for an AP or AP MLD discovery mechanism
  Although the new field like MLD Parameter is added, legacy STAs (like HE STA) can still parse the RNR element correctly, i.e., it could get enough info based on the first 13 octets in TBTT info field of RNR element
  In this way, legacy STAs could reuse regular Probe Request to find a proper AP among the APs in the AP MLD that is provided in RNR element
 | Neighbor AP TBTT Offset | BSSID (optional) | Short-SSID (optional) | BSS parameters | 20 MHz PSD | MLD parameters
Octets: | 1 | 0 or 6 | 0 or 4 | 0 or 1 | 0 or 1 | 0 or TBD

## Slide 9: Summary
In this contribution, we propose to reuse the regular Probe Request frame for ML Probe which could solicit the info of a single AP in an AP MLD
  This regular Probe Request frame could be used for legacy support.

## Slide 10: References
[1] 11-20-0772-05-00be-multi-link-element-format
[2] 11-20-1396-01-00be-multi-link-probe-request-design
[3] 11-20-1141-00-00be-restrictions-on-mld-probe
[4] 11-20-1255-00-00be-pdt-mac-mlo-discovery-discovery-procedures-including-probing-and-rnr

## Slide 11: SP 1
Do you agree to reuse the regular (non-ML) Probe Request frame to solicit the info of any single AP in an AP MLD?

## Slide 12: SP 2
Do you agree to reuse the regular (non-ML) Probe Request frame with either Address 1 field or Address 3 field set to the MAC address of an AP in an AP MLD to solicit the info of that AP in the AP MLD?