## Slide 1: Remaining TBDs on DCM
Date: 2020-07-20
Authors:
Name | Affiliations | Address | Phone | Email
Bin Tian | Qualcomm |  |  | btian@qti.qualcomm.com
Sameer Vermani |  |  |  | 
Alice Chen |  |  |  | 
Lin Yang |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
It has been proposed in [1] that DCM+MCS0 will be supported in 11be for 1ss
In this presentation we want to resolve some TBDs related to the DCM transmissions

## Slide 3: New RU/M-RU Size to Define DCM
11ax defines DCM operation up to RU 996x2 (160 MHz)
Suggest 11be defining DCM on all RU and M-RU size <= 996x2 plus RU 996x3 and 996x4
  New M-RU size <= 80 MHz: RU78, RU132 and RU726
    Need to define interleaver/DTM
  New M-RU size > 80 MHz: RU 996+484, RU 996+(484+242), RU 996x2, RU996x3 and RU 996x4
    Need to define DCM operation and update segment parser

## Slide 4: Interleaver and DTM for RU/MRU < 80MHz
 | NSD |  | BCC NCOL |  | BCC NROT |  | LDPC DTM | 
 | No DCM | DCM | No DCM | DCM | No DCM | DCM | No DCM | DCM
RU26 | 24 | 12 | 8 | 4 | 2 | - | 1 | 1
RU52 | 48 | 24 | 16 | 8 | 11 | - | 3 | 1
RU78 | 72 | 36 | 18 | 12 | 18 | - | 4 | 3
RU106 | 102 | 51 | 17 | 17 | 29 | - | 6 | 3
RU132 | 126 | 63 | 21 | 21 | 31 | - | 6 | 3
RU242 | 234 | 117 | 26 | 13 | 58 | - | 9 | 9
RU484 | 468 | 234 | - | - | - | - | 12 | 9
RU726 | 702 | 351 | - | - | - | - | 18 | 9
RU996 | 980 | 490 | - | - | - | - | 20 | 14
Simulation results show the performance not sensitive to the parameter selection [2]

## Slide 5: DCM for RU996x2 in 11ax
For 996x2, NSD= 980 for DCM=1
In essence, DCM subcarriers mapping is limited within each 80 MHz segment

## Slide 6: DCM for New RU/M-RU size >996
New RU/M-RU size >996 to define DCM
  RU 996+484, RU996+(484+242), RU 3x996, RU4x996,
Propose
  Use segment parser to distribute bits to each segment
    Proportional round robin scheme
  Perform DCM mapping on the per 80MHz Nsd_k, k is the index of 80MHz segment
    E.g. for RU 996 +(484+242) , the Nsd_1, Nsd_2, can be 490, 351 with DCM=1

## Slide 7: BCC Per Symbol Padding
Just like for RU106 and RU242, NSD of RU132 is odd number for DCM case
  In 11be, DCM only applies to MCS0 and 1ss. It requires even number of coded bits per OFDM symbol
Same as in 11ax, one padding bit is added after 2 x NDBPS coded bit for RU132
 | NSD | 
 | No DCM | DCM
RU26 | 24 | 12
RU52 | 48 | 24
RU78 | 72 | 36
RU106 | 102 | 51
RU132 | 126 | 63
RU242 | 234 | 117
RU484 | 468 | 234
RU726 | 702 | 351
RU996 | 980 | 490

## Slide 8: SP 1
Do you support 11be to define DCM for RU/M-RU size <= 996x2 plus RU 996x3 and 996x4
Y/N/ABS

## Slide 9: SP 2
Do you agree with the following BCC interleaver and LDPC DTM parameters for DCM
Y/N/ABS
 | NSD |  | BCC NCOL |  | BCC NROT |  | LDPC DTM | 
 | No DCM | DCM | No DCM | DCM | No DCM | DCM | No DCM | DCM
RU78 | 72 | 36 | 18 | 12 | 18 | - | 4 | 3
RU132 | 126 | 63 | 21 | 21 | 31 | - | 6 | 3
RU726 | 702 | 351 | - | - | - | - | 18 | 9

## Slide 10: SP 3
Do you support the following DCM scheme for RU/M-RU size > 80 MHz
  Use segment parser to distribute coded bits to each 80MHz segment
  Within each 80MHz, perform DCM mapping using per 80MHz Nsd_k, k is the index of 80MHz segment
Y/N/ABS

## Slide 11: SP 4
Do you support one padding bit is added after 2 x NDBPS coded bit when BCC is used for RU132 with DCM?
Y/N/ABS

## Slide 12: References
[1] 11-20-0986r0 Jianhan et al. “DCM for range extension in 6GHz LPI”
[2] 11-20-0405r1 Eunsung Park et al “LDPC Tone Mapper for Multiple RU Aggregation”