## Slide 1: ML element design
Date: 2020-08-10
Authors:

## Slide 2: Background
802.11be defines mechanism(s) to include ML element that a STA of an MLD provides in its mgmt. frames, during discovery and ML setup, as described below[1]:
  MLD Level/Common Info
  Information common to all the STAs of the MLD.
  Per-link information
  Capabilities and Operational parameter of other STAs of the MLD other than the advertising STA.
 | Element ID | Length | Element ID Extension | Common Control | MLD Address | … | … | … | Optional Sub-elements
Octets: | 1 | 1 | 1 | 1 | 0 or 6 | … | … | … | variable
MLD Level/Common Info
Per-Link Info
Multiple Link element
MLD Addr Present

## Slide 3: Recap
During the discovery phase, an AP within an AP MLD should only include the MLD-level/common info field of the ML element in the Beacon or non-ML Probe Response frame
  The MLD-level/common info includes MLD MAC address and other TBD info
  During the multi-link set up phase, a STA in a MLD can provide a complete ML element
  MLD-level information that is common to all STAs in the same MLD
  and per-link information that is specific to the STA on each link in management frames
  Moreover, an AP in an AP MLD can provide a complete or partial ML element in the ML Probe Response frame as per the ML Probe Request frame
  An AP receives the ML Probe Request frame which solicits the info of specific AP within the target AP MLD
  An AP receives the ML Probe Request frame which solicits the info of the specific AP MLD

## Slide 4: ML element in discovery phase
To speed up the AP MLD discovery phase, an AP in an AP MLD shall advertise the ML related info for each AP in the same AP MLD and other collocated AP MLD, such as Link ID, ML ID and so on in [2] [3] and[4]
  Link ID is carried in TBTT info of the RNR element for a reported AP, which is used to identify this AP
  ML ID is also carried in the TBTT info of the RNR element for a reported AP , which is used to identify the AP MLD with which this AP is affiliated
However, the ML related info for both transmitting AP and nontransmitted BSSID is missing as mentioned in [2]
  RNR element does not contain the info for both transmitting AP and nontransmitted BSSID (exception case is not consider here)
  Moreover, the locations of Change Sequence field for both transmitting AP and nontransmitted BSSID are also TBD now

## Slide 5: ML element in discovery phase
We propose to carry transmitting AP info in the MLD-level/common info field of the ML element
  MLD-level/common info field includes both Link ID and Change sequence
  If the reported AP is nontranmitted BSSID and this reported AP is in an MLD, the MLD-level/common info field of the ML element carried in non-transmitted BSSID profile shall include both Link ID and Change sequence
 | Element ID | Length | Element ID Extension | Common Control | MLD Address | Transmitting AP Info | … | … | Optional Sub-elements
Octets: | 1 | 1 | 1 | 1 | 0 or 6 | TBD | … | … | variable
MLD Level/Common Info
Per-Link Info
Multiple Link element
MLD Addr Present
Link ID
Change Sequence

## Slide 6: ML element in discovery phase
  Regarding Link ID of transmitting AP, the other way is obtained by derivation based on the Link IDs of the other APs in the same MLD by assuming all Link IDs are contiguous
  If Link IDs of the other APs in the same MLD are contiguous, then the Link ID of transmitting AP is the largest value plus one or the minimum value minus one
  If Link IDs of the other APs in the same MLD are not contiguous, then the Link ID of transmitting AP is the one which could make Link IDs of the other APs contiguous
  However the above assumption can not work if allowing ML link reconfiguration for AP MLD (one link is removed) [5]
  Moreover, this assumption lacks of some flexibility

## Slide 7: ML element in ML Probe
Based on the received RNR element during the discovery phase, a STA within a non-AP MLD can send the ML Probe Request frame to solicit the info of any single AP MLD of the following
  An AP MLD which includes the recipient AP
  An AP MLD which contains the non-transmitted BSSID that in the same multiple BSSID set as the recipient AP
  An AP MLD for which there is no affiliated AP working on the same link as the recipient AP and there is at least one AP of the AP MLD is in the same multiple BSSID set as an AP affiliated with the AP MLD of the recipient AP
  Since the basic info of the above 3 kinds of AP MLD is carried in RNR element during the discovery phase, the above ML Probe Request frame could be complementary to the discovery phase such that to obtain full info
  No “switch” operation is needed

## Slide 8: ML element in ML Probe
  Moreover, the ML Probe Request frame can be used to solicit the info of one or more AP MLDs which are advertised during discovery phase
  The non-ML （regular） Probe response frame can be used to solicit the info of single AP within an AP MLD
  For example as shown in the below figure, AP1x in MLD 1 receives a Probe Request frame which solicits the info of one or more AP MLDs
  MLD 1, MLD 2, MLD3
  The solicited Probe Response frame may carry more than one ML element
  The ML element for MLD 1 as an independent element
  The ML element for MLD 2 as an independent element
  The ML element for MLD 2 as an sub-element of multiple BSSID element
  We propose extra indication to differentiate
  the ML element for MLD 1 from the ML element
  for MLD 2

## Slide 9: Summary
In this contribution, we propose to design ML element from aspect of discovery
  Include the info of transmitting AP in the MLD-level/common info field of the ML element, such as link ID and change sequence
  Moreover
  The ML Probe Request can be used to solicit the info of 3 kinds of AP MLDs which are advertised by discovery phase
  the ML Probe Response can carry more than one ML elements as per the received ML Probe Request

## Slide 10: References
[1] 11-20-0566-62-00be-Compendium of straw polls and
potential changes to the Specification Framework Document
[2] 11-20-0615-03-00be-Discovery mechanism for MLD
[3] 11-20-0389-00-00be-Multi-link discovery part 1
[4] 11-20-0390-00-00be-Multi-link discovery part 2
[5] 11-20-1554-04-00be-ml-reconfiguration

## Slide 11: SP 1
Do you agree to include the transmitting AP info to the ML element in R1
  The transmitting AP info contains both Link ID subfield and Change Sequence subfield

## Slide 12: SP 2
Do you agree that the ML Probe Request frame can be used to solicit the info of any single AP MLD of the following in R1
  An AP MLD which includes the recipient AP
  An AP MLD which contains the non-transmitted BSSID that in the same multiple BSSID set as the recipient AP
  An AP MLD for which there is no affiliated AP working on the same link as the recipient AP and there is at least one AP of the AP MLD is in the same multiple BSSID set as an AP affiliated with the AP MLD of the recipient AP