## Slide 1
Authors:
Multi-Link Reference Model Discussion
Date: 2020-07-29
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | 
Zhiqiang Han | ZTE |  |  | 
Liuming Lu | ZTE |  |  | 
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution discusses the reference model to support multi-link operation in IEEE802.11be, and proposes architecture reference models to support multi-link device.

## Slide 3: Baseline Architecture Reference Model [1]
Logical Entities
  MAC Sublayer and MAC Sublayer Management in Data Link Layer
  PHY Sublayer and PHY Sublayer Management in Physical layer
SAP
  MAC SAP: is the interface of MAC Sublayer to the upper layer (802.1X)
  MLME SAP: is the interface of MLME to Station Management Entity (SME)
  PLME SAP: is the interface of PLME to Station Management Entity (SME)

## Slide 4: 802.11be Framework
Multi-Link Operation
  In SFD [2], some Multi-link device (MLD) related text are as follows:
    A device that has more than one affiliated STA and has one MAC SAP to LLC, which includes one MAC data service.
      NOTE 1 – The device can be logical.
    AP multi-link device (AP MLD): A MLD, where each STA affiliated with the MLD is an AP.
    Non-AP multi-link device (non-AP MLD): A MLD, where each STA affiliated with the MLD is a non-AP STA.
    An STA of an MLD can provide MLD-level information that is common to all STAs affiliated with the MLD and per-link information that is specific to the STA on each link in management frames during multi-link setup.
    A MLD has a MAC address that singly identifies the MLD management entity.
      For example, the MAC address can be used in multi-link setup between a non-AP MLD and an AP MLD.

## Slide 5: 802.11be Reference Model
  MLD MAC Sublayer Issues
  In the 802.11 baseline reference model, a STA has one MAC Sublayer.
  As MLO introduces the concept of Multi-link device (MLD) that has more than one affiliated STA, the MLD has to interact to multiple affiliated STAs.
  Both the MLD and its affiliated STAs are logical entities. It needs to define a architecture reference model about the MLD and its affiliated STAs in MAC Sublayer as the MAC SAP is the common interface for the affiliated STAs.
  MLD MLME Issues
  A MLME is the logical entity to manage the operation of MAC Sublayer. The MLME provides an interface MLME SAP to allow the SME to control the MAC Sublayer management.
  As MLD is introduced, it needs to define the interface of MLME to control the MLD MAC Sublayer management. But it is missing in the SFD now.

## Slide 6: 802.11be Reference Model
General Consideration
  The MLD architecture reference model should consider to reuse and align with the 802.11 reference model in the baseline as much as possible.
  The MLD architecture reference model needs to consider to support the multiple AP MLD in DSS as the Multi-AP is also one of important features of 802.11be.

## Slide 7: Multi-Link Reference Model
Existing Multi-Band Reference Model
  The transparent FST Entity is similar to the ML reference model, but it only provides the session transmission between two STAs.
  It does not provides the functions described in 802.11be SFD, such as ML discovery, ML setup, TID-to-link mapping, STR/non-STR, etc.

## Slide 8: Proposals
MLD Reference Models
  Logical Entities
    Option 1
      MAC Common Entity: a common MAC control entity to the MAC sublayer of all affiliated STAs of MLD
      MAC sublayer: an MAC sublayer of an affiliated STA of MLD
      PHY layer: a physical layer of an affiliated STA of MLD
      MLME: a MAC sublayer management entity
      PLME: a PHY sublayer management entity
    Option 2
      MAC upper layer (MAC-U): a common part of MAC sublayer to all affiliated STAs of MLD
      MAC lower layer (MAC-L): an individual part of MAC sublayer of an affiliated STA of MLD
      PHY layer: a physical layer of an affiliated STA of MLD
      MLME: a MAC sublayer management entity
      PLME: a PHY sublayer management entity
    Common entities to both options
      SME: a station management entity
      Multi-Link SME Management Entity: coordination of SMEs for ML operation among affiliated STAs to the MLD
  Service Access Points
    MAC SAP: MAC data service interface and primitives to the LLC
    MLME SAP: MAC management interface and primitives to SME
    PLME SAP: PHY management interface and primitives to SME

## Slide 9: Proposals
MLD Reference Models – Option 1
  Revise the existing 802.11 reference model for ML reference model
  Define a Common MAC Entity and a Multi-Link SME Management Entity
802.1X
Common MAC Entity
PHY
SME
SME
MAC Sublayer
Management
Entity
PHY Sublayer
Management
Entity
Multi-link SME Management Entity
MAC sublayer
PHY
MAC sublayer
MAC Sublayer
Management
Entity
PHY Sublayer
Management
Entity
MAC-SAP
MLME-PLME SAP
PHY-SAP
PHY-SAP
MLME-PLME SAP
MLME- SAP
PLME- SAP
PLME- SAP
MLME- SAP
STA1
STA2
IEEE 802.1X
Authentication or Supplicant
RSNA Key Management

## Slide 10: Proposals
MLD Reference Models – Option 1
  Reuse the existing 802.11 protocol stacks for multi-link operation
    Note: some functions may need to be enhanced for multi-link.
  Define a Common MAC Entity to control the MLD related ML Functions
  Define a ML SME Management Entity to coordinate ML SMEs for the ML setup, configuration, time synchronization and scheduling of affiliated STAs to the MLD
Common MAC Entity

## Slide 11: Proposals
MLD Reference Models – Option 2
  Revise the existing 802.11 reference model for ML reference model
  Specify MAC-U and MAC-L
    Note: The primitives between MAC-U and MLME, MAC-L and MLME need be considered.
802.1X
MAC-U
PHY
SME
SME
MAC Sublayer
Management
Entity
PHY Sublayer
Management
Entity
Multi-link SME Management Entity
MAC-L
PHY
MAC-L
MAC Sublayer
Management
Entity
PHY Sublayer
Management
Entity
MAC-SAP
MLME-PLME SAP
PHY-SAP
PHY-SAP
MLME-PLME SAP
MLME- SAP
PLME- SAP
PLME- SAP
MLME- SAP
STA1
STA2
IEEE 802.1X
Authentication or Supplicant
RSNA Key Management

## Slide 12: Proposals
MLD Reference Models – Option 2
 | TX |  | RX | 
MAC-U | A-MSDU Aggregation |  | A-MSDU De-aggregation | 
 | PS Defer Queue |  | (null) | 
 | Sequence Number Assignment |  | (null) | 
 | MSDU Integrity Protection (optional) |  | MSDU Integrity Protection (optional) | 
 | Fragmentation |  | Defragmentation | 
 | Packet Number Assignment |  | Replay Detection (optional) | 
 | (null) |  | SYNRA Receiver Filtering | 
 | (null) |  | Block Ack Buffering and Reordering | 
 | MPDU Encryption and Integrity Protection |  | MPDU Decryption and Integrity Check | 
 | (null) |  | Duplicate Detection and Removal | 
MAC-L | TX1 | TX2 | RX1 | RX2
 | (null) | (null) | Block Ack Scoreboarding | Block Ack Scoreboarding
 | (null) | (null) | Address 1 Filtering | Address 1 Filtering
 | MPDU Header + CRC Creation | MPDU Header + CRC Creation | MPDU Header + CRC Validation | MPDU Header + CRC Validation
 | A-MPDU Aggregation | A-MPDU Aggregation | A-MPDU De-aggregation | A-MPDU De-aggregation

## Slide 13: Summary
This contribution
  Discussed the issues in the existing architecture reference model to support multi-link device logical entity.
  Proposed a multi-link architecture reference model for 802.11be.

## Slide 14: Straw Polls
SP1
  Do you support in SFD to reuse the existing MLME-SAP as the MLD MAC management interface and primitives to SME ?

## Slide 15: Straw Polls
SP2
  Do you support to include the MLD reference model in SFD R1 with a common MAC entity for managing the MAC sublayer of the MLD ?
    Note: this is relate to the option 1 shown in page 9

## Slide 16: Straw Polls
SP3
  Do you support to include the MLD reference model in SFD R1 with
    MAC upper layer (MAC-U): a common part of MAC sublayer of affiliated STAs of the MLD
    MAC lower layer (MAC-L): an individual part of MAC sublayer of an affiliated STA of the MLD
  Note:
    this is relate to the option 2 shown in page 11

## Slide 17: Straw Polls
SP4
  Do you support to include the MLD reference model in SFD R1 with
    Multi-Link SME Management Entity for the coordination of ML operation among affiliated STAs to the MLD.

## Slide 18: References
IEEE802.11-REVmd D3.4
11-20-0566-43-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document
11-20-0068-00-00be-multi-link and multi-ap reference-model discussion

## Slide 19
Thank you!

## Slide 20: Backup
MAC-U (MLD Level)
  MAC-SAP
  ML Setup procedure, ML capabilities, ML association state, MLD level information …
  Sequence Number
  BA agreement
  Same PMK and PTK across links
  Etc.
MAC-L (affiliated STA Level)
  MPDU Header
  A-MPDU
  Etc.
MAC-U
MAC-L