## Slide 1: Thoughts on Extended Range (ER) Preamble
Date: 2020-07-23
Authors:
Name | Affiliations | Address | Phone | Email
Alice Chen | Qualcomm |  |  | 
Sameer Vermani |  |  |  | 
Bin Tian |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
11ax already supports ER SU PPDU while EHT R1 does not introduce any feature that enhances ER mode
  Suggest not defining EHT ER SU for R1.
  Open for more discussion in R2
Need to discuss whether to define Extended Range (ER) preamble in R1
  Mainly for forward compatibility on existence. Enable EHT R1 device to interpret preamble of future ER PPDU
  Only requirement on R1 device is to detect/classify ER preamble and decode/interpret the version independent fields of U-SIG
In this presentation we present an example of ER preamble design based on HE ER SU preamble

## Slide 3: Example of ER Preamble
Similar design as in 11ax ER SU preamble
  Power boosting L-STF/L-LTF
  Repeated L-SIG (RL-SIG)
  Four U-SIG symbols carry 2x26 bits U-SIG content. 11ax ER SU HE-SIGA alike repetition and interleaving scheme
    U-SIG-1 & U-SIG-2 carry same coded bits, and U-SIG-3 & U-SIG-4 carry same coded bits
    U-SIG-1 & U-SIG-3 use interleaving, while U-SIG-2 & U-SIG-4 don’t use interleaving, for better diversity
ER preamble classification
  RL-SIG + L_LEN%3 == 0  11be & beyond
  Q-BPSK rotation in U-SIG-2 to indicate ER preamble
L-SIG
RL SIG
U-SIG-1
U-SIG-2
U-SIG-3
U-SIG-4
L_LEN%3==0
QBPSK  ER Preamble detection
L-STF
L-LTF

## Slide 4: SP
Do you support to define ER preamble (classification and U-SIG decoding only for forward compatibility) but not ER PPDU in 11be in R1?
Y/N/ABS