## Slide 1: PAPR issues for EHT ER SU PPDU
Date: 2020-07-27
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
To extend the transmission range of the low power indoor Wi-Fi system in 6GHz, a new type of PPDU (EHT ER SU PPDU) was introduced in [1][2]
  Data part is duplicated in the frequency domain for the non-punctured 80/160/320MHz SU transmission
  Only BPSK with DCM is used
This frequency-duplicated data part leads to an increase in PAPR
  It may be a harmful issue when EHT ER SU PPDU is used for the outdoor support
  It may also cause a problem for STAs which only support indoor usage cases in 6GHz
In this contribution, we propose a simple method to reduce the PAPR of the data part in EHT ER SU PPDU

## Slide 3: PAPR Issue (1/2)
For STAs which support both indoor and outdoor environments in 6GHz, a PAPR increase due to the frequency-duplicated data part may cause a problem if this PPDU is used for outdoor cases
  For the low power indoor transmission, it is highly probable that PA operates within a linear range that means a little increase in PAPR for this low power mode may not cause a critical problem
  However, for the outdoor support where high power is used for the transmission, this increased PAPR can cause severe signal distortion, and thus, we need a decent method to reduce the PAPR

## Slide 4: PAPR Issue (2/2)
On the other hand, there are many devices used only for the indoor environment these days, and in this case, high PAPR may also need to be treated
  Various home appliances are equipped with a Wi-Fi system to provide smart home services
  IoT services are also prevalently used in many offices through Wi-Fi connection
  In these STAs, hardware can be implemented considering only the indoor support which results in cost reduction
    Considering the low power indoor in 6GHz, hardware requirement can be relaxed, e.g., 1dB compression point of PA can be a low value
  In this case, PAPR reduction may be beneficial for the hardware implementation as well as the performance (PER, throughput, etc.)

## Slide 5: Options for Duplication
We introduce two options for the duplication of the data part in the frequency domain for EHT ER SU PPDU
  Option 1: simple duplication
  Option 2: duplication + phase rotation of 180° (multiplied by -1) at the last (option 2a) / first (option 2b) half of the channel in duplicated data
    For 80MHz EHT ER SU PPDU, 484-tone RU is duplicated and the highest (2a) / second highest (2b) 20MHz subchannel is multiplied by -1
    For 160MHz EHT ER SU PPDU, 996-tone RU is duplicated and the highest (2a) / second highest (2b) 40MHz subchannel is multiplied by -1
    For 320MHz EHT ER SU PPDU, 2x996-tone RU is duplicated and the highest (2a) / second highest (2b) 80MHz subchannel is multiplied by -1
Duplicated Data
Data*
Multiplied by -1
*Data is generated by BPSK with DCM
Duplicated Data
Data*
Frequency domain
Duplicated Data
Data*
Multiplied by -1

## Slide 6: PAPR (1/2)
80MHz
QAM: non-duplicated random data with QPSK
BPSK: non-duplicated random data with BPSK
BPSK w/ DCM: non-duplicated random data with BPSK w/ DCM
For option 1, 2a and 2b, data is modulated using BPSK w/ DCM, and then, duplicated
Simple duplication method (option 1) increases PAPR by about 2dB compared to the non-duplicated case with BPSK w/ DCM
With the proposed phase rotation methods (option 2a and 2b), PAPR can be significantly reduced (even lower than the non-duplicated case with BPSK)
Option 2a and 2b have almost the same PAPR

## Slide 7: PAPR (2/2)
160MHz
320MHz
Trend is similar to the 80MHz frequency-duplicated transmission

## Slide 8: Conclusion
We have discussed PAPR issues for EHT ER SU PPDU which was introduced to enhance the coverage of the low power indoor Wi-Fi system in 6GHz
  EHT ER SU PPDU can be also used for the outdoor case where a high power transmission is assumed, and in this case, PAPR reduction may be necessary
  On the other hand, there are many devices only used in the indoor environment, and, in this case, increased PAPR may also be a problem due to cost-efficient hardware design
To reduce the PAPR for EHT ER SU PPDU, we have proposed to apply the phase rotation to the last / second last half of the channel in duplicated data
  We have verified that these methods achieve considerable reduction in PAPR and even have lower PAPR than the non-duplicated case modulated with BPSK

## Slide 9: Straw Poll #1
Which option do you prefer?
  Option 2a: the last quarter of the channel in the data field is multiplied by -1
  Option 2b: the third quarter of the channel in the data field is multiplied by -1
  Abstain
  This is not intended for SFD
Op1/Op2/A: //

## Slide 10: Straw Poll #2
Do you agree to add the following text to the TGbe SFD?
  11be supports the following duplication and phase rotation methods which are applied to the data field of the PPDU transmitted to a single user and limited to {MCS0+DCM, Nss=1}
    For 80MHz PPDU, 484-tone RU is duplicated and the tones corresponding to the highest 20MHz subchannel is multiplied by -1
    For 160MHz PPDU, 996-tone RU is duplicated and the tones corresponding to the highest 40MHz subchannel is multiplied by -1
    For 320MHz PPDU, 2x996-tone RU is duplicated and the tones corresponding to the highest 80MHz subchannel is multiplied by -1
    This is for rel. 1
Y/N/A: //

## Slide 11: Straw Poll #2a
Do you agree to add the following text to the TGbe SFD?
  11be supports the following duplication and phase rotation methods which are applied to the data field of the PPDU transmitted to a single user and limited to {MCS0+DCM, Nss=1}
    For 80MHz PPDU, 484-tone RU is duplicated and the tones corresponding to the second highest 20MHz subchannel is multiplied by -1
    For 160MHz PPDU, 996-tone RU is duplicated and the tones corresponding to the second highest 40MHz subchannel is multiplied by -1
    For 320MHz PPDU, 2x996-tone RU is duplicated and the tones corresponding to the second highest 80MHz subchannel is multiplied by -1
    This is for rel. 1
Y/N/A: //

## Slide 12: References
[1] 802-11-20/0965r1 6GHz LPI Range Extension
[2] 802-11-20/0986r0 DCM for Range Extension in 6GHz LPI