## Slide 1: CSA/eCSA within AP MLD
Date: 2020-10-08
Authors:

## Slide 2: CSA-eCSA
One AP of an AP MLD can be performing Channel switch Announcement or Extended Channel Switch Announcement
Associated (ML setup) Non-AP MLD that are currently monitoring other beacons on other links shall be informed of this procedure
We simply propose the following:
  If an AP1 of an AP MLD is performing Channel Switch Announcement or Extended Channel Switch announcement procedure, then all the other APs of the AP MLD shall include in the beacon and probe response frames they transmit the same Channel Switch Announcement element or Extended Channel Switch Announcement element for AP1 as the one that AP1 is including in the beacon and probe response frames it transmits

## Slide 3: CSA-eCSA
Further details on the eCSA procedure:
CSA/eCSA/Channel Switch Time elements shall be the same as transmitted on the other link
  Parameters are set in reference to the link that switches
    For instance, channel switch count will be used with the reference of the TBTT of the AP that switches, not the AP sending the element on the other links of the same AP MLD
    The reporting AP needs to provide the most recent timer values (i.e., decrement the TBTT count or Quiet Duration) so that it is consistent with the expected time of change on the other link (see next slide)
  As the AP that switches is mandated to include these elements until the intended channel switch time, the same applies to the other APs of the same AP MLD
  If Max Channel Switch Time element is included in the beacon of the AP that switches, it shall also be included in the other APs of the same AP MLD
    In order to aid new associations in case association happens around a channel switch, CSA/eCSA/Max Channel Switch Time element should to be included in the (re)association response of the reporting link until the reported AP resumes beaconing on the new channel

## Slide 5: Proposal
If an AP1 of an AP MLD is performing Channel Switch Announcement or Extended Channel Switch announcement procedure and include a Channel Switch Announcement element or an Extended Channel Switch Announcement element and/or a Max Channel Switch Time element in a beacon at a TBTT, then any other AP of the AP MLD shall include in the beacon and probe response frames they transmit (or that the transmitted BSSID in the same multiple BSSID set as the other AP transmits if the other AP is a non-transmitted BSSID) the same Channel Switch Announcement element or Extended Channel Switch Announcement element and/or Max Channel Switch Time element in the per-STA profile corresponding to AP1 in the Multi-link element
  The reporting AP needs to provide the most recent timer values (i.e., decrement the TBTT count) so that it is consistent with the expected time of change on the other link
Note: that means that the channel switch count field for instance is applied in reference to the TBTT of AP1 and not of the TBTT of the other AP of the AP MLD, and the TBTT of AP1 is already mandated to be included in the RNR
Note: that means that the CSA/eCSA will be included in every beacons/probe on all links until the intended channel switch time

## Slide 6: CSA/eCSA from non-AP MLD
The CSA/eCSA procedures shall be respected by the STA of the non-AP MLD that operates on the link on which the AP performs CSA/eCSA, when any STAs of the non-AP MLD receive an CSA/eCSA element for that AP.
We propose the following:
  A first STA of a non-AP MLD that is operating after multi-link setup in the link with a first AP of an AP MLD that is performing CSA/eCSA procedure shall follow the CSA/eCSA procedure described in 11.9 (Extended Channel Switching), if that first STA has not received any Channel Switch Announcement element or Extended Channel Switch Announcement element from the first AP but a second STA that is part of the same non-AP MLD received an Channel Switch Announcement element or Extended Channel Switch Announcement element for that first AP from a second AP from the same AP MLD as that first AP, as if that first STA had received the Channel Switch Announcement frame or Extended channel switch announcement frame.

## Slide 7: Quiet element
Similarly, we propose that if a first AP of an AP MLD includes a Quiet element in the beacon/probe response it transmits, then all the APs of the AP MLD include a Quiet element in the STA profile reporting this first AP in a Multi-link element in the beacon and probe response frames they transmit.
  Quiet element is the same as transmitted by the first AP at TBTT, if it is included in beacon/probe response between TBTT-BI and TBTT
  Timing parameters in the element uses the TBTT reference of the first AP, not the AP that sends the element on the other links

## Slide 8: Quiet element
If a quiet period is happening on one link and is part of a periodic quiet element, then we’ll need a way to indicate that in the other link as well

## Slide 9: SP1
Do you support the following:
  If an AP (AP1) of an AP MLD is performing (extended) Channel Switch Announcement procedure and includes a (extended) Channel Switch Announcement element and a Max Channel Switch Time element (if present) in a beacon frame or probe response frame, then any another AP (AP2) of the AP MLD shall include in the beacon and probe response frames they it transmits (or if another AP (AP2) of AP MLD corresponds to a nontransmitted BSSID, then that the transmitted BSSID in the same multiple BSSID set as AP2 as the other AP shall include in the beacon and probe response frame it transmits if the other AP is a non-transmitted BSSID) the (extended) Channel Switch Announcement element and Max Channel Switch Time element in the per-STA profile corresponding to AP1 in the Multi-link element
    The channel switch count field shall be applied in reference to the most recent TBTT and BI indicated in the corresponding element(s) of AP1 and not to the TBTT and BI of the other AP (AP2) of the AP MLD
  Note: the CSA/eCSA/Max Channel Switch Time elements will be included in every beacon and probe response frames on all links of the AP MLD from right after the time AP1 includes the elements in its beacons until the intended channel switch time

## Slide 10: SP1bis (merging SP1 and SP4)
  Do you support to add to the SFD:
  If an AP (AP1) of an AP MLD includes a (extended) Channel Switch Announcement element and a Max Channel Switch Time element (if present) or includes a Quiet element and optionally a Quiet Channel element in a beacon frame or probe response frame it transmits, then another AP (AP2) of the AP MLD shall include in the beacon and probe response frames it transmits (or if another AP (AP2) of the AP MLD corresponds to a nontransmitted BSSID, then the transmitted BSSID in the same multiple BSSID set as AP2 shall include in the beacon and probe response frame it transmits) the (extended) Channel Switch Announcement element and Max Channel Switch Time element or the Quiet element and Quiet Channel element in the per-STA profile corresponding to AP1 in a Multi-link element
    The timing fields in the Quiet element, Quiet Channel element, (extended) Channel Switch Announcement element shall be applied in reference to the most recent TBTT and BI indicated in the corresponding element(s) of AP1 and not to the TBTT and BI of the other AP (AP2) of the AP MLD
    Note: the CSA/eCSA/Max Channel Switch Time elements will be included in every beacon and probe response frames on all links of the AP MLD from right after the time AP1 includes the elements in its beacons until the intended channel switch time

## Slide 11: SP2
Do you support the following:
  When an AP1 of an AP MLD is switching from an initial operating channel/class to a target operating channel/class at a target switch time using (extended) channel switch announcement, then:
    another AP (AP2) of the AP MLD shall populate the fields corresponding to the AP1 that is reported in the RNR in beacon and probe response frames it transmits (or that the transmitted BSSID in the same Multiple BSSID set as the other AP (AP2) transmits if the other AP (AP2) is a non-transmitted BSSID) before the target switch time to the initial operating channel/class
    another AP (AP2) of the AP MLD shall populate the fields corresponding to the AP1 that is reported in the RNR in beacon and probe response frames it transmits (or that the transmitted BSSID in the same Multiple BSSID set as the other AP (AP2) transmits if the other AP (AP2) is a non-transmitted BSSID) after the target switch time to the target operating channel/class

## Slide 12: SP3
Do you support the following:
  If any STA (STA2) of a non-AP MLD receives a management frame with a field corresponding to an AP (AP1) of the AP MLD with which the non-AP MLD is associated, and if the non-AP MLD has an affiliated STA (STA1) that is associated with that AP (AP1), then that affiliated STA (STA1) shall follow the procedure (if any) corresponding to receiving such field from its associated AP (AP1), as if that element was received by the affiliated STA (STA1) from its associated AP (AP1).
    NOTE 1 – Management frames from AP2 that would carry such information include Beacon, Probe Response, (Re)Association Response frame.
    NOTE 2: The timing fields (when present) in such an element are applied with reference to AP1.

## Slide 13: SP4
Do you support that:
  if an AP (AP1) of an AP MLD includes a Quiet element and optionally a Quiet Channel element in the beacon or probe response frame it transmits, then all the another APs (AP2) of the AP MLD shall include in the beacon and probe response frame it transmit (or if another AP (AP2) of AP MLD corresponds to a nontransmitted BSSID, then the transmitted BSSID in the same multiple BSSID set shall include in the beacon and probe response frame it transmits) the Quiet element and Quiet Channel element in the per-STA profile reporting this AP1 in a Multi-link element in the beacon and probe response frames they it transmits
    The timing fields shall be applied in reference to the most recent TBTT and BI advertised in the Quiet element or Quiet Channel element by of AP1 and not of the TBTT and BI of the other AP (AP2) of the AP MLD

## Slide 14: SP5
Do you support that:
  If an AP (AP1) of an AP MLD is switching from an initial operating channel/class to a target operating channel/class at a target switch time using (extended) channel switch announcement, and another AP (AP2) of the AP MLD receives a (re)association request to perform ML setup with AP1 as a requested link, then:
    The other AP (AP2) shall include the (Extended) Channel Switch Announcement element and the same Max Channel Switch Time element (if any) in the per-STA profile corresponding to AP1 in the Multi-link element included in the (re)association frame it sends in response to indicate the time at which AP1 will start beaconing
    The other AP (AP2) shall include a Max Channel Switch Time element (if any) in the per-STA profile corresponding to AP1 in the Multi-link element included in the (re)association frame it sends in response to indicate the time at which AP1 will start beaconing, if the (re)association frame is sent between the last beacon on the initial operating channel/class and the first beacon on the target operating channel/class
  Otherwise, the other AP (AP2) shall not include Max Channel Switch Time element or (Extended) Channel Switch Announcement element in (re)association response
  The timing fields in the (Extended) Channel Switch Announcement element and Max Channel Switch Time element (if present) are applied with reference to the most recent values for AP1.

## Slide 15: SP6
Do you support that:
  When an AP (AP1) of an AP MLD has announced period(s) of silence using Quiet element and optionally Quiet Channel element, and another AP (AP2) of the same AP MLD receives a (re)association request to perform ML setup with AP1 as one of the requested link, then:
    The other AP (AP2) shall include the Quiet element and Quiet Channel element (if present) in the per-STA profile corresponding to AP1 in the Multi-link element included in the (re)association response frame it sends in response to indicate the time(s) at (and duration for) which AP1’s BSS will be silenced
    The timing fields shall be applied in reference to the most recent TBTT and to the BI of AP1 and not of the TBTT and BI of the other AP (AP2) of the AP MLD