## Slide 1
Authors:
ML AP MLD Network Reference Model
Date: 2020-08-03
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | 
Zhiqiang Han | ZTE |  |  | 
Liuming Lu | ZTE |  |  | 
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution discusses the existing DS reference model to support AP MLD network and suggests to reuse the existing DS-SAP to accept STA-to-AP mapping updates from the APs and enable access to the DS for associated non-AP MLDs.

## Slide 3: Background
ESS, DS and DS SAP [1]
  DS enables mobile device support by providing the logical services necessary to handle address to destination mapping and seamless integration of multiple BSSs.
  DS allow to create a wireless network of arbitrary size and complexity which is referred as ESS. An ESS is the union of the infrastructure BSSs with the same SSID connected by a DS.
  DS-SAP is the interface between the DS SAP service users and the DS SAP service provider. The DS-SAP service users are the connected APs and the portal. The DS-SAP service provider is the DS.
  DS provides the following functions through DS-SAP
    Accept MSDUs (as part of MAC service tuples) from APs, mesh gates, and the portal.
    Deliver MSDUs (as part of MAC service tuples) to APs, mesh gates, or the portal.
    Accept STA-to-AP mapping updates from the APs.
  DSAF is to enable access to the DS via the WM for associated STAs.

## Slide 4: AP MLD Network Reference Model
Typical Home Networking Model
  Option 1: ISM modem provide the gateway to Internet and routing function of home network which consists of multiple APs for radio coverage.
  Option 2: One AP is connected to the ISM modem for the Internet connection, and provides routing function in the home network. One or more APs are connected to the AP for radio coverage in the home
  A station can associate any AP in the home network.
AP1
AP2
AP3
ISM Modem
Ethernet or Wi-Fi
Ethernet or Wi-Fi
STA
(2)
Internet
AP1
AP2
AP3
ISM Modem
Ethernet
Ethernet
STA
(1)
Internet
AP will be replaced by AP MLD in the future
DS
DS

## Slide 5: AP MLD Network Reference Model
DS-SAP
  Reuse the existing DS-SAP
    Enable access to the DS for associated non-AP MLDs.
    Accept and deliver IEEE 802.11 MAC service tuples, including all of the parameters and data
AP MLD-2
Link21
Link22
AP MLD-1
STA (MAC/PHY)
Link11
STA (MAC/PHY)
Link12
MLME/PLME
SME
ML Common MAC Entity
ML Common MAC Entity
IEEE 802.1X
MAC-SAP
IEEE 802.1X
MAC-SAP
DS
SME
MLME/PLME
SME
MLME/PLME
STA (MAC/PHY)
STA (MAC/PHY)
MLME/PLME
SME
DS-SAP
DS-SAP

## Slide 6: Summary
This contribution
  Discussed the existing DS reference model to support AP MLD network.
  Suggested to reuse the existing DS-SAP to accept STA-to-AP mapping updates from the APs and enable access to the DS for associated non-AP MLDs.

## Slide 7: Straw Polls
SP1
  Do you support in SFD to reuse the existing DS-SAP to accept a non-AP MLD to an AP MLD mapping updates from the AP MLD and enable access to the DS for an associated non-AP MLD?

## Slide 8: References
[1] IEEE802.11-REVmd D3.4

## Slide 9
Thank you!