## Slide 1: E-SIG Detection with Different Puncturing Patterns
Date: 2020-08-03
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Yan Xin |  |  |  | yan.xin@huawei.com
Mengshi Hu |  |  |  | humengshi@huawei.com
Osama Aboul-Magd |  |  |  | osama.aboulmagd@huawei.com

## Slide 2: Background
80 MHz Preamble Detection and 2 content channels in each 80 MHz of E-SIG are decided [1][2]
  There shall be a variable MCS and variable length EHT-SIG, in an EHT PPDU sent to multiple users [3]
Since 40 MHz content channels are duplicated in each 80 MHz E-SIG, we may achieve combining gains for E-SIG detection in case of no preamble puncturing in the 80 MHz segment
We observed even further gain with different puncturing patterns applied to duplicated 40 MHz content channels
The overhead reduction in E-SIG is an imminent goal for our Release 1 progress
  The additional gain with the different puncturing patterns applied to the duplicated 40 MHz may help increase the MCS, especially for those MCSs in the boundary

## Slide 3: 40 MHz Duplicated E-SIG in 80 MHz segment with MCS2/4/5 having different puncturing patterns in each 40 MHz
At the receiver side,
(1) We compute the LLR of E-SIG per content channel  E-SIG is encoded per content channel
(2) Then, insert the zero bit at the punctured positions according to the Puncturing pattern designated to each content channel
(3) Combine the LLRs of primary 40 MHz with that of the secondary 40 MHz
(4) Run the BCC decoder per content channel based on the combined LLRs in Step 3
L-Preamble
/ RL-SIG
U-SIG
U-SIG
U-SIG
U-SIG
EHT-STF/LTF
and Payload
E-SIG - 1
with MCS2/4/5
E-SIG - 2
with MCS2/4/5
E-SIG - 1
with MCS2/4/5 - A
E-SIG - 2
with MCS2/4/5 - A
L-Preamble
/ RL-SIG
L-Preamble
/ RL-SIG
L-Preamble
/ RL-SIG

## Slide 4: Puncturing Patterns for the rate of 3/4 (MCS2/MCS4)
* Puncturing Pattern of BCC code rate 3/4 in the current 802.11
X0
X1
X2
X3
X4
X5
X6
X7
X8
A0
A1
A2
A3
A4
A5
A6
A7
A8
B0
B1
B2
B3
B4
B5
B6
B7
B8
A0
B0
A1
B2
A3
B3
A4
B5
A6
B6
A7
B8
A0
A1
A2
A3
A4
A5
A6
A7
A8
B0
B1
B2
B3
B4
B5
B6
B7
B8
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
* Puncturing Pattern for MCS2/4-A
X0
X1
X2
X3
X4
X5
X6
X7
X8
A0
A1
A2
A3
A4
A5
A6
A7
A8
B0
B1
B2
B3
B4
B5
B6
B7
B8
A0
B1
A2
B2
A3
B4
A5
B5
A6
B7
A8
B8
A0
A1
A2
A3
A4
A5
A6
A7
A8
B0
B1
B2
B3
B4
B5
B6
B7
B8
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
Information Bits
Coded Bits
Punctured Bit
Bit Punctured
Data
Decoded Bits
Bit Inserted
Data
Inserted Zero Bit
TX
RX

## Slide 5: Puncturing Patterns for the rate of 2/3 (MCS5)
* Puncturing Pattern of BCC code rate 2/3 in the current 802.11
* Puncturing Pattern for the rate 2/3 of MCS5-A
X0
X1
X2
X3
X4
X5
A0
A1
A2
A3
A4
A5
B0
B1
B2
B3
B4
B5
A0
B0
A1
A2
B2
A3
A4
B4
A5
Information Bits
Coded Bits
Punctured Bit
Bit Punctured
Data
Decoded Bits
Bit Inserted
Data
Inserted Zero Bit
TX
RX
A0
A1
A2
A3
A4
A5
B0
B1
B2
B3
B4
B5
Y0
Y1
Y2
Y3
Y4
Y5
X0
X1
X2
X3
X4
X5
A0
A1
A2
A3
A4
A5
B0
B1
B2
B3
B4
B5
A0
A1
B1
A2
A3
B3
A4
A5
B5
A0
A1
A2
A3
A4
A5
B0
B1
B2
B3
B4
B5
Y0
Y1
Y2
Y3
Y4
Y5

## Slide 6: Simulation setting
SISO 80 MHz w/ 40 MHz duplication
Primary 20 and the secondary 20 MHz are separately encoded in the primary 40 MHz / secondary 40 MHz
MCS1~5 for Primary 40 MHz
MCS1/2A/3/4A/5A for Secondary 40 MHz
Actual channel estimation
BCC and Viterbi decoder
ChanD
Packet size – 10 bytes per content channel

## Slide 7
MCS5
MCS4
MCS2
MCS1
MCS3
Mixed Puncturing Pattern: Mixture of Puncturing Pattern between MCS2/4/5 and MCS2A/4A/5A, when combining

## Slide 8: Summary
We proposed to apply different puncturing patterns to the duplicated secondary 40 MHz content channels in each 80 MHz segment
  Combining gains boosted by 1~2 dB depending on the MCS with the mixed puncturing patterns
  The MCS where corresponding SNRs are in the boundary may be upgraded to the higher MCS with the help of our proposal, which may eventually reduce the E-SIG overhead.
We propose MCS0~MCS5 for the E-SIG MCS
  with the proposed puncturing patterns for the duplicated channels
  DCM for MCS0/1/3/4 is supported for HE SIG-B in 802.11ax

## Slide 9: SP1
Do you agree to have MCS0/1/2/3/4/5 available to be applied for the E-SIG field?
  Support of DCM for MCS0/1/3/4 is TBD

## Slide 10: SP2
For each 80 MHz segment of any EHT-PPDU larger than or equal to 80 MHz BW, do you agree to apply the different puncturing patterns for MCS2/4/5 to two content channels in the secondary 40 MHz of E-SIG?
  Different Puncturing patterns are shown in slide 4&5, but not limited to the patterns

## Slide 11: Reference
[1] S. Vermani, et. al., “U-SIG structure and preamble processing”, 802.11-20/0380r0, Mar. 2020
[2] D. Lim, et. al., “Consideration for E-SIG Transmission”, 802.11-20/0020r3, Apr. 2020
[3] S. Vermani, et. al., “Further ideas on EHT preamble design”, 802.11-19/1870r4, Nov. 2019