## Slide 1: E-SIG Detection with Different Puncturing Patterns
Date: 2020-08-03
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Yan Xin |  |  |  | yan.xin@huawei.com
Mengshi Hu |  |  |  | humengshi@huawei.com
Osama Aboul-Magd |  |  |  | osama.aboulmagd@huawei.com

## Slide 2: Background
Since 40 MHz content channels are duplicated in each 80 MHz E-SIG, we may achieve combining gains for E-SIG detection in case of no preamble puncturing in the 80 MHz segment
We observed even further gain with additional diversity schemes applied to duplicated 40 MHz content channels
The overhead reduction in E-SIG is an critical goal for our Release 1 progress
  For the case of 6 E-SIG symbols with MCS 5  9 E-SIG symbols with MCS 3  36 E-SIG symbols with MCS 0 (MCS 0 does not fit with the max number of symbols)
  For the case of 3 E-SIG symbols with MCS 5  5 E-SIG symbols with MCS 3  24 E-SIG symbols with MCS 0

## Slide 3: Scheme 1: DCM applied to 40 MHz Duplicated E-SIG in 80 MHz segment
E-SIG-1 with DCM and E-SIG-2 with DCM are DCM-modulated over the entire content channel
  That is, for the E-SIG-1 with MCS1-DCM case, conj(Sk) where Sk is a QPSK constellation per subcarrier will be taken for the entire 20MHz content channel
L-Preamble
/ RL-SIG
U-SIG
U-SIG
U-SIG
U-SIG
EHT-STF/LTF
and Payload
E-SIG - 1
E-SIG - 2
E-SIG - 1
with DCM
E-SIG - 2
with DCM
L-Preamble
/ RL-SIG
L-Preamble
/ RL-SIG
L-Preamble
/ RL-SIG

## Slide 4: Simulation setting
SISO 80 MHz w/ 40 MHz duplication
Primary 20 and the secondary 20 MHz are separately encoded in the primary 40 MHz / secondary 40 MHz
MCS1~5 for Primary 40 MHz
MCS1~5 with DCM for Secondary 40 MHz
  Each entire content channel is DCM-modulated
Actual channel estimation
BCC and Viterbi decoder
ChanD
Packet size – 10 bytes per content channel

## Slide 5
MCS3 with DCM shows about 1 dB gain over MCS3 with simple combining
MCS3 is an important MCS for EHT-SIG in consideration of E-SIG overhead reduction

## Slide 6: Scheme 2: 40 MHz Duplicated E-SIG in 80 MHz segment with MCS2/4/5 having different puncturing patterns in each 40 MHz
At the receiver side,
(1) We compute the LLR of E-SIG per content channel  E-SIG is encoded per content channel
(2) Then, insert the zero bit at the punctured positions according to the Puncturing pattern designated to each content channel
(3) Combine the LLRs of primary 40 MHz with that of the secondary 40 MHz
(4) Run the BCC decoder per content channel based on the combined LLRs in Step 3
L-Preamble
/ RL-SIG
U-SIG
U-SIG
U-SIG
U-SIG
EHT-STF/LTF
and Payload
E-SIG - 1
with MCS2/4/5
E-SIG - 2
with MCS2/4/5
E-SIG - 1
with MCS2/4/5 - A
E-SIG - 2
with MCS2/4/5 - A
L-Preamble
/ RL-SIG
L-Preamble
/ RL-SIG
L-Preamble
/ RL-SIG

## Slide 7: Puncturing Patterns for the rate of 3/4 (MCS2/MCS4)
* Puncturing Pattern of BCC code rate 3/4 in the current 802.11
X0
X1
X2
X3
X4
X5
X6
X7
X8
A0
A1
A2
A3
A4
A5
A6
A7
A8
B0
B1
B2
B3
B4
B5
B6
B7
B8
A0
B0
A1
B2
A3
B3
A4
B5
A6
B6
A7
B8
A0
A1
A2
A3
A4
A5
A6
A7
A8
B0
B1
B2
B3
B4
B5
B6
B7
B8
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
* Puncturing Pattern for MCS2/4-A
X0
X1
X2
X3
X4
X5
X6
X7
X8
A0
A1
A2
A3
A4
A5
A6
A7
A8
B0
B1
B2
B3
B4
B5
B6
B7
B8
A0
B1
A2
B2
A3
B4
A5
B5
A6
B7
A8
B8
A0
A1
A2
A3
A4
A5
A6
A7
A8
B0
B1
B2
B3
B4
B5
B6
B7
B8
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
Information Bits
Coded Bits
Punctured Bit
Bit Punctured
Data
Decoded Bits
Bit Inserted
Data
Inserted Zero Bit
TX
RX

## Slide 8: Puncturing Patterns for the rate of 2/3 (MCS5)
* Puncturing Pattern of BCC code rate 2/3 in the current 802.11
* Puncturing Pattern for the rate 2/3 of MCS5-A
X0
X1
X2
X3
X4
X5
A0
A1
A2
A3
A4
A5
B0
B1
B2
B3
B4
B5
A0
B0
A1
A2
B2
A3
A4
B4
A5
Information Bits
Coded Bits
Punctured Bit
Bit Punctured
Data
Decoded Bits
Bit Inserted
Data
Inserted Zero Bit
TX
RX
A0
A1
A2
A3
A4
A5
B0
B1
B2
B3
B4
B5
Y0
Y1
Y2
Y3
Y4
Y5
X0
X1
X2
X3
X4
X5
A0
A1
A2
A3
A4
A5
B0
B1
B2
B3
B4
B5
A0
A1
B1
A2
A3
B3
A4
A5
B5
A0
A1
A2
A3
A4
A5
B0
B1
B2
B3
B4
B5
Y0
Y1
Y2
Y3
Y4
Y5

## Slide 9: Simulation setting
SISO 80 MHz w/ 40 MHz duplication
Primary 20 and the secondary 20 MHz are separately encoded in the primary 40 MHz / secondary 40 MHz
MCS1~5 for Primary 40 MHz
MCS1/2A/3/4A/5A for Secondary 40 MHz
Actual channel estimation
BCC and Viterbi decoder
ChanD
Packet size – 10 bytes per content channel

## Slide 10
MCS5
MCS4
MCS2
MCS1
MCS3
Mixed Puncturing Pattern: Mixture of Puncturing Pattern between MCS2/4/5 and MCS2A/4A/5A, when combining

## Slide 11: Summary
We proposed to apply an additional diversity scheme to the duplicated secondary 40 MHz content channels in each 80 MHz segment
  Additional 1 dB gain is observed for MCS 3 with DCM
  Combining gains boosted by 1~2 dB depending on the MCS with the mixed puncturing patterns
Since MCS3 is likely to be used quite often to reduce the E-SIG overhead, the robust detection of MCS 3 is very important

## Slide 12: SP1
For each 80 MHz segment of any EHT-PPDU larger than or equal to 80 MHz BW, do you agree to apply an additional diversity scheme to two content channels in the secondary 40 MHz of E-SIG?

## Slide 13: Reference
[1] S. Vermani, et. al., “U-SIG structure and preamble processing”, 802.11-20/0380r0, Mar. 2020
[2] D. Lim, et. al., “Consideration for E-SIG Transmission”, 802.11-20/0020r3, Apr. 2020
[3] S. Vermani, et. al., “Further ideas on EHT preamble design”, 802.11-19/1870r4, Nov. 2019