## Slide 1: Discussions on MU-MIMO Signaling
Date: 2020-08-05
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@Huawei.com
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan | Huawei |  |  | 

## Slide 2
  The number of spatial streams for the user is derived by using the row corresponding to the signaled 4-bit Spatial Configuration subfield and the column corresponding to the User field position in the User Specific field.
  The starting stream index for the user is computed by summing the NSTS in the columns prior to the column indicated by the user’s User field position.
In 11ax, there exists a Spatial Configuration subfield in each MU-MIMO User field. For a given value of Nuser, the MU-MIMO information can be indicated as follows:
Therefore, for an MU-MIMO user, the below information is needed to obtain its spatial configuration information
  Spatial Configuration subfield
  User field position
  Nuser (Number of MU-MIMO users)
Recap: MU-MIMO Indication in 11ax
Nuser
User field position
  Spatial Configuration subfield

## Slide 3
On the basis of the agreed EHT PPDU format sent to multiple users, an efficient per-80MHz preamble structure is designed [1-3]
… | U-SIG2 | EHT-SIG2_2 | …
… | U-SIG2 | EHT-SIG2_1 | …
… | U-SIG2 | EHT-SIG2_2 | …
… | U-SIG2 | EHT-SIG2_1 | …
… | U-SIG1 | EHT-SIG1_2 | …
… | U-SIG1 | EHT-SIG1_1 | …
… | U-SIG1 | EHT-SIG1_2 | …
… | U-SIG1 | EHT-SIG1_1 | …
Primary 80MHz
Secondary 80MHz
  A STA only needs to process up to one 80 MHz segment of the pre-EHT preamble (up-to and including EHT-SIG) to get all the assignment information for itself.
MU-MIMO in Per-80MHz Preamble Signaling
In this structure, if we follow the MU-MIMO indication method in 11ax, the signaling overhead will be high when the users participating in an MU-MIMO belong to different segments (for both OFDMA and non-OFDMA cases).
MU-MIMO with users belonging to more than one segment
  In the following, we first give the details of the above overhead analysis in OFDMA cases.

## Slide 4: Signal All User Fields (Opt. 1)
In 11ax, as we have shown previously, the User field position and the total number of MU-MIMO users are needed for a User to obtain its MU-MIMO information in Spatial Configuration table (See Appendix A [4]).
  If we follow the 11ax style, signaling all the user fields participating in an MU-MIMO is needed to maintain the User field positions. Here we call this method the Opt. 1 [5].
Examples for Opt. 1
  A 242-tone RU has 5 MU-MIMO users. The 1st and 3rd users in the Spatial Configuration table belong to Segment 1, and the 2nd, 4th and 5th users belong to Segment 2.
Opt 1.1
Opt 1.2
Yellow block: Corresponds to the users parked on segment 1
Orange block: Corresponds to the users parked on segment 2
White block: Dummy User fields

## Slide 5: Add Special User Field (Opt. 2)
Although Opt 1 has less specification modification, the overhead is high because it needs some additional User fields to maintain the User field position.
To save the overhead of user fields, in Opt 2 we propose to add a special user field to inform the total number of MU-MIMO users (Nuser) and the orders (User field positions) in the corresponding segment.
  This special user field only occurs when there exists multi-segment MU-MIMO, and can be indicated by a special STA ID.
  We still use the table of Spatial Configuration table to inform the spatial configuration.
Subfield | Number of bits | Description
STA ID | 11 | Special STA ID (indicating a user field signaling the information of multi-segment MU-MIMO)
Number of MU-MIMO Users | 3 | Indicates the total number of MU-MIMO users (Nuser, not the number of users in a segment) in one multi-segment MU-MIMO
Order Bitmap | 8 | Used to show the orders of the user fields (User field positions) in the table of spatial configuration subfield encoding
… | … | …
User field with special STA ID
  Note: Needed information for MU-MIMO 1. Spatial Configuration subfield 2. User field position 3. Nuser (Number of MU-MIMO users)

## Slide 6: Add Special User Field (Opt. 2)
Example for Opt. 2
  A 242-tone RU has 5 MU-MIMO users. The 1st and 3rd users in the Spatial Configuration table belong to segment 1, and the 2nd, 4th and 5th users belong to segment 2.
Yellow block: Corresponds to the users parked on segment 1
Orange block: Corresponds to the users parked on segment 2
White block: Special User fields used to inform the spatial configuration.
Order Bitmap in Special User field: 1010 0000 (indicates the User field positions in Spatial Configuration table)
Number of MU-MIMO Users (indicates Nuser)
  This number is indicated by the RU Allocation subfield
  This special user field is at the front of the user fields related to a multi-segment MU-MIMO
  Note: Needed information for MU-MIMO 1. Spatial Configuration subfield 2. User field position 3. Nuser (Number of MU-MIMO users)
Spatial Configuration subfield exists in these User fields

## Slide 7: Overhead Analysis for OFDMA Cases
Options | Overhead of User fields | Overhead Analysis
Opt 1 Signal all User fields | For an RU/MRU, The number of User fields in a segment is equal to the total number of MU-MIMO users | For one multi-segment MU-MIMO with users in two segments, the number of user fields in these segments are 2N for an RU/MRU, where N is the total number of MU-MIMO users (N>=2). Similarly, for one multi-segment MU-MIMO with users in three segments, the number is 3N. …
Opt 2 Add a special User field to indicate the user orders in Spatial Configuration Table | For an RU/MRU, the number of User fields in a segment is equal to the number of MU-MIMO users in the segment + 1 | For one multi-segment MU-MIMO with users in two segments, the number of user fields in these segments are N+2 for an RU/MRU. Similarly, for one multi-segment MU-MIMO with users in three segments, the number is N+3. …
The special user field only occurs when there exists multi-segment MU-MIMO in OFDMA cases.
Note that because N is always larger than or equal to 2, 2N is equal to or larger than N+2. With the increase of N, the overhead benefit of Opt 2 becomes larger. Furthermore, if there are more than one multi-segment MU-MIMO in OFDMA cases, the overhead can be further saved.

## Slide 8: Non-OFDMA Cases based on Opt. 1
Non-OFDMA cases based on Opt 1
  EHT has adopted that the number of EHT-SIG symbols field always exists in U-SIG of a PPDU that is not a EHT TB PPDU
  The field is not reinterpreted as the number of MU-MIMO users
  In OFDMA transmission, the number of MU-MIMO users can be indicated by RU Allocation subfield
  In Non-OFDMA transmission, the number of MU-MIMO users can exist in the EHT-SIG to inform the total number of MU-MIMO users.
Example:
The total number of User fields in two content channels is equal to the total number of MU-MIMO users

## Slide 9: Non-OFDMA Cases based on Opt. 2
Non-OFDMA cases based on Opt 2
  On the basis of Opt 2, we can also remove the special User field, and add the Order Bitmap (e.g. an 8-bit bitmap) to EHT-SIG in non-OFDMA cases.
  The number of MU-MIMO users is also needed in the EHT-SIG to inform the total number of MU-MIMO users.
  The Order Bitmap can indicate the User field positions and the number of User fields in the corresponding segment. The existence of this subfield can also be indicated by some other subfields.
Example:
e.g. 1011 0000
The total number of User fields in two content channels is equal to the number of MU-MIMO users in the segment

## Slide 10: Summary
Proposed Opt. 2 to further reduce the overhead in the cases where the users participating in an MU-MIMO belong to different segments
Non-OFDMA cases based on Opt. 1 and Opt. 2 were discussed.
  The Number of MU-MIMO Users subfield is needed in EHT-SIG
  Add an Order Bitmap (e.g. an 8-bit bitmap) subfield to EHT-SIG in non-OFDMA cases can save the overhead.
Options | Examples | Overhead
Opt 1 Signal all User fields |  | Total number of MU-MIMO users
Opt 2 Add a special User field to indicate the user orders in Spatial Configuration Table |  | MU-MIMO users in the corresponding segment + 1
Note that the Special User field in Opt. 2 only occurs when there exists multi-segment MU-MIMO in OFDMA cases

## Slide 11
[1] IEEE 802.11-20/0439r0 Efficient EHT Preamble Design
[2] IEEE 802.11-20/0380r0 U-SIG Structure and Preamble Processing
[3] IEEE 802.11-20/0605r0 Further Discussions on Efficient EHT Preamble
[4] IEEE 802.11-20/0930r3 Consideration on User-specific field in EHT-SIG
[5] IEEE 802.11-20/1102r0 Zero User RUs for Per-80MHz Resource Unit Allocation Signaling
References

## Slide 12
Straw Poll #1
Do you agree that the Number of MU-MIMO Users subfield exists in the Common field of EHT-SIG of an EHT MU PPDU in a non-OFDMA transmission?
  Note: The Number of MU-MIMO Users subfield indicates the total number of MU-MIMO users in a non-OFDMA transmission.
  Y/N/A

## Slide 13
Straw Poll #2
Do you agree that for an RU/MRU with MU-MIMO, the corresponding number of MU-MIMO User fields in a segment can be smaller than the total number of MU-MIMO users?
  Y/N/A

## Slide 14
Straw Poll #3
Do you agree that a special user field can be used in the cases where the users participating in an MU-MIMO belong to different segments ?
  The special user field carries the Number of MU-MIMO Users subfield and an Order Bitmap subfield.
  The Order Bitmap subfield is used to indicate the User field positions.
  Y/N/A

## Slide 15
Straw Poll #4
Do you agree that an Order Bitmap subfield exists in the Common field of EHT-SIG of an EHT MU PPDU in a non-OFDMA transmission?
  The Order Bitmap subfield is used to indicate the User field positions and the number of User fields in the corresponding segment.
  Y/N/A

## Slide 16: Appendix A: Spatial Configuration table (1/3)
Nuser | B5…B0 | Nsts[1] | Nsts[2] | Nsts[3] | Nsts[4] | Nsts[5] | Nsts[6] | Nsts[7] | Nsts[8] | Total Nsts | total entry
2 | 000000-000011 | 1-4 | 1 |  |  |  |  |  |  | 2-5 | 10
 | 000100-000110 | 2-4 | 2 |  |  |  |  |  |  | 4-6 | 
 | 000111-001000 | 3-4 | 3 |  |  |  |  |  |  | 6-7 | 
 | 001001 | 4 | 4 |  |  |  |  |  |  | 8 | 
3 | 000000-000011 | 1-4 | 1 | 1 |  |  |  |  |  | 3-6 | 20
 | 000100-000110 | 2-4 | 2 | 1 |  |  |  |  |  | 5-7 | 
 | 000111-001000 | 3-4 | 3 | 1 |  |  |  |  |  | 7-8 | 
 | 001001 | 4 | 4 | 1 |  |  |  |  |  | 9 | 
 | 001010-001100 | 2-4 | 2 | 2 |  |  |  |  |  | 6-8 | 
 | 001101-001110 | 3-4 | 3 | 2 |  |  |  |  |  | 8-9 | 
 | 001111 | 4 | 4 | 2 |  |  |  |  |  | 10 | 
 | 010000-010001 | 3-4 | 3 | 3 |  |  |  |  |  | 9-10 | 
 | 010010 | 4 | 4 | 3 |  |  |  |  |  | 11 | 
 | 010011 | 4 | 4 | 4 |  |  |  |  |  | 12 | 
4 | 000000-000011 | 1-4 | 1 | 1 | 1 |  |  |  |  | 4-7 | 35
 | 000100-000110 | 2-4 | 2 | 1 | 1 |  |  |  |  | 6-8 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 |  |  |  |  | 8-9 | 
 | 001001 | 4 | 4 | 1 | 1 |  |  |  |  | 10 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 |  |  |  |  | 7-9 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 |  |  |  |  | 9-10 | 
 | 001111 | 4 | 4 | 2 | 1 |  |  |  |  | 11 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 |  |  |  |  | 10-11 | 
 | 010010 | 4 | 4 | 3 | 1 |  |  |  |  | 12 | 
 | 010011 | 4 | 4 | 4 | 1 |  |  |  |  | 13 | 
 | 010100-010110 | 2-4 | 2 | 2 | 2 |  |  |  |  | 8-10 | 
 | 010111-011000 | 3-4 | 3 | 2 | 2 |  |  |  |  | 10-11 | 
 | 011001 | 4 | 4 | 2 | 2 |  |  |  |  | 12 | 
 | 011010-011011 | 3-4 | 3 | 3 | 2 |  |  |  |  | 11-12 | 
 | 011100 | 4 | 4 | 3 | 2 |  |  |  |  | 13 | 
 | 011101 | 4 | 4 | 4 | 2 |  |  |  |  | 14 | 
 | 011110-011111 | 3-4 | 3 | 3 | 3 |  |  |  |  | 12-13 | 
 | 100000 | 4 | 4 | 3 | 3 |  |  |  |  | 14 | 
 | 100001 | 4 | 4 | 4 | 3 |  |  |  |  | 15 | 
 | 100010 | 4 | 4 | 4 | 4 |  |  |  |  | 16 | 

## Slide 17: Appendix A: Spatial Configuration table (2/3)
Nuser | B5…B0 | Nsts[1] | Nsts[2] | Nsts[3] | Nsts[4] | Nsts[5] | Nsts[6] | Nsts[7] | Nsts[8] | Total Nsts | total entry
5 | 000000-000011 | 1-4 | 1 | 1 | 1 | 1 |  |  |  | 5-8 | 49
 | 000100-000110 | 2-4 | 2 | 1 | 1 | 1 |  |  |  | 7-9 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 | 1 |  |  |  | 9-10 | 
 | 001001 | 4 | 4 | 1 | 1 | 1 |  |  |  | 11 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 | 1 |  |  |  | 8-10 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 | 1 |  |  |  | 10-11 | 
 | 001111 | 4 | 4 | 2 | 1 | 1 |  |  |  | 12 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 | 1 |  |  |  | 11-12 | 
 | 010010 | 4 | 4 | 3 | 1 | 1 |  |  |  | 13 | 
 | 010011 | 4 | 4 | 4 | 1 | 1 |  |  |  | 14 | 
 | 010100-010110 | 2-4 | 2 | 2 | 2 | 1 |  |  |  | 9-11 | 
 | 010111-011000 | 3-4 | 3 | 2 | 2 | 1 |  |  |  | 11-12 | 
 | 011001 | 4 | 4 | 2 | 2 | 1 |  |  |  | 13 | 
 | 011010-011011 | 3-4 | 3 | 3 | 2 | 1 |  |  |  | 12-13 | 
 | 011100 | 4 | 4 | 3 | 2 | 1 |  |  |  | 14 | 
 | 011101 | 4 | 4 | 4 | 2 | 1 |  |  |  | 15 | 
 | 011110-011111 | 3-4 | 3 | 3 | 3 | 1 |  |  |  | 13-14 | 
 | 100000 | 4 | 4 | 3 | 3 | 1 |  |  |  | 15 | 
 | 100001 | 4 | 4 | 4 | 3 | 1 |  |  |  | 16 | 
 | 100010-100100 | 2-4 | 2 | 2 | 2 | 2 |  |  |  | 10-12 | 
 | 100101-100110 | 3-4 | 3 | 2 | 2 | 2 |  |  |  | 12-13 | 
 | 100111 | 4 | 4 | 2 | 2 | 2 |  |  |  | 14 | 
 | 101000-101001 | 3-4 | 3 | 3 | 2 | 2 |  |  |  | 13-14 | 
 | 101010 | 4 | 4 | 3 | 2 | 2 |  |  |  | 15 | 
 | 101011 | 4 | 4 | 4 | 2 | 2 |  |  |  | 16 | 
 | 101100-101101 | 3-4 | 3 | 3 | 3 | 2 |  |  |  | 14-15 | 
 | 101110 | 4 | 4 | 3 | 3 | 2 |  |  |  | 16 | 
 | 101111-110000 | 3-4 | 3 | 3 | 3 | 3 |  |  |  | 15-16 | 
6 | 000000-000011 | 1-4 | 1 | 1 | 1 | 1 | 1 |  |  | 6-9 | 54
 | 000100-000110 | 2-4 | 2 | 1 | 1 | 1 | 1 |  |  | 8-10 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 | 1 | 1 |  |  | 10-11 | 
 | 001001 | 4 | 4 | 1 | 1 | 1 | 1 |  |  | 12 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 | 1 | 1 |  |  | 9-11 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 | 1 | 1 |  |  | 11-12 | 
 | 001111 | 4 | 4 | 2 | 1 | 1 | 1 |  |  | 13 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 | 1 | 1 |  |  | 12-13 | 
 | 010010 | 4 | 4 | 3 | 1 | 1 | 1 |  |  | 14 | 
 | 010011 | 4 | 4 | 4 | 1 | 1 | 1 |  |  | 15 | 
 | 010100-010110 | 2-4 | 2 | 2 | 2 | 1 | 1 |  |  | 10-12 | 
 | 010111-011000 | 3-4 | 3 | 2 | 2 | 1 | 1 |  |  | 12-13 | 
 | 011001 | 4 | 4 | 2 | 2 | 1 | 1 |  |  | 14 | 
 | 011010-011011 | 3-4 | 3 | 3 | 2 | 1 | 1 |  |  | 13-14 | 
 | 011100 | 4 | 4 | 3 | 2 | 1 | 1 |  |  | 15 | 
 | 011101 | 4 | 4 | 4 | 2 | 1 | 1 |  |  | 16 | 
 | 011110-011111 | 3-4 | 3 | 3 | 3 | 1 | 1 |  |  | 14-15 | 
 | 100000 | 4 | 4 | 3 | 3 | 1 | 1 |  |  | 16 | 
 | 100001-100011 | 2-4 | 2 | 2 | 2 | 2 | 1 |  |  | 11-13 | 
 | 100100-100101 | 3-4 | 3 | 2 | 2 | 2 | 1 |  |  | 13-14 | 
 | 100110 | 4 | 4 | 2 | 2 | 2 | 1 |  |  | 15 | 
 | 100111-101000 | 3-4 | 3 | 3 | 2 | 2 | 1 |  |  | 14-15 | 
 | 101001 | 4 | 4 | 3 | 2 | 2 | 1 |  |  | 16 | 
 | 101010 - 101011 | 3-4 | 3 | 3 | 3 | 2 | 1 |  |  | 15-16 | 
 | 101100 | 3 | 3 | 3 | 3 | 3 | 1 |  |  | 16 | 
 | 101101-101111 | 2-4 | 2 | 2 | 2 | 2 | 2 |  |  | 12-14 | 
 | 110000-110001 | 3-4 | 3 | 2 | 2 | 2 | 2 |  |  | 14-15 | 
 | 110010 | 4 | 4 | 2 | 2 | 2 | 2 |  |  | 16 | 
 | 110011-110100 | 3-4 | 3 | 3 | 2 | 2 | 2 |  |  | 15-16 | 
 | 110101 | 3 | 3 | 3 | 3 | 2 | 2 |  |  | 16 | 

## Slide 18: Appendix A: Spatial Configuration table (3/3)
Nuser | B5…B0 +B92 | Nsts[1] | Nsts[2] | Nsts[3] | Nsts[4] | Nsts[5] | Nsts[6] | Nsts[7] | Nsts[8] | Total Nsts | total entry
7 | 000000-000011 | 1-4 | 1 | 1 | 1 | 1 | 1 | 1 |  | 7-10 | 50
 | 000100-000110 | 2-4 | 2 | 1 | 1 | 1 | 1 | 1 |  | 9-11 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 | 1 | 1 | 1 |  | 11-12 | 
 | 001001 | 4 | 4 | 1 | 1 | 1 | 1 | 1 |  | 13 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 | 1 | 1 | 1 |  | 10-12 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 | 1 | 1 | 1 |  | 12-13 | 
 | 001111 | 4 | 4 | 2 | 1 | 1 | 1 | 1 |  | 14 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 | 1 | 1 | 1 |  | 13-14 | 
 | 010010 | 4 | 4 | 3 | 1 | 1 | 1 | 1 |  | 15 | 
 | 010011 | 4 | 4 | 4 | 1 | 1 | 1 | 1 |  | 16 | 
 | 010100-010110 | 2-4 | 2 | 2 | 2 | 1 | 1 | 1 |  | 11-13 | 
 | 010111-011000 | 3-4 | 3 | 2 | 2 | 1 | 1 | 1 |  | 13-14 | 
 | 011001 | 4 | 4 | 2 | 2 | 1 | 1 | 1 |  | 15 | 
 | 011010-011011 | 3-4 | 3 | 3 | 2 | 1 | 1 | 1 |  | 14-15 | 
 | 011100 | 4 | 4 | 3 | 2 | 1 | 1 | 1 |  | 16 | 
 | 011101-011110 | 3-4 | 3 | 3 | 3 | 1 | 1 | 1 |  | 15-16 | 
 | 011111-100001 | 2-4 | 2 | 2 | 2 | 2 | 1 | 1 |  | 12-14 | 
 | 100010-100011 | 3-4 | 3 | 2 | 2 | 2 | 1 | 1 |  | 14-15 | 
 | 100100 | 4 | 4 | 2 | 2 | 2 | 1 | 1 |  | 16 | 
 | 100101-100110 | 3-4 | 3 | 3 | 2 | 2 | 1 | 1 |  | 15-16 | 
 | 100111 | 3 | 3 | 3 | 3 | 2 | 1 | 1 |  | 16 | 
 | 101000-101010 | 2-4 | 2 | 2 | 2 | 2 | 2 | 1 |  | 13-15 | 
 | 101011-101100 | 3-4 | 3 | 2 | 2 | 2 | 2 | 1 |  | 15-16 | 
 | 101101 | 3 | 3 | 3 | 2 | 2 | 2 | 1 |  | 16 | 
 | 101110-101111 | 2-4 | 2 | 2 | 2 | 2 | 2 | 2 |  | 14-16 | 
 | 110000 | 3 | 3 | 2 | 2 | 2 | 2 | 2 |  | 16 | 
8 | 000000-000011 | 1-4 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 8-12 | 41
 | 000100-000110 | 2-4 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 10-12 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 | 1 | 1 | 1 | 1 | 12-13 | 
 | 001001 | 4 | 4 | 1 | 1 | 1 | 1 | 1 | 1 | 14 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 11-13 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 | 1 | 1 | 1 | 1 | 13-14 | 
 | 001111 | 4 | 4 | 2 | 1 | 1 | 1 | 1 | 1 | 15 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 | 1 | 1 | 1 | 1 | 13-14 | 
 | 010010 | 4 | 4 | 3 | 1 | 1 | 1 | 1 | 1 | 16 | 
 | 010011-010101 | 2-4 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 12-14 | 
 | 010110-010111 | 3-4 | 3 | 2 | 2 | 1 | 1 | 1 | 1 | 14-15 | 
 | 011000 | 4 | 4 | 2 | 2 | 1 | 1 | 1 | 1 | 16 | 
 | 011001-011010 | 3-4 | 3 | 3 | 2 | 1 | 1 | 1 | 1 | 15-16 | 
 | 011011 | 3 | 3 | 3 | 3 | 1 | 1 | 1 | 1 | 16 | 
 | 011100-011110 | 2-4 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 13-15 | 
 | 011111-100000 | 3-4 | 3 | 2 | 2 | 2 | 1 | 1 | 1 | 15-16 | 
 | 100001 | 3 | 3 | 3 | 2 | 2 | 1 | 1 | 1 | 16 | 
 | 100010-100100 | 2-4 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 14-16 | 
 | 100101 | 3 | 3 | 2 | 2 | 2 | 2 | 1 | 1 | 16 | 
 | 100110-100111 | 2-3 | 2 | 2 | 2 | 2 | 2 | 2 | 1 | 15-16 | 
 | 101000 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 16 |