## Slide 1: Discussions on MU-MIMO Signaling
Date: 2020-08-05
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@Huawei.com
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan | Huawei |  |  | 

## Slide 2
  The number of spatial streams for the user is derived by using the row corresponding to the signaled 4-bit Spatial Configuration subfield and the column corresponding to the User field position in the User Specific field.
  The starting stream index for the user is computed by summing the NSTS in the columns prior to the column indicated by the user’s User field position.
In 11ax, there exists a Spatial Configuration subfield in each MU-MIMO User field. For a given value of Nuser, the MU-MIMO information can be indicated as follows:
Therefore, for an MU-MIMO user, the below information is needed to obtain its spatial configuration information
  Spatial Configuration subfield
  User field position
  Nuser (Number of MU-MIMO users)
Recap: MU-MIMO Indication in 11ax
Nuser
User field position
  Spatial Configuration subfield

## Slide 3
On the basis of the agreed EHT PPDU format sent to multiple users, an efficient per-80MHz preamble structure is designed [1-3]
… | U-SIG2 | EHT-SIG2_2 | …
… | U-SIG2 | EHT-SIG2_1 | …
… | U-SIG2 | EHT-SIG2_2 | …
… | U-SIG2 | EHT-SIG2_1 | …
… | U-SIG1 | EHT-SIG1_2 | …
… | U-SIG1 | EHT-SIG1_1 | …
… | U-SIG1 | EHT-SIG1_2 | …
… | U-SIG1 | EHT-SIG1_1 | …
Primary 80MHz
Secondary 80MHz
  A STA only needs to process up to one 80 MHz segment of the pre-EHT preamble (up-to and including EHT-SIG) to get all the assignment information for itself.
MU-MIMO in Per-80MHz Preamble Signaling
In this structure, if we follow the MU-MIMO indication method in 11ax, the signaling overhead will be high when the users participating in an MU-MIMO belong to different segments (for both OFDMA and non-OFDMA cases).
MU-MIMO with users belonging to more than one segment
  In the following, we first give the details of the above overhead analysis in OFDMA cases.

## Slide 4: Signal All User Fields (Opt. 1)
In 11ax, as we have shown previously, the User field position and the total number of MU-MIMO users are needed for a user to obtain its MU-MIMO information in Spatial Configuration table (See Appendix A [4]).
  If we follow the 11ax style, signaling all the user fields participating in an MU-MIMO is needed to maintain the User field positions. Here we call this method the Opt. 1 [5].
Examples for Opt. 1
  A 242-tone RU has 5 MU-MIMO users. The 1st and 3rd users in the Spatial Configuration table belong to Segment 1, and the 2nd, 4th and 5th users belong to Segment 2.
Opt 1.1
Opt 1.2
Yellow block: Corresponds to the users parked on segment 1
Orange block: Corresponds to the users parked on segment 2
White block: Dummy User fields

## Slide 5: Add Special User Field (Opt. 2)
Although Opt 1 has less specification modification, the overhead is high because it needs some additional User fields to maintain the User field position.
To save the overhead of user fields, in Opt 2 we propose to add a Special User field to inform the total number of MU-MIMO users (Nuser) and the orders (User field positions) in the corresponding segment.
  The Special User field only occurs when there exists multi-segment MU-MIMO, and can be indicated by a special STA ID.
  This Special User field is at the front of the corresponding user fields of each multi-segment MU-MIMO.
  We still use the table of Spatial Configuration table to inform the spatial configuration.
Subfield | Number of bits | Description
STA ID | 11 | Special STA ID (indicating a user field signaling the information of multi-segment MU-MIMO)
Number of MU-MIMO Users | 3 | Indicates the total number of MU-MIMO users (Nuser, not the number of users in a segment) in one multi-segment MU-MIMO
Order Bitmap | 8 | Used to show the orders of the user fields (User field positions) in the table of spatial configuration subfield encoding
… | … | …
User field with special STA ID
  Note: Needed information for MU-MIMO 1. Spatial Configuration subfield 2. User field position 3. Nuser (Number of MU-MIMO users)

## Slide 6: Add Special User Field (Opt. 2)
Example for Opt. 2
  A 242-tone RU has 5 MU-MIMO users. The 1st and 3rd users in the Spatial Configuration table belong to segment 1, and the 2nd, 4th and 5th users belong to segment 2.
Yellow block: Corresponds to the users parked on segment 1
Orange block: Corresponds to the users parked on segment 2
White block: Special User fields used to inform the spatial configuration.
Order Bitmap in Special User field: 1010 0000 (indicates the User field positions in Spatial Configuration table)
Number of MU-MIMO Users (indicates Nuser)
  This number is indicated by the RU Allocation subfield
  This Special User field is at the front of the corresponding user fields of each multi-segment MU-MIMO.
  Note: Needed information for MU-MIMO 1. Spatial Configuration subfield 2. User field position 3. Nuser (Number of MU-MIMO users)
Spatial Configuration subfield exists in these User fields

## Slide 7: Overhead Analysis for OFDMA Cases
Options | Overhead in a segment | Overhead in all segments
Opt 1 Signal all User fields | For an RU/MRU, the number of User fields in segment i is equal to the total number of MU-MIMO users (N) | For one multi-segment MU-MIMO with users in X segments, the total number of User fields in these segments is XN for an RU/MRU.
Opt 2 Add a Special User field | For an RU/MRU, the number of User fields in segment i is equal to the number of MU-MIMO users in the segment + 1 (Ni+1) | For one multi-segment MU-MIMO with users in X segments, the total number of User fields in these segments are N+X for an RU/MRU.
Parameter
  N is the total number of MU-MIMO users for an RU/MRU (N>=2)
  Ni is the number of MU-MIMO users in segment i for an RU/MRU
Analysis
  The user fields that can be saved in a segment for an RU/MRU is N-Ni-1
  With the increase of N and X, the overhead benefit of Opt 2 becomes larger. Furthermore, if there are more than one multi-segment MU-MIMO in OFDMA cases, the overhead can be further saved.
  In the following, we give some concrete analyses on overhead comparison.

## Slide 8: Examples of Overhead (1/4)
Extreme case (no load balance, 242-tone RU)
  Take Content Channel 1 as an example (corresponding to the blue blocks). if in each blue block there exists an MU-MIMO user parking on segment 2, the needed number of user fields in the Content Channel 1 in segment 2 is equal to:
  8*8 = 64 User fields for Content Channel 1 for Opt. 1
  8+8 = 16 User fields for Content Channel 1 for Opt. 2
  Assume that each User field needs 22+5 bits. Then the number of additional needed bits for Opt. 1 is (64-16)*27 = 1296.
  Around 50 symbols (1296/26≈49.8) can be saved for one segment at MCS0.
Corresponds to Content Channel 1
Users parking on segment 2
Users parking on other segments

## Slide 9: Examples of Overhead (2/4)
Extreme case (load balance, 484-tone RU)
  If in each blue block there exists an MU-MIMO user parked on segment 2, the needed number of user fields in the two Content Channels in segment 2 is equal to:
  8*8 = 64 User fields in two content channels for Opt. 1
  8+8 = 16 User fields in two content channels for Opt. 2
  Assume that each User field needs 22+5 bits. Because 484-tone RU support load balance in two Content Channels, the number of additional needed bits for Opt. 1 is (64-16)*27/2 = 648
  Around 25 symbols (648/26≈24.9) can be saved at MCS0.
Corresponds to Content Channel 1
Users parking on segment 2
Users parking on other segments

## Slide 10: Examples of Overhead (3/4)
Practical case (no load balance, 242-tone RU)
  Take Content Channel 1 as an example (corresponding to the blue block). if in the blue block there exists some MU-MIMO users parking on segment 2, the needed number of user fields in Content Channel 1 in segment 2 for this RU is equal to:
  8 User fields for Content Channel 1 for Opt. 1
  2~8 User fields for Content Channel 1 for Opt. 2
  Assume that each User field needs 22+5 bits. Then the number of additional needed bits for Opt. 1 is (0~6)*27 = 0~162.
  Around 0~7 symbols can be saved at MCS0 for one RU/MRU.
Corresponds to Content Channel 1
Users parking on segment 2
Users parking on other segments
  Note: The user fields that can be approximately saved in a segment for an RU/MRU is N-Ni-1

## Slide 11: Examples of Overhead (4/4)
Practical case (load balance, 484-tone RU)
  If in the blue block there exists an MU-MIMO user parked on segment 2, the needed number of user fields in the two Content Channels in segment 2 is equal to:
  8 User fields in two content channels for Opt. 1
  2~8 User fields in two content channels for Opt. 2
  Assume that each User field needs 22+5 bits. Because 484-tone RU support load balance in two Content Channels, the number of additional needed bits for Opt. 1 is (0~6)*27/2 = 0~81
  Around 0~4 symbols can be saved at MCS0 for one RU/MRU.
Corresponds to Content Channel 1
Users parking on segment 2
Users parking on other segments
  Note: The user fields that can be approximately saved in a segment for an RU/MRU is N-Ni-1
  In the following, we give some considerations on non-OFDMA cases.

## Slide 12: Non-OFDMA Cases based on Opt. 1
Non-OFDMA cases based on Opt 1
  EHT has adopted that the number of EHT-SIG symbols field always exists in U-SIG of a PPDU that is not a EHT TB PPDU
  The field is not reinterpreted as the number of MU-MIMO users
  In OFDMA transmission, the number of MU-MIMO users can be indicated by RU Allocation subfield
  In Non-OFDMA transmission, the number of MU-MIMO users can exist in the EHT-SIG to inform the total number of MU-MIMO users.
Example:
The total number of User fields in two content channels is equal to the total number of MU-MIMO users (N)

## Slide 13: Non-OFDMA Cases based on Opt. 2
Non-OFDMA cases based on Opt 2
  Using a Special User field can also support multi-segment MU-MIMO in non-OFDMA cases. However, we can also remove the Special User field, and add the Order Bitmap (e.g. an 8-bit bitmap) to EHT-SIG in non-OFDMA cases.
  The number of MU-MIMO users is also needed in the EHT-SIG to inform the total number of MU-MIMO users.
  The Order Bitmap can indicate the User field positions and the number of User fields in the corresponding segment. The existence of this subfield can also be indicated by some other subfields.
Example:
e.g. 1011 0000
The total number of User fields in two content channels is equal to the number of MU-MIMO users in the segment (Ni)

## Slide 14: Summary
Proposed Opt. 2 to further reduce the overhead in the cases where the users participating in an MU-MIMO belong to different segments
Needed number of User fields in a segment for an RU/MRU with multi-segment MU-MIMO:
 | Opt. 1 | Opt. 2
OFDMA cases | N | Ni+1 (Add a Special User field)
Non-OFDMA cases | N | Ni+1 (Add a Special User field) or Ni (Use an 8-bit subfield)
  N is the total number of MU-MIMO users for an RU/MRU
  Ni is the number of MU-MIMO users in segment i for an RU/MRU

## Slide 15
[1] IEEE 802.11-20/0439r0 Efficient EHT Preamble Design
[2] IEEE 802.11-20/0380r0 U-SIG Structure and Preamble Processing
[3] IEEE 802.11-20/0605r0 Further Discussions on Efficient EHT Preamble
[4] IEEE 802.11-20/0930r3 Consideration on User-specific field in EHT-SIG
[5] IEEE 802.11-20/1102r0 Zero User RUs for Per-80MHz Resource Unit Allocation Signaling
References

## Slide 16
Straw Poll #1
Do you agree that the Number of MU-MIMO Users subfield exists in the Common field of EHT-SIG of an EHT MU PPDU in a non-OFDMA transmission?
  Note: The Number of MU-MIMO Users subfield indicates the total number of MU-MIMO users in a non-OFDMA transmission.
  Y/N/A

## Slide 17
Straw Poll #2
Do you agree that for an RU/MRU with MU-MIMO, the corresponding number of MU-MIMO User fields in a segment can be smaller than the total number of MU-MIMO users?
  Y/N/A

## Slide 18
Straw Poll #3
Do you agree that a Special User field can be used in the cases where the users participating in an MU-MIMO belong to different segments ?
  The Special User field carries a Number of MU-MIMO Users subfield and an Order Bitmap subfield.
  Spatial Configuration table parsing is based on the number of MU-MIMO users and the User field positions indicated by the Order Bitmap subfield.
  Note: RU Allocation subfield in Common field still indicates the number of MU-MIMO User fields (including the Special User field) the RU Allocation subfield contributed in one Content Channel
  Y/N/A

## Slide 19
Straw Poll #4
Do you agree that an Order Bitmap subfield exists in the Common field of EHT-SIG of an EHT MU PPDU in a non-OFDMA transmission?
  The Order Bitmap subfield is used to indicate the User field positions and the number of User fields in the corresponding segment.
  Y/N/A

## Slide 20: Appendix A: Spatial Configuration table (1/3)
Nuser | B5…B0 | Nsts[1] | Nsts[2] | Nsts[3] | Nsts[4] | Nsts[5] | Nsts[6] | Nsts[7] | Nsts[8] | Total Nsts | total entry
2 | 000000-000011 | 1-4 | 1 |  |  |  |  |  |  | 2-5 | 10
 | 000100-000110 | 2-4 | 2 |  |  |  |  |  |  | 4-6 | 
 | 000111-001000 | 3-4 | 3 |  |  |  |  |  |  | 6-7 | 
 | 001001 | 4 | 4 |  |  |  |  |  |  | 8 | 
3 | 000000-000011 | 1-4 | 1 | 1 |  |  |  |  |  | 3-6 | 20
 | 000100-000110 | 2-4 | 2 | 1 |  |  |  |  |  | 5-7 | 
 | 000111-001000 | 3-4 | 3 | 1 |  |  |  |  |  | 7-8 | 
 | 001001 | 4 | 4 | 1 |  |  |  |  |  | 9 | 
 | 001010-001100 | 2-4 | 2 | 2 |  |  |  |  |  | 6-8 | 
 | 001101-001110 | 3-4 | 3 | 2 |  |  |  |  |  | 8-9 | 
 | 001111 | 4 | 4 | 2 |  |  |  |  |  | 10 | 
 | 010000-010001 | 3-4 | 3 | 3 |  |  |  |  |  | 9-10 | 
 | 010010 | 4 | 4 | 3 |  |  |  |  |  | 11 | 
 | 010011 | 4 | 4 | 4 |  |  |  |  |  | 12 | 
4 | 000000-000011 | 1-4 | 1 | 1 | 1 |  |  |  |  | 4-7 | 35
 | 000100-000110 | 2-4 | 2 | 1 | 1 |  |  |  |  | 6-8 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 |  |  |  |  | 8-9 | 
 | 001001 | 4 | 4 | 1 | 1 |  |  |  |  | 10 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 |  |  |  |  | 7-9 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 |  |  |  |  | 9-10 | 
 | 001111 | 4 | 4 | 2 | 1 |  |  |  |  | 11 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 |  |  |  |  | 10-11 | 
 | 010010 | 4 | 4 | 3 | 1 |  |  |  |  | 12 | 
 | 010011 | 4 | 4 | 4 | 1 |  |  |  |  | 13 | 
 | 010100-010110 | 2-4 | 2 | 2 | 2 |  |  |  |  | 8-10 | 
 | 010111-011000 | 3-4 | 3 | 2 | 2 |  |  |  |  | 10-11 | 
 | 011001 | 4 | 4 | 2 | 2 |  |  |  |  | 12 | 
 | 011010-011011 | 3-4 | 3 | 3 | 2 |  |  |  |  | 11-12 | 
 | 011100 | 4 | 4 | 3 | 2 |  |  |  |  | 13 | 
 | 011101 | 4 | 4 | 4 | 2 |  |  |  |  | 14 | 
 | 011110-011111 | 3-4 | 3 | 3 | 3 |  |  |  |  | 12-13 | 
 | 100000 | 4 | 4 | 3 | 3 |  |  |  |  | 14 | 
 | 100001 | 4 | 4 | 4 | 3 |  |  |  |  | 15 | 
 | 100010 | 4 | 4 | 4 | 4 |  |  |  |  | 16 | 

## Slide 21: Appendix A: Spatial Configuration table (2/3)
Nuser | B5…B0 | Nsts[1] | Nsts[2] | Nsts[3] | Nsts[4] | Nsts[5] | Nsts[6] | Nsts[7] | Nsts[8] | Total Nsts | total entry
5 | 000000-000011 | 1-4 | 1 | 1 | 1 | 1 |  |  |  | 5-8 | 49
 | 000100-000110 | 2-4 | 2 | 1 | 1 | 1 |  |  |  | 7-9 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 | 1 |  |  |  | 9-10 | 
 | 001001 | 4 | 4 | 1 | 1 | 1 |  |  |  | 11 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 | 1 |  |  |  | 8-10 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 | 1 |  |  |  | 10-11 | 
 | 001111 | 4 | 4 | 2 | 1 | 1 |  |  |  | 12 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 | 1 |  |  |  | 11-12 | 
 | 010010 | 4 | 4 | 3 | 1 | 1 |  |  |  | 13 | 
 | 010011 | 4 | 4 | 4 | 1 | 1 |  |  |  | 14 | 
 | 010100-010110 | 2-4 | 2 | 2 | 2 | 1 |  |  |  | 9-11 | 
 | 010111-011000 | 3-4 | 3 | 2 | 2 | 1 |  |  |  | 11-12 | 
 | 011001 | 4 | 4 | 2 | 2 | 1 |  |  |  | 13 | 
 | 011010-011011 | 3-4 | 3 | 3 | 2 | 1 |  |  |  | 12-13 | 
 | 011100 | 4 | 4 | 3 | 2 | 1 |  |  |  | 14 | 
 | 011101 | 4 | 4 | 4 | 2 | 1 |  |  |  | 15 | 
 | 011110-011111 | 3-4 | 3 | 3 | 3 | 1 |  |  |  | 13-14 | 
 | 100000 | 4 | 4 | 3 | 3 | 1 |  |  |  | 15 | 
 | 100001 | 4 | 4 | 4 | 3 | 1 |  |  |  | 16 | 
 | 100010-100100 | 2-4 | 2 | 2 | 2 | 2 |  |  |  | 10-12 | 
 | 100101-100110 | 3-4 | 3 | 2 | 2 | 2 |  |  |  | 12-13 | 
 | 100111 | 4 | 4 | 2 | 2 | 2 |  |  |  | 14 | 
 | 101000-101001 | 3-4 | 3 | 3 | 2 | 2 |  |  |  | 13-14 | 
 | 101010 | 4 | 4 | 3 | 2 | 2 |  |  |  | 15 | 
 | 101011 | 4 | 4 | 4 | 2 | 2 |  |  |  | 16 | 
 | 101100-101101 | 3-4 | 3 | 3 | 3 | 2 |  |  |  | 14-15 | 
 | 101110 | 4 | 4 | 3 | 3 | 2 |  |  |  | 16 | 
 | 101111-110000 | 3-4 | 3 | 3 | 3 | 3 |  |  |  | 15-16 | 
6 | 000000-000011 | 1-4 | 1 | 1 | 1 | 1 | 1 |  |  | 6-9 | 54
 | 000100-000110 | 2-4 | 2 | 1 | 1 | 1 | 1 |  |  | 8-10 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 | 1 | 1 |  |  | 10-11 | 
 | 001001 | 4 | 4 | 1 | 1 | 1 | 1 |  |  | 12 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 | 1 | 1 |  |  | 9-11 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 | 1 | 1 |  |  | 11-12 | 
 | 001111 | 4 | 4 | 2 | 1 | 1 | 1 |  |  | 13 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 | 1 | 1 |  |  | 12-13 | 
 | 010010 | 4 | 4 | 3 | 1 | 1 | 1 |  |  | 14 | 
 | 010011 | 4 | 4 | 4 | 1 | 1 | 1 |  |  | 15 | 
 | 010100-010110 | 2-4 | 2 | 2 | 2 | 1 | 1 |  |  | 10-12 | 
 | 010111-011000 | 3-4 | 3 | 2 | 2 | 1 | 1 |  |  | 12-13 | 
 | 011001 | 4 | 4 | 2 | 2 | 1 | 1 |  |  | 14 | 
 | 011010-011011 | 3-4 | 3 | 3 | 2 | 1 | 1 |  |  | 13-14 | 
 | 011100 | 4 | 4 | 3 | 2 | 1 | 1 |  |  | 15 | 
 | 011101 | 4 | 4 | 4 | 2 | 1 | 1 |  |  | 16 | 
 | 011110-011111 | 3-4 | 3 | 3 | 3 | 1 | 1 |  |  | 14-15 | 
 | 100000 | 4 | 4 | 3 | 3 | 1 | 1 |  |  | 16 | 
 | 100001-100011 | 2-4 | 2 | 2 | 2 | 2 | 1 |  |  | 11-13 | 
 | 100100-100101 | 3-4 | 3 | 2 | 2 | 2 | 1 |  |  | 13-14 | 
 | 100110 | 4 | 4 | 2 | 2 | 2 | 1 |  |  | 15 | 
 | 100111-101000 | 3-4 | 3 | 3 | 2 | 2 | 1 |  |  | 14-15 | 
 | 101001 | 4 | 4 | 3 | 2 | 2 | 1 |  |  | 16 | 
 | 101010 - 101011 | 3-4 | 3 | 3 | 3 | 2 | 1 |  |  | 15-16 | 
 | 101100 | 3 | 3 | 3 | 3 | 3 | 1 |  |  | 16 | 
 | 101101-101111 | 2-4 | 2 | 2 | 2 | 2 | 2 |  |  | 12-14 | 
 | 110000-110001 | 3-4 | 3 | 2 | 2 | 2 | 2 |  |  | 14-15 | 
 | 110010 | 4 | 4 | 2 | 2 | 2 | 2 |  |  | 16 | 
 | 110011-110100 | 3-4 | 3 | 3 | 2 | 2 | 2 |  |  | 15-16 | 
 | 110101 | 3 | 3 | 3 | 3 | 2 | 2 |  |  | 16 | 

## Slide 22: Appendix A: Spatial Configuration table (3/3)
Nuser | B5…B0 +B92 | Nsts[1] | Nsts[2] | Nsts[3] | Nsts[4] | Nsts[5] | Nsts[6] | Nsts[7] | Nsts[8] | Total Nsts | total entry
7 | 000000-000011 | 1-4 | 1 | 1 | 1 | 1 | 1 | 1 |  | 7-10 | 50
 | 000100-000110 | 2-4 | 2 | 1 | 1 | 1 | 1 | 1 |  | 9-11 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 | 1 | 1 | 1 |  | 11-12 | 
 | 001001 | 4 | 4 | 1 | 1 | 1 | 1 | 1 |  | 13 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 | 1 | 1 | 1 |  | 10-12 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 | 1 | 1 | 1 |  | 12-13 | 
 | 001111 | 4 | 4 | 2 | 1 | 1 | 1 | 1 |  | 14 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 | 1 | 1 | 1 |  | 13-14 | 
 | 010010 | 4 | 4 | 3 | 1 | 1 | 1 | 1 |  | 15 | 
 | 010011 | 4 | 4 | 4 | 1 | 1 | 1 | 1 |  | 16 | 
 | 010100-010110 | 2-4 | 2 | 2 | 2 | 1 | 1 | 1 |  | 11-13 | 
 | 010111-011000 | 3-4 | 3 | 2 | 2 | 1 | 1 | 1 |  | 13-14 | 
 | 011001 | 4 | 4 | 2 | 2 | 1 | 1 | 1 |  | 15 | 
 | 011010-011011 | 3-4 | 3 | 3 | 2 | 1 | 1 | 1 |  | 14-15 | 
 | 011100 | 4 | 4 | 3 | 2 | 1 | 1 | 1 |  | 16 | 
 | 011101-011110 | 3-4 | 3 | 3 | 3 | 1 | 1 | 1 |  | 15-16 | 
 | 011111-100001 | 2-4 | 2 | 2 | 2 | 2 | 1 | 1 |  | 12-14 | 
 | 100010-100011 | 3-4 | 3 | 2 | 2 | 2 | 1 | 1 |  | 14-15 | 
 | 100100 | 4 | 4 | 2 | 2 | 2 | 1 | 1 |  | 16 | 
 | 100101-100110 | 3-4 | 3 | 3 | 2 | 2 | 1 | 1 |  | 15-16 | 
 | 100111 | 3 | 3 | 3 | 3 | 2 | 1 | 1 |  | 16 | 
 | 101000-101010 | 2-4 | 2 | 2 | 2 | 2 | 2 | 1 |  | 13-15 | 
 | 101011-101100 | 3-4 | 3 | 2 | 2 | 2 | 2 | 1 |  | 15-16 | 
 | 101101 | 3 | 3 | 3 | 2 | 2 | 2 | 1 |  | 16 | 
 | 101110-101111 | 2-4 | 2 | 2 | 2 | 2 | 2 | 2 |  | 14-16 | 
 | 110000 | 3 | 3 | 2 | 2 | 2 | 2 | 2 |  | 16 | 
8 | 000000-000011 | 1-4 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 8-12 | 41
 | 000100-000110 | 2-4 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 10-12 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 | 1 | 1 | 1 | 1 | 12-13 | 
 | 001001 | 4 | 4 | 1 | 1 | 1 | 1 | 1 | 1 | 14 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 11-13 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 | 1 | 1 | 1 | 1 | 13-14 | 
 | 001111 | 4 | 4 | 2 | 1 | 1 | 1 | 1 | 1 | 15 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 | 1 | 1 | 1 | 1 | 13-14 | 
 | 010010 | 4 | 4 | 3 | 1 | 1 | 1 | 1 | 1 | 16 | 
 | 010011-010101 | 2-4 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 12-14 | 
 | 010110-010111 | 3-4 | 3 | 2 | 2 | 1 | 1 | 1 | 1 | 14-15 | 
 | 011000 | 4 | 4 | 2 | 2 | 1 | 1 | 1 | 1 | 16 | 
 | 011001-011010 | 3-4 | 3 | 3 | 2 | 1 | 1 | 1 | 1 | 15-16 | 
 | 011011 | 3 | 3 | 3 | 3 | 1 | 1 | 1 | 1 | 16 | 
 | 011100-011110 | 2-4 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 13-15 | 
 | 011111-100000 | 3-4 | 3 | 2 | 2 | 2 | 1 | 1 | 1 | 15-16 | 
 | 100001 | 3 | 3 | 3 | 2 | 2 | 1 | 1 | 1 | 16 | 
 | 100010-100100 | 2-4 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 14-16 | 
 | 100101 | 3 | 3 | 2 | 2 | 2 | 2 | 1 | 1 | 16 | 
 | 100110-100111 | 2-3 | 2 | 2 | 2 | 2 | 2 | 2 | 1 | 15-16 | 
 | 101000 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 16 |