## Slide 1
Authors:
Multi-Link Setup Discussion
Date: 2020-0x-xx
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | 
Zhiqiang Han | ZTE |  |  | 
Liuming Lu | ZTE |  |  | 
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution discusses some issues in Multi-Link setup and proposes a solution to address those issues.

## Slide 3: Association in Baseline [1]
Association
  The service is used to establish an access point (AP) or personal basic service set (PBSS) control point (PCP), and a station (STA) and enable STA invocation of the distribution system services (DSSs).
  It provides the STA to AP mapping to the DS.
Reassociation
  The reassociation service is invoked to “move” a current association of a non-AP STA from one AP to another. In an ESS with a DS, the reassociation service informs the DS of the current mapping between AP and STA as the STA moves from BSS to BSS within the ESS.
Deassociation
  The disassociation service is invoked when an existing association is to be terminated.
The Association is in the Station level between non-AP STA and AP

## Slide 4: Association in Baseline [1]
Association/Reassociation Procedure
  BSS Discovery
  Open authentication
  Association/Reassociation
  802.1X EAP authentication and 4-ways handshaking if needed
If 802.1x EAP authentication is used

## Slide 5: 802.11be Framework
Multi-Link Operation Setup in SFD [2]
  Setup Procedure
    A MLD has a MAC address that singly identifies the MLD management entity.
    An EHT MLD shall indicate its MLD MAC address during ML setup.
    Association Request/Response frames are reused for multi-link setup.
    A mechanism to teardown an existing multi-link setup agreement
      Reuse disassociation frame for multi-link teardown.
    Re-setup with another AP MLD or changing configuration of existing multi-link setup with an AP MLD.
      Reassociation Request/Response frame is used for this purpose.
ML Setup is in the MLD level between non-AP MLD and AP MLD, reuses existing association, de-association and re-association

## Slide 6: ML Operation Issues
  Multi-Link Operation Setup Issue
  A non-AP MLD may have different capability than an AP MLD. During the ML setup, the non-AP MLD may associate to the AP MLD with its affiliated STAs to a subset of the affiliated APs of AP MLD.
  A link, that is setup as part of a multi-link setup, is defined as Enabled if that link can be used for frame exchange and at least one TID is mapped to that link.
  ML setup issues
    Are other links that are NOT as part of a multi-link setup in Disabled?
    When the non-AP MLD switches its affiliated STA from one link in the initial ML setup to the link that is not in the initial ML setup, what is the state of that link in the initial ML setup?
    “Changing configuration of existing multi-link setup with an AP MLD” requires the re-association between the non-AP MLD and AP MLD.
      The re-association procedure may require re-authentication which causes the extra delay for the ML channel switching and restrict support low latency services.

## Slide 7: A Proposal of ML Setup (1)
  The MLD Setup Procedure
  The ML setup should allow a non-AP MLD to associate with the AP MLD for all possibly supported links (channels) announced by the AP MLD based on the capability of non-AP MLD.
    The number of associated links may be larger than the number of affiliated STAs of the non-AP MLD.
  ML radio (STA) and the associated link mapping
    If non-AP MLD has the same number of affiliated STAs as that of affiliated APs of AP MLD, then non-AP MLD may one-to-one map its radios to “associated” links.
    If non-AP MLD has less affiliated STAs than affiliated APs of AP MLD, the non-AP MLD may
      assign its STAs to a subset of “associated” links (i.e. APs of AP MLD), and
      remain other subset of “associated” links as “unassigned associated links”.
    When the non-AP MLD needs to switch to the channel related to a “unassigned” link, the non-AP MLD can perform the re-mapping between its STAs and the “associated” links. In this way it could avoid the delay in the de-association and re-association procedure.

## Slide 8: A Proposal of ML Setup (2)
  The MLD Setup Procedure
  Initial ML setup: the non-AP MLD sets up MLO with the AP MLD through link1, and establish the association for all links, but link3 is not assigned to a STA.
  In the ML switching, the non-AP MLD can re-map its STA and associated link via re-assigning a STA to operate on an associated link.
Link1
Non-AP MLD MAC
Non-AP MLD
STA1
STA2
Link2
Link3
AP MLD MAC
AP MLD
AP1
AP2
AP3
Link1
Non-AP MLD MAC
Non-AP MLD
STA1
STA2
Link2
Link3
AP MLD MAC
AP MLD
AP1
AP2
AP3
Initial ML Setup
ML Switching

## Slide 9: A Proposal of ML Setup (3)
  MLD and Link State
  For MLD level, the non-AP MLD may be in the state of
    Unassociated: the non-AP MLD does not associate with an AP MLD
      The non-AP MLD operates on at least one link.
      The non-AP MLD can only transmit a management frame to the AP MLD on an operation link.
    Associated: the non-AP MLD has associated with the AP MLD and operates on at least one link.
      The non-AP MLD can transmit any frame to the AP MLD on an operation link(s).
  For Link level, a link after ML setup may be in the state of
    Link Enabled: the link is assigned to a STA and in the ML operation
    Link Disabled: the link is unassigned to a STA and not in the ML operation

## Slide 10: Summary
This contribution discusses
  Some issues in the Multi-Link setup
  Suggest a non-AP MLD to associate with an AP MLD for all possible supported links provided by AP MLD based on the capability of the non-AP MLD.

## Slide 11: Straw Polls
SP1
  Do you support to add to the 11be SFD in R1
    The ML association is between a non-AP MLD and an AP MLD. A non-AP MLD cannot de-associate with the AP MLD for one affiliated STA after ML setup.

## Slide 12: Straw Polls
SP2
  Do you support to add to the 11be SFD in R1
    if a non-AP MLD with the number of affiliated STAs (X) is capable to operate on channels of an AP MLD with the number of affiliated APs (Y) and associates with this AP MLD, the (Y-X) links are in disabled (Y>X) after ML setup.

## Slide 13: References
IEEE802.11-REVmd D3.2
11-20-0566-46-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document
11-20-0386-04-00be-multi-link-association-follow-up
IEEE paper, “Why It Takes So Long to Connect to a WiFi Access Point”, May 2017

## Slide 14
Thank you!