## Slide 1: 802.11be Architecture Discussion
Date: 2020-08-10
Authors:

## Slide 2: Abstract
This presentation considers the relationship of TGbe concepts, as captured in the evolving SFD, to the existing 802.11 architecture. This follows ideas in some first presentations in the ARC SC session on Aug 6, and following discussion.

## Slide 3: MLD Overview diagram
Diagrams for the reference model have been discussed, for the Multi-link Device architecture, mostly focused around a derivation from the multi-band transparent FST architecture introduced by 802.11ad:

## Slide 4: MLD Overview diagram
There are definitely similarities, so the extension is natural. However, there are some key differences, and other complications:
In a multi-band device, there are two distinct and complete, and standalone STAs, with complete MAC sublayer function, and a (relatively thin) “shim layer” that makes them transparent to the LLC sublayer.
In a TGbe multi-link device, there is considerable “sharing” of MAC function across the links. It is confusing to show this “shared MAC” portion as similar to the transparent FST “shim layer” concept, since it is a much larger component of the architecture than the FST entity.
On the management plane, due to the large amount of shared function in an MLD, the management entities are not just “coordinated” as they are in FST, but must be integrated significantly, making the “left-side/right-side” visual of the FST diagram a challenge.

## Slide 5: MLD Overview diagram
Suggest instead that the view be made to show that an MLD has significant structure around the shared components and state, and that the per-link entities and their management are just part of the structure (next slide)

## Slide 6: MLD Overview diagram

## Slide 7: Legacy support
This approach allows the visualization of a “legacy support mode” of operation, as simply the activation of only one of the link’s set of components, and the shared components operating in a legacy mode, where they use the single link in a legacy-compatible style:

## Slide 8: “MAC-U” and “MAC-L”
All the figures/discussion presented in discussion so far have had some concept of some MAC functions that are per-link and “lower” in the stack, and some MAC functions that are shared across the links “at MLD level” and shown “higher” in the stack.
A proposed split/allocation of MAC functions:
Per-link:
  CCA, backoff, NAV, etc.
  A-MPDU aggregation/de-aggregation
  Address 1 matching
MLD (shared state across all links/can use any available link):
  Security Association/state
  Encryption/Decryption
  A-MSDU aggregation/de-aggregation
  BlockAck
  Retransmission

## Slide 9: “MAC-U” and “MAC-L”
Implications from the above lists:
MLD:
  Authentication and (Re)Association
  Sequence Numbers (are per MSDU/MMPDU)
  Single Block Ack reordering buffer across all links
  Packet Numbers (are assigned pre-encryption, checked post-decryption)
  MIC (generated by encryption, checked as part of decryption)
  Scoreboard (maintained for each block ack agreement)
Per-link:
  Control frames (RTS/CTS, Acks, NDP, etc.)
  BlockAckReq/BlockAck, but ‘pulls’ information from shared scoreboard
  Beacon generation: has link-specific capabilities/attributes
  Probe Request/Response

## Slide 10: “MAC-U” and “MAC-L”
Consider the “stack up” per Figure 5-1:
Common (MLD level) components include most of the stack
Per-link components are only the bottom three functions

## Slide 11: “MAC-U” and “MAC-L”
So, something like: