## Slide 1: 4x 320MHz EHT-LTF Design
Date: 2020-08-18
Authors:
Name | Affiliations | Address | Phone | email
Leo Montreuil | Broadcom |  |  | leo.montreuil@broadcom.com
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Introduction
Designing a good sequence with low PAPR for all puncturing cases of 320MHz proves to be a challenge.
[1] and [2] propose a 4x 320MHz LTF design.
In revision r3 we propose another variant of the sequence proposed in r2. Both variants meet our preference for a modular design while having very low PAPR.
The 320MHz EHT-LTF sequences are constructed using a 80MHz base sequence and 8 or 16 coefficient values to expand it to 320MHz

## Slide 3: 80 MHz 4x base sequence
LTF80_4x = [ ...
+1 -1 -1 +1 -1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 +1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 +1 +1 +1 -1 +1 +1 +1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 ...
-1 -1 -1 -1 -1 -1 -1 +1 -1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 +1 +1 -1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 +1 +1 ...
+1 -1 -1 +1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 +1 +1 -1 -1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 +1 -1 +1 -1 -1 +1 +1 ...
-1 +1 +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 -1 -1 -1 +1 -1 +1 -1 -1 -1 -1 +1 -1 ...
+1 +1 -1 -1 +1 -1 -1 -1 -1 +1 +1 -1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 +1 -1 -1 -1 +1 +1 -1 -1 ...
-1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 +1 -1 -1 +1 +1 +1 +1 -1 +1 +1 -1 -1 +1 -1 +1 +1 +1 +1 -1 +1 -1 +1 +1 ...
+1 +1 -1 -1 -1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 +1 +1 +1 -1 +1 +1 -1 -1 -1 -1 +1 -1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 ...
-1 +1 -1 -1 +1 -1 +1 -1 -1 +1 +1 -1 +1 +1 +1 +1 +1 +1 +1 -1 +1 -1 +1 +1 -1 -1 -1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 ...
-1 -1 -1 +1 -1 +1 -1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 -1 +1 -1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 -1 +1 -1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 -1 ...
+1 +1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 +1 +1 +1 -1 +1 +1 -1 -1 -1 -1 +1 -1 -1 +1 +1 -1 +1 -1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 -1 -1 -1 -1 +1 -1 +1 -1 0 0 ...
0 ...
0 0 +1 -1 +1 +1 -1 +1 +1 -1 -1 +1 -1 -1 +1 -1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 +1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 +1 +1 +1 -1 +1 +1 +1 ...
-1 -1 +1 -1 -1 -1 -1 -1 +1 +1 -1 -1 -1 -1 -1 -1 -1 -1 +1 -1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 +1 +1 -1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 ...
+1 -1 -1 -1 +1 +1 -1 +1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 -1 -1 -1 +1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 +1 +1 -1 -1 -1 -1 +1 +1 -1 +1 ...
-1 +1 +1 +1 +1 -1 +1 -1 -1 +1 +1 -1 +1 +1 +1 +1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 -1 -1 ...
-1 -1 +1 -1 +1 -1 -1 -1 -1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 +1 +1 -1 +1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 +1 +1 +1 -1 -1 +1 +1 ...
+1 +1 +1 -1 -1 -1 -1 +1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 -1 +1 -1 -1 +1 +1 ...
-1 +1 -1 -1 -1 -1 +1 -1 +1 -1 -1 -1 -1 +1 +1 +1 +1 -1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 +1 -1 ...
+1 +1 -1 -1 +1 -1 +1 +1 +1 +1 -1 +1 -1 +1 +1 -1 +1 -1 +1 +1 -1 -1 +1 -1 -1 -1 -1 -1 -1 -1 +1 -1 +1 -1 -1 +1 +1 +1 -1 -1 -1 +1 +1 -1 -1 -1 -1 +1 +1 -1 ...
-1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 +1 +1 +1 -1 +1 -1 +1 -1 -1 -1 -1 +1 -1 -1 +1 +1 +1 +1 -1 +1 +1 -1 -1 +1 -1 +1 +1 +1 +1 -1 +1 -1 +1 +1 -1 +1 +1 +1 +1 ...
+1 -1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 +1 -1 -1 -1 +1 -1 +1 -1 +1 -1 -1 -1 +1 -1 -1 +1 +1 +1 +1 -1 +1 +1 -1 -1 +1 -1 +1 +1 +1 +1 -1 +1 -1 +1 +1 -1];
Covering 1001 tones [-500:500] for RU996 in any 80MHz

## Slide 4: 320MHz 4x EHT-LTF Option 1 (from r2)
LTF320_4x = [ ...
[C(1)*LTF80_4x(1:500), 0, C(2)*LTF80_4x(502:1001)], zeros(1,23), ...
[C(3)*LTF80_4x(1:500), 0, C(4)*LTF80_4x(502:1001)], zeros(1,23), ...
[C(5)*LTF80_4x(1:500), 0, C(6)*LTF80_4x(502:1001)], zeros(1,23), ...
[C(7)*LTF80_4x(1:500), 0, C(8)*LTF80_4x(502:1001)] ];
C = [ +1 +1, -1 +1, +1 +1, +1 -1 ]

## Slide 5: 320MHz 4x EHT-LTF Option 2
LTF320_4x = [ ...
[C(1)*LTF80_4x(1:245), C(2)*LTF80_4x(246:500), 0, C(3)*LTF80_4x(502:756), C(4)*LTF80_4x(757:1001)], zeros(1,23), ...
[C(5)*LTF80_4x(1:245), C(6)*LTF80_4x(246:500), 0, C(7)*LTF80_4x(502:756), C(8)*LTF80_4x(757:1001)], zeros(1,23), ...
[C(9)*LTF80_4x(1:245), C(10)*LTF80_4x(246:500), 0, C(11)*LTF80_4x(502:756), C(12)*LTF80_4x(757:1001)], zeros(1,23), ...
[C(13)*LTF80_4x(1:245), C(14)*LTF80_4x(246:500), 0, C(15)*LTF80_4x(502:756), C(16)*LTF80_4x(757:1001)] ];
C = [+1 -1 +1 -1, +1 -1 -1 +1, +1 +1 -1 -1, +1 +1 +1 +1];

## Slide 6: Multi-RU PAPR for Nss = 1 to 8
RU size | BPSK | LTF Opt1 | LTF Opt2
996 | 8.84 | 5.88 | 6.26
 |  | 6.25 | 5.97
 |  | 5.88 | 6.25
 |  | 6.25 | 5.88
996 + 484 | 9.17 | 7.50 | 8.15
 |  | 8.11 | 7.97
 |  | 7.70 | 7.70
 |  | 7.83 | 7.75
 |  | 7.90 | 7.63
 |  | 7.95 | 7.62
 |  | 7.67 | 7.90
 |  | 7.42 | 7.95
2*996 | 9.27 | 6.10 | 6.08
 |  | 6.33 | 6.65
3*996 (puncture 80MHz) | 9.54 | 8.57 | 8.09
 |  | 7.99 | 7.38
 |  | 7.56 | 8.10
 |  | 8.07 | 7.67
3*996 + 484 (puncture 40MHz) | 9.55 | 8.18 | 8.27
 |  | 8.09 | 8.59
 |  | 8.35 | 7.88
 |  | 8.19 | 7.58
 |  | 7.13 | 8.12
 |  | 7.25 | 8.41
 |  | 8.40 | 7.59
 |  | 8.21 | 8.13
4*996 | 9.60 | 6.45 | 7.93
RU size | BPSK | LTF Opt1 | LTF Opt2
2*996 + 484 | 9.50 | 7.42 | 8.17
 |  | 7.37 | 7.97
 |  | 8.41 | 8.92
 |  | 8.58 | 8.78
 |  | 7.46 | 8.06
 |  | 7.33 | 8.97
 |  | 8.22 | 8.46
 |  | 8.46 | 8.05
 |  | 8.22 | 8.11
 |  | 8.46 | 8.68
 |  | 9.54 | 9.31
 |  | 9.48 | 8.21
 |  | 8.62 | 9.23
 |  | 8.96 | 8.82
 |  | 7.56 | 8.05
 |  | 7.56 | 9.22
 |  | 7.98 | 8.47
 |  | 8.08 | 7.66
 |  | 8.18 | 7.57
 |  | 8.35 | 9.07
 |  | 9.40 | 9.10
 |  | 9.63 | 7.84
 |  | 8.18 | 8.00
 |  | 8.35 | 7.93
2*996 discrete | 9.28 | 8.60 | 8.85
 |  | 8.89 | 7.83
 |  | 6.45 | 7.80
 |  | 6.45 | 7.63
RU size | BPSK | LTF Opt1 | LTF Opt2
3*996+484+242 (puncture 20MHz) |  | 7.60 | 8.76
 |  | 7.68 | 8.50
 |  | 7.40 | 8.70
 |  | 7.30 | 8.46
 |  | 7.93 | 7.69
 |  | 7.73 | 7.67
 |  | 7.28 | 7.11
 |  | 7.38 | 8.50
 |  | 7.41 | 8.58
 |  | 7.39 | 8.12
 |  | 7.75 | 7.46
 |  | 7.26 | 8.96
 |  | 7.28 | 8.29
 |  | 7.50 | 7.67
 |  | 7.47 | 8.52
 |  | 7.79 | 7.85

## Slide 7: Worst case PAPR for Nss = 1 to 8
Sequence | BPSK Median | Legacy 11ax HE-LTF | Legacy 11ax HE-LTF | [1] LGE C1 Opt1 EHT-LTF | [1] LGE C2 Opt1 EHT-LTF | [2] Huawei EHT-LTF | BRCM Opt1 EHT-LTF | BRCM Opt2 EHT-LTF
Tone Plan | 5.89 | 11ax | 11be |  |  |  |  | 
RU26 | 6.71 | 4.25 | 7.29 | 7.29 | 7.29 | 7.29 | 3.78 | 3.78
RU52 | 7.29 | 4.97 | 8.48 | 8.48 | 8.48 | 8.48 | 5.12 | 5.12
RU106 | 7.94 | 5.53 | 6.69 | 6.69 | 7.54 | 6.69 | 5.27 | 5.27
RU242 | 8.44 | 5.60 | 7.07 | 7.07 | 7.83 | 7.07 | 5.27 | 5.27
RU484 | 8.84 | 6.00 | 7.38 | 7.38 | 7.46 | 7.38 | 5.98 | 6.19
RU996 | 5.89 | 6.29 | 6.74 | 7.41 | 8.17 | 7.41 | 6.25 | 6.18
4*RU996 | 9.60 |  |  | 10.12 | 8.95 | 7.39 | 6.45 | 7.93
3*RU996 | 9.54 |  |  | 9.41 | 8.71 | 9.50 | 8.57 | 8.10
3*RU996 + RU484 | 9.55 |  |  | 10.02 | 9.33 | 9.47 | 8.40 | 8.59
2*RU996 + RU484 | 9.50 |  |  | 10.12 | 9.50 | 10.87 | 9.63 | 9.31
2*RU996 | 9.27 |  |  | 7.25 | 8.05 | 9.55 | 6.33 | 6.65
RU996 + RU484 | 9.17 |  |  | 9.31 | 9.35 | 9.22 | 8.11 | 8.85
RU484 + RU242 | 8.83 |  |  | 8.46 | 8.67 | 8.52 | 8.04 | 8.04
RU106 + RU26 | 7.44 |  |  | 6.50 | 6.50 | 6.50 | 6.09 | 6.09
RU52 + RU26 | 7.10 |  |  | 6.90 | 6.90 | 6.90 | 6.49 | 6.49
Lowest PAPR are in BOLD
Highest PAPR are in RED

## Slide 8: Observations and Conclusion
Proposed two variants of a base sequence with lowest PAPR
Much lower PAPR for RU<=996 and RU=2x996 compared to [1][2] - especially small RU values are competitive with 11ax
Very low PAPR for 320MHz in option 1 (1.5dB advantage over option 2) which is a key transmission BW for 11be
Lowest maximum PAPR overall with option 2
Lower PAPR for other punctured cases compared with [1][2]

## Slide 9: References
“4x EHT-LTF sequence”, IEEE 802.11-20/1066r0
“EHT-LTFs Sequences Design”, IEEE 802.11-20/0926r0 Slide 16, Option 2

## Slide 10: SP #1
Which option do you prefer?
Option 1 – slides 3 and 4?
Option 2 – slides 4 and 5?
Y
N
A