## Slide 1: Open Issues on Preamble Design
Date: 2020-08-17
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
In these slides, we propose designs for the following
  U-SIG content & overflow for the Unified SU/MU PPDU
    Punctured channel indication design is the focus
  EHT-SIG design
    EHT-SIG common contents
    EHT-SIG content channel structure
    Compressed Modes Signaling
    NDP and DUP PPDU indication
    Coding structure
    User field format

## Slide 3: Background: Punctured Channel Indication
Previous motions
  802.11be signaling in U-SIG for BW/puncturing information in every non-punctured 20 MHz of an 80 MHz segment shall allow even an OBSS or unassociated device to decode the puncturing pattern of at least the specific 80 MHz that contains the 20 MHz.
    [Motion 113, [9] and [46]]
  802.11be supports BW field which does not include puncturing information.
    [Motion 112, #SP29, [9] and [46]]
Based on above motions, U-SIG should be able to convey the preamble puncturing pattern of the relevant 80MHz to even an OBSS device
In next slide, we propose a design which achieves this while keeping the signalling overhead low
  Note that low overhead for puncturing indication is desirable if we want to keep the EHT-SIG field length to 2 symbols for MCS0 SU transmissions  More on this later

## Slide 4: Punctured Channel Indication Design
A single version dependent 6-bit (5 bit plus 1 reserved)field which conveys
  For non-OFDMA cases, the global puncturing information of entire PPDU BW for 11be
    BW dependent table shown in Appendix
  For OFDMA cases, the puncturing pattern of the current 80MHz
    4 bits per 80MHz (simple bit-map)
  Enables OBSS devices to get puncturing info of the 80MHz being monitored in both cases
Desirable traits of this proposal due to efficient signaling
  One reserved bit to leave room for future expansion of non-OFDMA puncturing modes
  Leaves room in U-SIG to accommodate additional TxOP/BSS Color bits if needed
  Ability to reduce EHT-SIG MCS0 overhead to 2 symbols for SU transmissions
We will illustrate these traits in subsequent slides

## Slide 5: New U-SIG/EHT-SIG contents
5 bit punctured channel indication in version dependent section in the U-SIG
  1 reserved bit below it for future proofing
8 Reserved bits in U-SIG
  1 below punctured channel indication
  1 below ‘PPDU type and compression mode’
  6 more; May instead be used for additional TxOP/BSS Color bits
4 reserved bits in U-SIG overflow part of EHT-SIG-common
Overflow bits kept to 17 to make sure EHT-SIG can fit to 2 symbols at MCS0
  More on this later
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | PPDU BW | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | Reserved | 6
 | Version Dependent | Punctured channel indication(global for non-OFDMA) | 5
 |  | Reserved | 1
 |  | PPDU type & Compression Mode | 2
 |  | Reserved | 1
 |  | EHT-SIG MCS | 2
 |  | Number of EHT-SIG symbols | 5
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52
EHT-SIG | Version Dependent (U-SIG Overflow) | Spatial reuse | 4
 |  | GI+LTF size | 2
 |  | Number of EHT-LTF symbols | 3
 |  | Pre-FEC padding | 2
 |  | LDPC extra symbol segment | 1
 |  | Reserved | 4
 |  | PE disambiguity | 1
 | Total # of Overflow Bits |  | 17

## Slide 6: EHT-SIG MCS
We propose to lower the size of EHT-SIG MCS field in U-SIG to 2 bits
4 MCSs are more than enough to cover a good range of data rates for the SIG field
  MCS0, MCS1, MCS3 and ‘MCS0+DCM’
Saves a bit in U-SIG

## Slide 7: No STBC bit
Propose to remove STBC from 11be
With beamforming becoming a popular mode, open loop Tx diversity schemes like STBC offer limited appeal
No signaling needed in SIG field

## Slide 8: No Doppler bit for R1
We propose to not have Doppler bit for R1
  No support for midambles in R1
This topic can be revisited during R2
  Support of midambles in R2 is TBD
Sufficient reserved bits if needed for this feature

## Slide 9: GI+LTF Size
Propose to remove support for ‘ 1x LTF+0.8us GI’ from 11be and make the options consistent across SU and MU transmissions (as the PPDU types are unified too)
  SU transmission GI/LTF options, total of 4
    1x LTF + 0.8us GI -Allowed in 11ax
    2x LTF + 0.8us GI
    2x LTF + 1.6us GI
    4x LTF + 3.2us GI
    4x LTF + 0.8us GI
  MU transmission GI/LTF Options, total of 4
    2x LTF + 0.8us GI
    2x LTF + 1.6us GI
    4x LTF + 3.2us GI
    4x LTF + 0.8us GI
Rationale
  Mode reduction and saves 1 bit in the ‘GI+LTF size’ field
  1x LTF is not very useful in the field due to the degraded performance from interpolation of 1x LTF to 4x tones

## Slide 10: EHT-SIG Common Contents
The EHT-SIG common field will include the following
  U-SIG overflow
    Repeated in each content channel to be friendly to 20MHz operating devices
  Total number of non-OFDMA users (3 bits for 1-8 users)
    Only present in the non-OFDMA compressed mode
    Repeated in each content channel (similar to 11ax where the number of MU-MIMO users in the compressed mode was carried in HE-SIG-A)
  RU allocation subfields (RUA)
    Only present in the uncompressed mode
    Contents are sent parallelized into two content channels
This means that EHT-SIG Common Field is duplicated in both content channels for all modes other than the uncompressed mode

## Slide 11: DUPed SU PPDU & Preamble Design
The DUPed SU PPDU in R1 will use MCS0+DCM for 1ss and 2x Duplication, starting from 80MHz PPDU BW
  Achieve up to 4x combining gain in non-punctured case
Propose a preamble design for up to 4x combining gain
  U-SIG is DUPed in every 20MHz within each 80MHz to achieve up to 4x combining gain
  EHT-SIG using the [1 1 1 1] content channel structure and MCS0 achieves up to 4x combining gain
DUPed PPDU can be signaled using a value of the MCS field in EHT-SIG user field of the SU transmission

## Slide 12: Overall EHT-SIG Content Channel Structure
We propose two types of content channel structures for EHT SIG to cover different types of transmissions
  [ 1 1 1 1]
    Used for SU, DUPed SU and NDP packets
    Punctured channels will not be populated
  [ 1 2 1 2]
    Used for all transmissions other than SU, DUPed SU and NDP
    Punctured channels will not be populated
Propose to indicate the content channel being [1 1 1 1] vs [1 2 1 2] through the “PPDU type and compression mode” bits state

## Slide 13: Overall View of PPDU types and Content Channel Design
EHT PPDUs
Compressed Modes
Uncompressed mode
SU transmission
Non-OFDMA MU-MIMO
DUPed SU
NDP
Trigger Based
Non-trigger Based
[ 1 2 1 2] content channel
[ 1 1 1 1] content channel

## Slide 14: PPDU Type and Compression Mode Field
Recall that originally, we were thinking of the following in the U-SIG
  1 bit PPDU format field
  2 bit compression mode field
However, it seems that we can jointly encode these 2 fields to convey the same information through a 2 bit field
  Saves 1 bit in the U-SIG
Next slide shows the encoding for such a field

## Slide 15: PPDU Type and Compression Mode
Proposal essentially jointly encodes the PPDU format and compression mode fields
Purple modes are compressed modes (no RU allocation)
 | DL/UL (1 bit) | PPDU type and compression mode(2 bits) | Note
TB PPDU | UL | 0 | No EHT-SIG
DL OFDMA | DL | 0 | EHT-SIG, RU Allocation, [1 2 1 2]
UL SU/SU DUP/NDP | UL | 1 | EHT-SIG, No RU Allocation,[1 1 1 1]
DL SU/SU DUP/NDP | DL | 1 | EHT-SIG, No RU Allocation, [1 1 1 1]
DL non-OFDMA MU-MIMO | DL | 2 | EHT-SIG, No RU Allocation, [1 2 1 2]

## Slide 16: Compressed Modes (no RU allocation)
Compressed Modes would use the following states of “PPDU Type and Compression Mode” field
  State 1: SU, NDP (one user with special AID), and DUPed SU (using [1 1 1 1] content channel structure for EHT-SIG)
  State 2: Used for non-OFDMA MU-MIMO with [1 2 1 2] structure of EHT-SIG
SU and DUPed SU | Common Field |  | User Specific Field |  |  | 
Content channel #1 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
Content channel #2 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
NDP | Common Field |  | User Specific Field |  |  | 
Content channel #1 | U-SIG Overflow | #User = 1 | User Field 1 |  |  | 
Content channel #2 | U-SIG Overflow | #User = 1 | User Field 1 |  |  | 
5-user MU-MIMO | Common Field |  | User Specific Field |  |  | 
Content channel #1 | U-SIG Overflow | #User = 5 | User field 1 | User field 2 | User field 3 | 
Content channel #2 | U-SIG Overflow | #User = 5 | User field 4 | User field 5 | Padding | 
User Field with a special AID
U-SIG overflow needs to be 17 bits or lower for a 2 symbol EHT-SIG at MCS0
U-SIG overflow + 3 bits (#of users) + 22 (user-field)+10 bits CRC/tail needs to be within 52 bits

## Slide 17: How to signal an NDP packet?
Recommend using a similar method as 11ac and 11ax
Use the L-SIG length along with N_LTF and number of EHT-SIG symbols to tell that there is no data in this packet
  Similar way is used by 11ax and 11ac
  No separate bit or ‘state of any field’ is wasted on this indication in U-SIG
Note that the PHY anyway must do this calculation to determine the number of data symbols
  No added complexity to doing this
Also, the user field here can convey the Nsts of the NDP

## Slide 18: EHT-SIG Coding Structure
Common Field
  Non-OFDMA compressed mode
    Use 1 code block to encode entire common field plus the 1st user field
  Uncompressed mode of 20/40/80MHz PPDU
    Use 1 code block to encode entire common field
  Uncompressed mode of 160/320MHz PPDU
    Use 2 code blocks
      1st code block has fixed size (U-SIG overflow + 2 RUA = ~35 bits)
      2nd code block includes all remaining RU allocation subfields (2 RUA in 160MHz, 6 RUA in 320MHz)
User field
  Reuse 11ax like code block structure for every 2 user fields, and the last code block may have 1 or 2 user field(s), except for the following
    In non-OFDMA compressed mode, 1st user field (or padding in a NDP) is encoded with the common field, the remaining user fields (if any) follow this rule

## Slide 19: Reason for jointly encoding the common with 1st user field in compressed modes
The main motivation to use 1 code block to encode entire common field plus the 1st user field (or padding in NDP) in the non-OFDMA compressed mode is to make the EHT-SIG fit into two MCS0 symbols for MCS0 for SU transmissions
If the Common field and User Specific field are encoded separately, need 3 MCS0 symbols for total 62 bits
  Common field: 17 (U-SIG overflow)+3 (# user)+10 (CRC/tail)=30 bits
  User field: 22 (user info)+10 (CRC/tail) = 32 bits
If the Common field and 1st user field are jointly encoded, need 2 MCS0 symbols
  17 (U-SIG overflow)+3 (# user)+22 (user info or padding)+ 10 (CRC/tail)=52 bits

## Slide 20: EHT-SIG User Field Design
We propose a 22-bit 11ax like user field design to support up to 16ss
  Just expand NSTS and spatial configuration subfields to support more spatial streams
  Remove DCM bit since DCM is absorbed into MCS
  SU uses the non-MU-MIMO format of user field
User field for a Non-MU-MIMO allocation
User field for an MU-MIMO allocation
Subfield | Number of Bits
STA-ID | 11
MCS | 4
Spatial Configuration | 6
Coding | 1
Subfield | Number of Bits
STA-ID | 11
MCS | 4
Reserved | 1
NSTS | 4
Beamformed | 1
Coding | 1

## Slide 21: Summary
Proposed the following
  Puncturing channel information in U-SIG
    A single version dependent 5 bit field
      Interpreted differently for non-OFDMA vs OFDMA
      One reserved bit for future proofing
  U-SIG and EHT-SIG common contents
  Content channel structure for various PPDUs
  A joint “PPDU type & Compression Mode” field
  For compressed modes, encode the common information with the first user field
    Reduces preamble overhead of SU transmissions to 2 symbol EHT-SIG for even MCS0
  Code block design for the uncompressed modes
  User field contents for EHT-SIG

## Slide 22: SP1
Do you support the 5-bit punctured channel information in U-SIG for the non-OFDMA case to use the BW dependent table on slide 25?
  Table tells, for a specific PPDU BW, the mapping of the “Punctured channel indication” field value to the non-OFDMA puncturing pattern being used in the PPDU

## Slide 23: appendix
NDP Indication, DUP Mode Indication, 5 bit puncturing info table and code block sizes

## Slide 24: Punctured Channel Indication -I
Need 5 bits to indicate the allowed punctured patterns of the entire PPDU BW in 11be (covers all the non-OFDMA puncturing modes)
PPDU BW | Cases | # of Entires | Note
80MHz | No puncturing | 1 | 
 | 20MHz punctured | 4 | 
 | Total | 5 | 
160MHz | No puncturing | 1 | 
 | 20MHz punctured | 8 | 
 | 40MHz punctured | 4 | 
 | Total | 13 | 
320MHz | No puncturing | 1 | 
 | 40MHz punctured | 8 | 
 | 80MHz punctured | 4 | 240/160+80MHz: [1 1 1 x], [1 1 x 1], [1 x 1 1], [x 1 1 1]
 | 320-80-40 | 12 | For each contiguous 240MHz ([1 1 1 1 1 1 x x] and [x x 1 1 1 1 1 1]), one out of six 40MHz may be punctured
 | Total | 25 | 

## Slide 25: Punctured Channel Indication-II
Detailed table shown below
PPDU BW | Cases |  | Value
80MHz | No puncturing | [1 1 1 1] | 0
 | 20MHz punctured | [x 1 1 1] | 1
 |  | [1 x 1 1] | 2
 |  | [1 1 x 1] | 3
 |  | [1 1 1 x] | 4
160MHz | No puncturing | [1 1 1 1 1 1 1 1] | 0
 | 20MHz punctured | [x 1 1 1 1 1 1 1] | 1
 |  | [1 x 1 1 1 1 1 1] | 2
 |  | [1 1 x 1 1 1 1 1] | 3
 |  | [1 1 1 x 1 1 1 1] | 4
 |  | [1 1 1 1 x 1 1 1] | 5
 |  | [1 1 1 1 1 x 1 1] | 6
 |  | [1 1 1 1 1 1 x 1] | 7
 |  | [1 1 1 1 1 1 1 x] | 8
 | 40MHz punctured | [x x 1 1 1 1 1 1] | 9
 |  | [1 1 x x 1 1 1 1] | 10
 |  | [1 1 1 1 x x 1 1] | 11
 |  | [1 1 1 1 1 1 x x] | 12
PPDU BW | Cases |  | Value
320MHz | No puncturing | [1 1 1 1 1 1 1 1] | 0
 | 40MHz punctured | [x 1 1 1 1 1 1 1] | 1
 |  | [1 x 1 1 1 1 1 1] | 2
 |  | [1 1 x 1 1 1 1 1] | 3
 |  | [1 1 1 x 1 1 1 1] | 4
 |  | [1 1 1 1 x 1 1 1] | 5
 |  | [1 1 1 1 1 x 1 1] | 6
 |  | [1 1 1 1 1 1 x 1] | 7
 |  | [1 1 1 1 1 1 1 x] | 8
 | 80MHz punctured | [x x 1 1 1 1 1 1] | 9
 |  | [1 1 x x 1 1 1 1] | 10
 |  | [1 1 1 1 x x 1 1] | 11
 |  | [1 1 1 1 1 1 x x] | 12
PPDU BW | Cases |  | Value
320MHz | 320-80-40 | [x x x 1 1 1 1 1] | 13
 |  | [x x 1 x 1 1 1 1] | 14
 |  | [x x 1 1 x 1 1 1] | 15
 |  | [x x 1 1 1 x 1 1] | 16
 |  | [x x 1 1 1 1 x 1] | 17
 |  | [x x 1 1 1 1 1 x] | 18
 |  | [x 1 1 1 1 1 x x] | 19
 |  | [1 x 1 1 1 1 x x] | 20
 |  | [1 1 x 1 1 1 x x] | 21
 |  | [1 1 1 x 1 1 x x] | 22
 |  | [1 1 1 1 x 1 x x] | 23
 |  | [1 1 1 1 1 x x x] | 24

## Slide 26: EHT-SIG Common Field Coding
Mode | Content Channel | Subfield in EHT-SIG Common Field | 20MHz | 40MHz | 80MHz | 160MHz | 320MHz
Non-OFDMA (Includes SU, non-OFDMA MU-MIMO, DUPed SU) Compressed | #1 | U-SIG Overflow | 17 | 17 | 17 | 17 | 17
 |  | Number of non-OFDMA users (0-8 users) | 3 | 3 | 3 | 3 | 3
 | #2 | U-SIG Overflow | N/A | 17 | 17 | 17 | 17
 |  | Number of non-OFDMA users (0-8 users) | N/A | 3 | 3 | 3 | 3
 | Total # of Signaling Bits in One Content Channel |  | 20 | 20 | 20 | 20 | 20
 | Code Block Size in One Content Channel (including 1 user field, CRC & Tail) |  | 52 | 52 | 52 | 52 | 52
Uncompressed | #1 | U-SIG Overflow | 17 | 17 | 17 | 17 | 17
 |  | Odd indexed 20MHz RU allocation subfield(s) | 9 | 9 | 18 | 36 | 72
 | #2 | U-SIG Overflow | N/A | 17 | 17 | 17 | 17
 |  | Even indexed 20MHz RU allocation subfield(s) | N/A | 9 | 18 | 36 | 72
 | Total # of Signaling Bits in One Content Channel |  | 26 | 26 | 35 | 53 | 89
 | Code Block #1 Size in One Content Channel (including CRC & Tail) |  | 36 | 36 | 45 | 45 | 45
 | Code Block #2 Size in One Content Channel (including CRC & Tail) |  | N/A | N/A | N/A | 28 | 64