## Slide 1: How many MACs? And, Spacetime in reference models
Date: 2020-08-17
Authors:

## Slide 2: Abstract
This presentation is intended to encourage discussion about how to best represent the 11be reference model, in terms of how many of the “shared” or “upper” (or whatever we call it) MAC entities should be shown.
  It seems that the discussion depends, at least in part, on a mutual understanding of how parallelism is (and is not) shown in the spacetime view of reference models.

## Slide 3: Context
11-20/1200 proposed a MAC reference model like the one to the right, for the MLD structure.
This has led to off-line comments/discussion about whether this means some components of the “MAC stack” could not be implemented in separate/parallel components in implementations.

## Slide 4: Some foundation
As a foundation, let’s consider the “spacetime” of the MAC reference model.
In particular, note that the reference model provides exactly (and only) that -- a model that can be used by independent implementers to ensure their devices can interoperate, because they share a common understanding of expected (externally visible/interoperable) behavior.
So, if something doesn’t affect interoperability, it doesn’t matter, in the reference model.

## Slide 5: Implications of foundation
“Time” doesn’t matter, except where explicitly described.
That is, for example, of course PHY timing matters. Of course the ability to power save queue MSDUs/MMPDUs for a period of time matters. But, most other actions within the reference model are assumed to be “timeless”.
As a result, the question of “what can happen in parallel?” is not answered by the reference model. As long as the resulting behavior (as viewed externally or by a peer device) matches what would be done by a direct implementation of the reference model, how a given implementation actually does it is out-of-scope.
And, as another result, the question of “how many of X are distributed (in space)” doesn’t matter, either.

## Slide 6: An example
Consider the Packet Number (PN) assignment block, just as an example.
The PN block is responsible, for each MPDU, to:
  Obtain a PN for this temporal key (or key and TID/ACI for PV1), and associate it with the MPDU (how is implementation specific) for use in the encryption block
  Increment the PN for this temporal key (and TID/ACI for PV1).
  If the PN space for this temporal key (and TID/ACI for PV1) is exhausted, trigger the exhaustion action.
These actions are modeled as being timeless (effectively, taking zero time), and happening in any order.

## Slide 7: An example
Thus, implementations can implement PN assignment in any of a number of ways, including serializing each MPDU, doing parallel PN assignment with one “thread” for each temporal key, or doing massive parallelism with appropriate ‘locks’, ‘rollbacks’ or whatever, to ensure the net result appears correct, or other methods.
This implies that the sharing of state (like current PNs) between multiple instances of a PN assignment block, is an implementation detail, and not shown in the MAC reference model.
Again, the reference model assumes ‘timeless’ operation, so parallelism or distributed processing does not have any effect on, or limitation caused by, the reference model.

## Slide 8: An example
So, these are all equivalent models:

## Slide 9: Deduction
We don’t need to worry about “how many” instances of a block appear in the MAC reference model, UNLESS:
  There is important (and explicit) time aspect to the function, for example the buffering operations. In such a case, how many actors (one or many) can interact via that time aspect is important to understand and describe.
  It is important to interoperability to have agreement about where parallelism can occur, and the peer device needs to be aware of this because it will detect the behavior.
But, we should also be aware of situations where the peer device might become aware of the difference, but it is not important to operation, and we can leave it to implementation option. It is important to describe these as well, so the peer does not make a poor assumption.

## Slide 10: Conclusion
The blocks within the MAC reference model don’t exist in time and space.
If time (or space) differences matter (to a peer), those need to be explicitly described in terms of the interaction between the blocks that interact across that boundary(ies).
For each of the major functions shown in the MAC reference model, we need to consider whether spacetime is observable by a remote peer.
  If no, keep the reference model simple, and leave it out.
  If yes, show the split, make the block-block interactions clear
  If “maybe”, show in the reference model that options are possible, and peers must be designed to handle them.