## Slide 1: Puncturing Patterns for OFDMA
Date: 2020-08-20
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Introduction
The group agreed on puncturing patterns for non-OFDMA modes
OFDMA (to multiple users) allows more flexibility as far as puncturing modes
Propose puncturing patterns that balance flexibility and implementation complexity

## Slide 3: Design Philosophy and Proposal
Observation 1 – 11be supports STA parking on secondary 80MHz. Hence in any 80MHz segment STA need to get at least one instance of each content channel.
Observation 2 – for non-OFDMA one hole is supported. Using similar logic propose to restrict to one hole per 80MHz segment in OFDMA.
Proposal: in OFDMA each 80MHz segment may be punctured in one of the following ways:
  20MHz - any one 20MHz (4 options)
  40MHz – any one 40MHz (3 options [ 1 2 x x], [ x x 1 2], [1 x x 2])

## Slide 4: SP #1
Do you support that in OFDMA each 80MHz segment may be punctured in one of the following ways:
  20MHz - any one 20MHz (4 options)
  40MHz - any one 40MHz (3 options [ 1 2 x x], [ x x 1 2], [1 x x 2])