## Slide 1: NGV 60GHz Beamforming
Date: 2020-9-15
Authors:

## Slide 2: Abstract
60 GHz band transceivers utilize beamforming to achieve practical communication range (several 100s of meters) in V2X scenarios.
Beamformed transmission/reception is suitable for unicast communication.
We propose discovery procedure in OCB mode that is required for performing beamforming training and/or beamformed unicast transmission.
The concept was proposed in:
[1] 11-20/1162r2 OCB for 60GHz

## Slide 3: Beamforming gain
It is expected to utilize 10 dBi or (much) higher antenna gain in 60 GHz band communication.
Beamforming gain is essential to enable the desired communication range (one to a few hundreds meters) for outdoor scenarios.
In these scenarios, STAs not in proximity of each other have to perform “initial” beamforming training before starting data transmission.
  Typically in 11ad/ay (non-TDD), “initial” beamforming training is performed during scan procedure.
  This assumption/situation is different from 5.9 GHz OCB communication.
STA
w/ quasi-omni antenna
w/ beamformed antenna
Antenna gain e.g. +10 dB
Array gain(*) e.g. +10 dB
(*) total input power may increase with a large array antenna in real implementation

## Slide 4: Beamforming procedure in BTI (11ad)
Beamforming using DMG Beacon frames (BTI) is one of the procedures to be used for the initial beamforming.
DBcn
DBcn
DBcn
DBcn
Initiator STA
Responder STA
SSW
SSW
SSW-FB
1) A STA sweeps sectors using multiple DMG Beacon (DBcn) frames
DBcn
3) A peer STA sweeps sectors using SSW frames
Including feedback: best Sector ID=2
Sector ID
0
1
2
N-1
SSW
Sector ID=2 (example)
Received DBcn frame
with the best quality
SSW
Sector ID
0
1
N-1
Sector ID=1 (example)
Received SSW frame
with the best quality
A-BFT slot#0
A-BFT slot#1
A-BFT slot#2...
2) Responder STA chooses one of A-BFT slot by random to perform Tx Sector Sweep
4) Initiator STA transmits SSW-Feedback frame
Including feedback: best Sector ID=1
BTI

## Slide 5: DMG Beacon transmission with Discovery mode = 1 (11ad)
11ad specifies a beacon transmission procedure before establishment of a BSS (802.11-2016[2], subclause 11.1.3.4)
DMG Beacon transmission, followed by beamforming training, is performed with random interval to discover peer STA(s).
STA
Transmission of DMG Beacon
frames (BTI)
A-BFT slots
waiting for responses
from peer STAs
The Interval should be set to a random duration, about 10 – 200ms:
from 802.11-2016:
“At each TBTT, the STA should generate a random value for the Beacon Interval field within the DMG Beacon frame from a uniform distribution
between [10 TUs, 200 TUs), i.e., 10 TUs to 199 TUs.”

## Slide 6: Requirements in V2X
The procedure in the previous slides (Discovery beacon transmission) seems to be reusable for V2X scenario. What’s the difference between 11ad and V2X?
11ad STA | STA in V2X/OCB
Upon having discovered peer STA(s): The STA proceeds with probing, and establishing or joining a BSS, with stopping of DMG Beacon transmission. | Upon having discovered peer STA(s): 1) The STA should start data communication with the discovered STA immediately. 2) The STA should continue transmission of DMG Beacon frames to discover the other, newly approaching STAs.

## Slide 7: Proposed procedure of DMG OCB Discovery
MAC frame exchange procedure should be reused from BTI with Discovery mode in 11ad.
MLME should have primitives to request the MAC entity to start OCB operation with continuous discovery procedure.
The MAC entity should indicate the discovered peers’ info to the higher layer, at least including:
  MAC address
  Support of NGV(OCB) operation
DMG Beacon transmission with random interval may be continued until the MLME requests to stop the OCB operation.

## Slide 8: Proposed spec changes overview
Add a signaling field/element within the DMG Beacon, SSW and SSW-feedback frames to indicate the support of OCB operation in 60GHz.
Specify the procedure for MLME and higher MAC based on the figure in the previous slide.
The text is proposed in 11-20-1303/r0[4]

## Slide 9: Conclusion
This submission discusses DMG beamforming for STAs operating OCB.
A discovery procedure for DMG STAs operating OCB is proposed.

## Slide 10: References
[1] 11-19/1162r2 OCB for 60GHz
[2] IEEE802.11-2016
[3] 11-19/497r6 802.11bd Specification Framework Document
[4] 11-20/1303r0 NGV 60 GHz beamforming - text

## Slide 11: Straw Poll
Do you support to add the following text to Section 4 of SFD[3]:
  11bd shall enable a procedure for continuous discovery of other DMG STAs with dot11OCBActivated equals to true, based on beacon transmission procedure before establishment of a BSS (802.11-2016, subclause 11.1.3.4)
  The MLME service interface shall be extended to provide higher layers with the ability to continuously discover other DMG STAs with dot11OCBActivated equals to true.
  11bd shall enable DMG STAs with dot11OCBActivated equals to true to perform data transmission shortly after discovery.
Y /N /A