## Slide 1: Coding Bit in MU-MIMO
Date: 2020-08-25
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Srinath Puducheri | Broadcom |  |  | 

## Slide 2: Discussion and Proposal
Contribution 20/1238 “Open Issues on Preamble Design” proposes (among other things) an E-SIG user field design.
We note that in it the non-MU-MIMO field has one reserved bit whereas the MU-MIMO doesn’t.
The reserved bit may be useful for rel. 2 and beyond, e.g. adding more MCS.
We also note that in the per-user field for MU-MIMO one bit is used to differentiate LDPC from BCC. Unlike 11ax, in 11be BCC in MU-MIMO can only be used over RU 242.
Propose to define the meaning of the coding bit in MU-MIMO for RU>242 as reserved.

## Slide 3: SP #1
Do you support defining the meaning of the coding bit in MU-MIMO per-user field for RU>242 as reserved?
Y
N
A