## Slide 1: AP assisted SU PPDU Tx for 11be R1
Date: 2020-10-30
Authors:

## Slide 2: AP assisted SU PPDU Tx for 11be R1

## Slide 3: Introduction
11ax has introduced Triggered UL operations to improve medium and QoS Mgt efficiency in a congested BSS.
In 11ax TB operations an AP needs to
  Compute the MCS, NSS, Tx power at STA side,
  For medium efficiency, compute the TB PPDU length by collecting exact BSR information or incur padding penalty.
To just solve the issue of UL contention, we only need a low complexity TB mechanism where an AP simply allocates time in a TXOP to one STA at a time.
  The STA can use the time allocation for transmitting UL SU PPDUs to AP.
  The STA can also use the time allocation for its P2P links.
This mechanism can then be complementary to the restricted TWT proposal (1046r8) where an AP improves the QoS performance of STAs in its BSS (incl. P2P links) by limiting the UL contention.

## Slide 4: AP assisted SU PPDU
AP schedules one associated STA at a time by a TBD Trigger frame (“SU-TF”)
  Trigger includes the duration of time for an Intra-TxOP SP, that starts SIFS after trigger
During the intra-TxOP SP, the scheduled STA transmits one or more non-TB PPDUs
  STA is in control of selecting its own operating params (e.g., MCS, NSS, Tx Power).
  STA does what it wants during Intra-TxOP SP (P2P, UL, …).
AP nominally regains control of medium at the end of the allocation.
AP can also regain control earlier if
  medium is idle for PIFS after the SU-TF (baseline rule),
  SIFS after the time known from duration information in the frames from the scheduled STA.
  SIFS after receiving TBD frame (e.g., QoS Null frame) transmitted by scheduled STA to AP.
Notes: Special value (e.g., 0) in allocation may signal rest of TXOP is allocated to STA.
C add a bit indicating whether 1 frame exchange or more than that...,
add bit to signal whether alloc is for P2P ?

## Slide 5: Signaling using modified MU-RTS frame
MU-RTS frame is an 11ax TF that has several reserved fields and trigger CTS => can be modified to solicit other SU PPDU.
Use Reserved field(s) to signal this frame is an SU-TF and not the baseline MU-RTS frame and whether the SU-TF is for P2P or for UL frame transmissions. This can be signaled by defining a TBD field whose:
  Value 0 corresponds to baseline MU-RTS,
  Value 1 corresponds to UL only traffic.
  Value 2 corresponds to P2P traffic (+ UL traffic).
  Other values are reserved.
A TBD field signals the intra-TXOP SP Duration.
A TBD field that signals whether the AP requires the first frame in the intra-TXOP SP to be a CTS frame to confirm the assignment.
  If AP requires STA to send CTS, then the STA shall send CTS
  However, if AP does not require STA to send CTS, then the STA may send the CTA (has a choice to either still send the CTS or to skip sending the CTS)

## Slide 6: Example
Transmission of UL SU PPDU transmission during intra-TXOP SP
SU PPDU from STA-1 to AP
BA
New MU-RTS from AP (allocation = T, RA: STA1)
Intra-TXOP SP for STA-1 (T)
DL Data from AP
SU PPDU from STA-1 to AP
BA
TXOP owned by AP
DL Data from AP
BA
Transmission of P2P SU PPDU transmission during intra-TXOP SP
CTS
BA
PPDU from P2P STA-1 to P2P STA-2
BA
New MU-RTS from AP (allocation = T, RA: STA1)
Intra-TXOP SP for STA-1 (T)
DL Data from AP
PPDU from P2P STA-1 to P2P STA-2
BA
TXOP owned by AP
DL Data from AP
BA
CTS
BA
Notes: Separate bit for CTS..
BA is sent in an SU PPDU if CTS bit = 0 and subtype = 1 and aggregated with QoS Data
Subtype = 1 => for single SU PPDU
Subtype = 1 => UL SU transmission
SubType = 2 => P2P…

## Slide 7: Summary
We propose a simple AP assisted non-TB PPDU transmission technique that requires very minimal changes to the spec and hence does not impact R1 timeline.
The proposed protocol, when implemented under the TF framework, can significantly improve TF usage in field and pave the way towards efficient BSS management.

## Slide 8: Straw Poll
Do you support the inclusion of the following in the SFD for 802.11be R1:
  802.11be shall define a mechanism for an AP to transmit a modified MU-RTS Trigger frame that allocates time within a TXOP for transmitting one or more non-TB PPDUs
    The time allocation starts after the end of transmission of the MU-RTS frame.
    It is TBD whether the AP can optionally not solicit CTS in some cases.
    This is optional mechanism for non-AP and AP STAs ?
  Note: The non-TB PPDUs may be transmitted by the non-AP STA to AP or to a peer of a peer-to-peer link.