## Slide 1: SIG contents discussion for EHT sounding NDP
Date: 2020-08-20
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Mengshi Hu | Huawei |  |  | 
Ming Gan | Huawei |  |  | 

## Slide 2: Background
In [1], U-SIG and EHT-SIG contents have been very well discussed (see the table on the right).
There are some parts we want to discuss in this proposal (marked in red).
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | PPDU BW | 3
 | Version Dependent | Punctured channel indication(global for non-OFDMA) | 5
 |  | Reserved | 1
 |  | PPDU format | 1
 |  | Reserved | 6
 |  | EHT-SIG MCS | 2
 |  | Number of EHT-SIG symbols | 5
 |  | EHT-SIG Compression | 2
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52
EHT-SIG | Version Dependent (U-SIG Overflow) | Spatial reuse | 4
 |  | GI+LTF size | 3
 |  | Number of EHT-LTF symbols and midamble periodicity | 3
 |  | Reserved | 1
 |  | Pre-FEC padding | 2
 |  | LDPC extra symbol segment | 1
 |  | Reserved | 2
 |  | PE disambiguity | 1
 | Total # of Overflow Bits |  | 17

## Slide 3: Background: EHT-SIG for single user case [1]
[1] proposes: Overflow bits kept to <=17 to make sure EHT-SIG can fit to 2 symbols at MCS0 for single user case.
  17 bits overflow bits, together with 3 bit number of non-OFDMA users, 22-bit user field, 10 bit CRC + Tail, 52 bits in total.
  EHT-SIG with MCS0 (BSPK, R 1/2) can carry 26 uncoded bits per symbol.
Subfield | Number of Bits
STA-ID | 11
Spatial Configuration | 6
MCS | 4
Coding | 1
User field for a Non-MU-MIMO allocation
User field for an MU-MIMO allocation
Subfield | Number of Bits
STA-ID | 11
NSTS | 4
Beamformed | 1
MCS | 4
Reserved | 1
Coding | 1

## Slide 4: Background: EHT-SIG for sounding NDP in [1]
[1] proposes the same format of NDP as single user case EHT MU PPDU.
  Can lead to additional 2 more symbols overhead compared with HE sounding NDP
    11ax: 2 symbols HE-SIG-A
    11be: 2 symbols U-SIG + 2 symbols EHT-SIG (with MCS 0)
      EHT-SIG carries a meaningless number of non-OFDMA users subfield (3bits, 1-8) + 32 bits padding of “User Block”  the 2nd symbol of EHT-SIG is all padding+CRC+Tail.
Padding or dummy user field
to make length same as SU
U-SIG overflow needs to be 17 bits or lower for a 2 symbol EHT-SIG at MCS0
U-SIG overflow + 3 bits (#of users) + 22 (user-field)+10 bits CRC/tail needs to be within 52 bits
SU and DUPed SU | Common Field |  | User Specific Field |  |  | 
Content channel #1 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
Content channel #2 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
NDP | Common Field |  | Padding |  |  | 
Content channel #1 | U-SIG Overflow | #User = 1 | Padding |  |  | 
Content channel #2 | U-SIG Overflow | #User = 1 | Padding |  |  | 

## Slide 5
Propose to have a sounding NDP always with one symbol EHT-SIG to save overhead.
Still have the same U-SIG contents and U-SIG Overflow contents as other EHT MU PPDU for consistency and unification.
Propose to have 16 bits U-SIG Overflow for all modes of EHT MU PPDU. 10 bits CRC+Tail in EHT-SIG SYM 1 for EHT sounding NDP.
Updated in r2: Propose to still enable separate indication of Number of EHT-LTF Symbols and Nss.
Proposed EHT sounding NDP
SU | Common Field |  | User Specific Field |  |  | 
Content channel #1 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
Content channel #2 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
NDP | Common Field |  |  |  |  | 
Content channel #1 | U-SIG Overflow | CRC+Tail |  |  |  | 
Content channel #2 | U-SIG Overflow | CRC+Tail |  |  |  | 
16 bits U-SIG overflow + 10 bits CRC/tail = 26 bits
U-SIG overflow needs to be 16 bits or lower
16 bits U-SIG overflow + 3 bits (#of users) + 22 (user-field)+10 bits CRC/tail + 1 bit padding bit = 52 bits

## Slide 6
Three options are proposed in [1] to signal NDP:
Signaling of NDP
SU | Common Field |  | User Specific Field |  |  | 
Content channel #1 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
Content channel #2 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
NDP | Common Field |  |  |  |  | 
Content channel #1 | U-SIG Overflow | CRC+Tail |  |  |  | 
Content channel #2 | U-SIG Overflow | CRC+Tail |  |  |  | 
Options [1] | My comment
Option 1: Use the L-SIG length along with N_LTF and number of EHT-SIG symbols to tell that there is no data in this packet Similar way is used by 11ax and 11ac | still applicable for 11be
Option 2: Set the EHT-SIG MCS to 0 and number of EHT-SIG symbols to 1 Update in r2: for EHT NDP with one symbol EHT-SIG, besides Option 1, this can act an explicit indication of EHT NDP | provides early/easy detection of NDP, don’t consume additional signaling bits/entries. Only applicable to the proposed sounding NDP (most preferred)

## Slide 7
Updated in r2: several fields are not needed for EHT NDP:
  Pre-FEC padding (2 bit)
  LDPC extra symbol segment (1bit)
  PE Disambiguity (1 bit)
  Reserved (4 bit to 3 bit for EHT NDP)
Propose to indicate Nss (4bit) by reusing Pre-FEC padding factor + PE disambiguity + LDPC extra symbol segment indication.
One reserved bit is used for Beamformed indication
The other two reserved bits are still kept for other potential purposes.
SIG contents in EHT NDP
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | PPDU BW | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | Reserved | 6
 | Version Dependent | Punctured channel indication(global for non-OFDMA) | 5
 |  | Reserved | 1
 |  | PPDU type & Compression Mode | 2
 |  | Reserved | 1
 |  | EHT-SIG MCS | 2
 |  | Number of EHT-SIG symbols | 5
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52
EHT-SIG (before repurposed ) | Version Dependent (U-SIG Overflow) | Spatial reuse | 4
 |  | GI+LTF size | 2
 |  | Number of EHT-LTF symbols | 3
 |  | Pre-FEC padding | 2
 |  | PE disambiguity | 1
 |  | LDPC extra symbol segment | 1
 |  | Reserved | 3
 | Total # of Overflow Bits |  | 16
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6

## Slide 8
SIG contents in EHT NDP
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | PPDU BW | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | Reserved | 6
 | Version Dependent | Punctured channel indication(global for non-OFDMA) | 5
 |  | Reserved | 1
 |  | PPDU type & Compression Mode | 2
 |  | Reserved | 1
 |  | EHT-SIG MCS | 2
 |  | Number of EHT-SIG symbols | 5
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52
EHT-SIG (after repurposed ) | Version Dependent (U-SIG Overflow) | Spatial reuse | 4
 |  | GI+LTF size | 2
 |  | Number of EHT-LTF symbols | 3
 |  | NSS | 4
 |  | Beamformed | 1
 |  | Reserved | 2
 | Total # of Overflow Bits |  | 16
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6

## Slide 9: Summary
In [1], U-SIG and EHT-SIG contents have been very well discussed and some parts are discussed in this proposal regarding sounding NDP and its signaling, PPDU format + EHT-SIG compression, and BSS color.
An efficient sounding NDP format is proposed, in which case one symbol EHT-SIG is enough for MCS 0. And provide a signaling method for early detection of sounding NDP.

## Slide 10: Straw Poll #2
Do you agree to add the following text in the TGbe SFD:
  The EHT-SIG of EHT sounding NDP is always modulated with BPSK R 1/2, and has only one symbol.
    The EHT-SIG of EHT sounding NDP contains 16 bit U-SIG overflow bits and 4 bit CRC and 6 bit Tail.
    This is for R1.

## Slide 11: Straw Poll #3
Do you agree to add the following text in the TGbe SFD:
  For an EHT sounding NDP:
    Number of EHT-SIG symbols field indicates one symbol
    EHT-SIG MCS field is set to MCS0
    This is for R1.

## Slide 12: Straw Poll #4
Do you agree to add the following text in the TGbe SFD:
  Pre-FEC padding factor + PE disambiguity + LDPC extra symbol segment indication are repurposed to signal NSS (4 bit) in an EHT sounding NDP.
    Indicating 1SS-8SS in R1
    The other 8 entries are reserved for R2
    This is for R1.

## Slide 13: Straw Poll #5
Do you agree to add the following text in the TGbe SFD:
  One reserved bit in EHT-SIG is used to indicate beamformed in an EHT sounding NDP.
    This is for R1.

## Slide 14
https://mentor.ieee.org/802.11/dcn/20/11-20-1238-00-00be-open-issues-on-preamble-design.pptx, Sameer Vermani, Qualcomm
https://mentor.ieee.org/802.11/dcn/20/11-20-0566-60-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document.docx, Edward Au, Huawei
https://mentor.ieee.org/802.11/dcn/20/11-20-1015-02-00be-eht-ndpa-frame-design-discussion.pptx, Chenchen Liu, Huawei
https://mentor.ieee.org/802.11/dcn/20/11-20-1474-00-00be-ndp-design-for-eht.pptx, Eunsung Jeon
References